***** File EPAS.DOC                                                                                                               
                                                                                                                                  
        THE ISEE-3/ICE  ENERGETIC PARTICLE  ANISOTROPY SPECTROMETER (EPAS)                                                        
                                                                                                                                  
                                                                                                                                  
	INTRODUCTION                                                                                                                     
	The ISEE-3/ICE	spacecraft encountered comet Giacobini-Zinner (G-Z)                                                               
	on 11 September 1985 and obtained detailed observations of particle                                                              
	and fields  in the  cometary environment.   To date, it is the only                                                              
	spacecraft to  have passed  through a  cometary  plasma  tail.	The                                                               
	Energetic Particle Anisotropy Spectrometer (EPAS) on the spacecraft                                                              
	provided  observations	 of  the   3-dimensional  distribution	 of                                                                
	energetic (> 65 keV) cometary ions.  These ions were detected up to                                                              
	4 million km from  the comet  nucleus and  the maximum	ion  fluxes                                                               
	attained during  the encounter were among the highest ever observed                                                              
	by the	instrument.   The  ions  originate  as	cometary  neutrals,                                                                
	principally  water  molecules,	which  sublime	from  the  cometary                                                                
	nucleus at  typical speeds of 1 km/s.  They are subsequently photo-                                                              
	dissociated and  ionized, either by charge-exchange with solar wind                                                              
	protons or  by solar  UV radiation,  on time  scales  of  around  1                                                              
	million seconds,  resulting in	a cloud  of cometary ions extending                                                               
	several million  km from the comet.  The ions are then picked up by                                                              
	the solar  wind flow and accelerated to energies of several tens of                                                              
	keV, allowing them to be detected by EPAS.  However, ions with much                                                              
	higher energies, extending up to around 400 keV were also detected,                                                              
	in particular in the vicinity of, and downstream from, the cometary                                                              
	bow shock,  indicating that  further acceleration  must  have  been                                                              
	taking place in addition to solar wind pick-up.                                                                                  
                                                                                                                                  
	THE ISEE-3/ICE MISSION                                                                                                           
	The International  Sun-Earth  Explorer-3  spacecraft  (ISEE-3)	was                                                               
	launched on  12 August 1978  and initially  placed in  a halo orbit                                                              
	around	the  L1  libration  point,  some  240 Re  (1.5	million km)                                                                
	upstream of  the Earth.  In late 1982-late 1983, the trajectory was                                                              
	changed to  one which took the spacecraft into the geomagnetic tail                                                              
	using a  series of  lunar-gravitationally assisted orbits.  Then in                                                              
	December 1983,	ISEE-3, renamed the International Cometary Explorer                                                               
	(ICE), made  a close  encounter with  the moon and was ejected from                                                              
	the Earth-moon	system to  make a  pass through  the tail  of comet                                                               
	Giacobini-Zinner on  11 September (DOY 254) 1985.   The  spacecraft                                                              
	travelled approximately  from south  to north relative to the comet                                                              
	at 21 km/s.   Closest approach to the comet nucleus (7800 km on the                                                              
	tailside) occurred  at 1102 UT.  The cometary bow shock was crossed                                                              
	inbound and outbound at approximately 0927 UT and 1220 UT.  Further                                                              
	details of  the encounter  and initial	results  can  be  found  in                                                               
	Science, 232, 1986.                                                                                                              
                                                                                                                                  
	The  ISEE-3/ICE	 Project Scientist  was  originally  Dr. Tycho  von                                                              
        Rosenvinge  and  is currently  Dr. Keith Ogilvie, Code 692, Goddard                                                       
        Space Flight Center.                                                                                                      
                                                                                                                                  
	THE ISEE-3/ICE ENERGETIC PARTICLE ANISOTROPY SPECTROMETER (EPAS)                                                                 
	The  Imperial	College,  London/   Space  Science  Dept.  of  ESA,                                                                
	Noordwijk/ Space  Research Laboratory,	Utrecht, Energetic Particle                                                               
	Anisotropy  Spectrometer   (EPAS)     on  the	spacecraft  (ISEE-3                                                                
	experiment designation	DFH,  Principal  Investigator,	Prof.  R.J.                                                                
	Hynds of  Imperial College) measures the 3-dimensional distribution                                                              
	of energetic ions about the spacecraft.  It consists of a system of                                                              
	three identical  semi-conductor particle  telescopes mounted on the                                                              
	body of  the spacecraft  and inclined  at 30 degrees (Telescope 1),                                                              
	60 degrees (Telescope  2) and  135 degrees  (Telescope	3)  to	the                                                                
	spacecraft spin  axis which  is  maintained  perpendicular  to	the                                                               
	ecliptic plane (to within 1 degree).  The spacecraft spin period is                                                              
	3.04 s.   Each telescope  has a  conical field	of view  of 16 deg.                                                               
	semi-cone angle  and a	geometrical factor  of	0.05 cm2 sr.	The                                                                   
	telescopes  detect   ions  (electrons  being  excluded	by  "broom"                                                               
	magnets) and  measure their  total kinetic  energy (but  not  their                                                              
	mass) by  each	using  a  stack  of  two  silicon  surface  barrier                                                               
	detectors.   The front	detector (A) is  33 micrometers thick while                                                               
	the second (B)	is 150 micrometers  thick.    Particle	counts	are                                                                 
	defined by  anticoincidence (A.not B),	i.e. the  ions deposit	all                                                                
	their energy in the A detector and do not intercept and trigger the                                                              
	B detector.  The amplitude of the signal produced in the A detector                                                              
	is dependent  on the  energy deposited in the silicon, and hence on                                                              
	the incident  ion energy.   This  signal is  fed  to  pulse  height                                                              
	discriminators which  define 8	primary energy	channels, E1 to E8.                                                                
	In addition, a further channel, E0, monitors the instrument thermal                                                              
	noise but can register ions above the background if the ion flux is                                                              
	sufficiently high.  No background noise counting-rate correction is                                                              
	required in  any of  the primary  energy channels,  i.e. the counts                                                              
	recorded are  actual particle  counts.	 The channel  energy ranges                                                               
	depend slightly  on ion  mass.	 This is  due principally  to mass-                                                               
	dependent energy  losses when  the ions  pass through  a thin  gold                                                              
	electrode on  the front surface of the A detector.  For protons and                                                              
	water-group ions  (such as  were observed at comet G-Z), the energy                                                              
	ranges are:                                                                                                                      
                                                                                                                                  
				 Protons	 Water Group                                                                                                         
		    (Noise) E0:  21-35	keV	 35-65	keV(approx.)                                                                                  
			    E1:  35-56	keV	 65-95	keV                                                                                                  
			    E2:  56-91	keV	 95-140 keV                                                                                                 
			    E3:  91-147 keV	140-205 keV                                                                                                
			    E4: 147-238 keV	205-310 keV                                                                                                
			    E5: 238-384 keV	310-480 keV                                                                                                
			    E6: 384-620 keV                                                                                                            
			    E7: 620-1000 keV	(From Hynds et al.,                                                                                       
			    E8: 1000-1600 keV	Science 232, 361, 1986)                                                                                  
                                                                                                                                  
	(The water-group  energy ranges  for channels  E6-E8 have  not been                                                              
	determined.)                                                                                                                     
                                                                                                                                  
	In this  G-Z data set, observations from Channels E1 to E5 only are                                                              
	included since cometary ions were not detected in the higher energy                                                              
	channels.    For  each	of  these  channels,  particle	counts	are                                                                 
	accumulated in	eight azimuthal  sectors of  45 deg. width  in each                                                               
	telescope. The	sectors are numbered from 1 to 8 anticlockwise when                                                               
	viewed from  above the ecliptic, with  Sector 1 centred on the sun-                                                              
	Earth line, i.e. it views in the sunward direction and detects ions                                                              
	streaming away	from the  Sun.	 At Giacobini-Zinner, a complete 3-                                                                
	dimensional distribution  function was	obtained at  32 s intervals                                                               
	during the  main encounter  phase,  changing  to  64 s	at  greater                                                               
	distances e.g. after 1830 UT on 12 September outbound.                                                                           
                                                                                                                                  
        Cometary pick-up ions at large distances (millions of km) from the                                                        
	nucleus are characterized by highly anisotropic distributions, with                                                              
	large fluxes in the sunward viewing sectors (1,2,8).  Closer to the                                                              
	comet, within  around 500,000 km  or 6 hours  of closest  approach,                                                              
	broader distributions  with a  antisolar  streaming  are  observed.                                                              
	Here enhanced  solar  wind  turbulence	excited  by  cometary  ions                                                               
	scatters the  ions into near isotropy in the solar wind frame.	The                                                               
	observed anisotropy  is then  due to  the ions	convecting with the                                                               
	solar wind.                                                                                                                      
                                                                                                                                  
	Further details  of the  EPAS instrument can be found in: Balogh et                                                              
	al., IEEE Trans. on Geoscience Electronics, GE-16, No. 3, 176, 1978                                                              
	and van Rooijen et al., Space Science Instrumentation, 4, 373, 1979.                                                             
	Preliminary observations  from the G-Z encounter are given in Hynds                                                              
	et al.,  Science, 232,	361, 1986.  The instrument configuration is                                                               
	also illustrated in Richardson et al., Planetary and Space Science,                                                              
	36, 1429, 1988.                                                                                                                  
                                                                                                                                  
	Contact addresses:                                                                                                               
                                                                                                                                  
	Profs. R.J. Hynds/S.W.H. Cowley,	Dr. I.G. Richardson,                                                                            
	Blackett Laboratory,			Code 661,                                                                                                 
	Imperial College,			NASA/Goddard Space Flight                                                                                    
						Center,                                                                                                                     
	London, SW7 2BZ,			Greenbelt,                                                                                                    
	U.K.					MD 20771,                                                                                                               
						USA.                                                                                                                        
						SPAN LHEAVX::RICHARDSON                                                                                                     
                                                                                                                                  
	Drs. K.-P. Wenzel/T.R. Sanderson,                                                                                                
	Space Science Dept. of ESA,                                                                                                      
	2200 AG Noordwijk,                                                                                                               
	The Netherlands                                                                                                                  
	SPAN ESTCS1::KWENZEL or TSANDERS                                                                                                 
                                                                                                                                  
                                                                                                                                  
        ==================================================================                                                        
                                                                                                                                  
	REFERENCES                                                                                                                       
                                                                                                                                  
                                                                                                                                  
        Balogh, A., van Dijen, G., van Genechten, J., Henrion, J.,  Hynds,                                                        
        R., Korfmann, G., Iversen, T., van Rooijen, J., Sanderson, T.,                                                            
        Stevens, G., Wenzel, K.-P., Low energy proton experiment on ISEE-C,                                                       
        IEEE Trans. Geosci. Electron., GE-16, No. 3, 176-180, July 1978.                                                          
                                                                                                                                  
        Daly P.W., Sanderson, T.R., Wenzel, K.-P., Survey of  energetic (E                                                        
        > 35 keV) ion anisotropies in the deep geomagnetic tail,  J.                                                              
        Geophys. Res., 89, No. A12, 10733-10739, 1984.                                                                            
                                                                                                                                  
        Hynds, R.J., Cowley, S.W.H., Richardson, I.G., Sanderson,  T.R.,                                                          
        Tranquille, C., Wenzel, K.-P., Daly, P.W., Energetic ion                                                                  
        observations during comet Giacobini-Zinner encounter, Adv. Space                                                          
        Res.,  5, No. 12, 17-25, 1986.                                                                                            
                                                                                                                                  
        Hynds, R.J., Cowley, S.W.H., Sanderson, T.R., Wenzel, K.-P.,  Van                                                         
        Rooijen, J.J., Observations of energetic ions from Comet                                                                  
        Giacobini-Zinner, Science, 232, 361-365, Apr. 1986.                                                                       
                                                                                                                                  
        Richardson, I.G., Cowley, S.W.H., Tranquille, C.T., Sanderson,                                                            
        T.R., Hynds, R.J., Wenzel, K.-P., Daly, P.W., Observations of                                                             
        energetic water-group ions at comet Giacobini-Zinner: Implications                                                        
        for  ion acceleration processes, Planet. Space Sci., 35, No. 10,                                                          
        1323-1345,  Oct. 1987.                                                                                                    
                                                                                                                                  
        Richardson, I.G., Cowley, S.W.H., Moore, V.M., Staines, K.,  Hynds,                                                       
        R.J., Sanderson, T.R., Wenzel, K.-P., Daly, P.W., Energy  spectra                                                         
        of energetic heavy ions in the vicinity of comet                                                                          
        P/Giacobini-Zinner, Astron. Astrophys., 187, 276-280, Nov. 1987.                                                          
                                                                                                                                  
        Richardson, I.G., Cowley, S.W.H., Hynds, R.J., Daly P.W.,                                                                 
        Sanderson, T.R., Wenzel, K.-P., properties of energetic water-group                                                       
        ions in the extended pick up region surrounding comet                                                                     
        Giacobini-Zinner, Planet. Space Sci., 36, No. 12, 1429-1450, 1988.                                                        
                                                                                                                                  
        Richardson, I.G., Cowley, S.W.H., Hynds, R.J., Daly, P.W.,                                                                
        Sanderson, T.R., Wenzel, K.-P., Energetic cometary ion flows in the                                                       
        pick-up region of Comet giacobini-Zinner, Adv. Space Res., 9,                                                             
        (3)381-(3)384, Mar. 1989.                                                                                                 
                                                                                                                                  
        Richardson, I.G., Cowley, S.W.H., Wenzel, K.-P., Scarf, F.L.,                                                             
        Plasma wave, magnetic field and energetic ion observations in the                                                         
        ion  pick-up region of Comet Giacobini-Zinner, Adv. Space Res., 9,                                                        
        (3)377-(3)380, Mar. 1989.                                                                                                 
                                                                                                                                  
        Sanderson, T.R., Reinhard, R., Wenzel, K.-P., The propagation  of                                                         
        upstream protons between the earth's bow shock and ISEE 3, J.                                                             
        Geophys. Res., 86, No. A6, 4425-4434, 1981.                                                                               
                                                                                                                                  
        Staines, K., Balogh, A., Cowley, S.W.H., Hynds, R.J., Yates,  T.S.,                                                       
        Richardson, I.G., Sanderson, T.R., Wenzel, K.-P., McComas, D.J.,                                                          
        Tsurutani, B.T., Cometary water-group ions in the region                                                                  
        surrounding  comet Giacobini-Zinner: Distribution functions and                                                           
        bulk parameter  estimates, Planet. Space Sci., 39, No. 3, 479-506,                                                        
        1991.                                                                                                                     
                                                                                                                                  
        Stevens, G.A., van Rooijen, J.J., The distribution function of                                                            
        upstream energetic particle populations, J. Geophys. Res., 86, No.                                                        
        A6, 4435-4444, 1981.                                                                                                      
                                                                                                                                  
        Van Rooijen, J.J., van Dijen, G., Lafleur, H., Th., Lowes, P.,  A                                                         
        low energy proton spectrometer for directional distribution                                                               
        measurements in space, Space Science Instrumentation, 4, 373-392,                                                         
        1979.                                                                                                                     
                                                                                                                                  
	I.G. Richardson,                                                                                                                 
	Code 661,                                                                                                                        
	Goddard Space Flight Center,                                                                                                     
	Greenbelt, MD 20771, USA.                                                                                                        
                                                                                                                                  
                                                                                                                                  
        =================================================================                                                         
                                                                                                                                  
                                                                                                                                  
                                                                                                                                  
        FORMAT OF ORIGINAL G-Z ENCOUNTER EPAS DATA AS PROVIDED BY I. G.                                                           
        RICHARDSON                                                                                                                
                                                                                                                                  
	Data are  provided for	8-14 September (DOY  251-257) 1985.                                                                       
	The data  are time  ordered and  provided at the highest resolution                                                              
	available, i.e.  32 s averages	for the main part of the encounter,                                                               
	and 64 s for the outer region (after 1830 UT on 12 September).	For                                                               
	each time period, the data are provided in the following format:                                                                 
                                                                                                                                  
	RECORD 1: Time record.                                                                                                           
                                                                                                                                  
	     Year; Day of year; Hours; Minutes; Seconds.                                                                                 
	     Format:  2I4, 3I3                                                                                                           
                                                                                                                                  
	RECORDS 2  to 16:  Sectored data  for 3 telescopes x Channels E1 to                                                              
	E5.                                                                                                                              
                                                                                                                                  
	     Telescope no.;  Channel no.; No. of spins; Counts in Sectors 1                                                              
	     to 8.                                                                                                                       
	     Format:  I2,I3,8F8.0                                                                                                        
                                                                                                                                  
	     No. of  spins =  number of spacecraft spins (of 3.04 s period)                                                              
	     over which the particle counts are accumulated.                                                                             
	     The number  of counts  in each  sector is the actual number of                                                              
	     counts accumulated during this number of spacecraft spins.                                                                  
                                                                                                                                  
	RECORD 17: Direction-averaged ion intensities (using 3 telescopes x                                                              
	8 sectors) for Channels E1 to E5, in units of counts/(cm2-sec-sr-keV)                                                            
	(assuming water group ions) and Channel E1 ion streaming direction,                                                              
	relative to the spacecraft.                                                                                                      
                                                                                                                                  
             Direction-averaged ion intensities in Channels E1 to E5; Theta;                                                      
             Phi                                                                                                                  
             Format:  5E10.2, 2F7.1                                                                                               
                                                                                                                                  
	     Theta  ranges   from  0 degrees   (northward   streaming)	 to                                                               
	     180 degrees (southward).                                                                                                    
	     Phi = 0 deg. corresponds  to sunward  streaming, and increases                                                              
	     anti-clockwise as	viewed from  above the ecliptic.  Thus, for                                                               
	     example, for  antisolar streaming	in the ecliptic, theta = 90                                                               
	     deg. and phi = 180 deg.                                                                                                     
                                                                                                                                  
	     The ion  streaming direction  is derived  from the first-order                                                              
	     term of a third-order spherical harmonic fit to the log of the                                                              
	     sectored data  in Channel E1  (Daly et  al., J. Geophys. Res.,                                                              
	     89, 10733, 1984).                                                                                                           
                                                                                                                                  
	     Variations in  the ion  streaming direction  at G-Z  and their                                                              
	     interpretation have  been	discussed  in  Richardson  et  al.,                                                               
	     Geophys. Res. Lett., 13, 415, 1986, Daly et al., Geophys. Res.                                                              
	     Lett. 13, 419, 1986 and Richardson et al., Planet. Space Sci.,                                                              
	     36, 1429, 1988.                                                                                                             
                                                                                                                                  
	N.B.:                                                                                                                            
                                                                                                                                  
	1) -999 is used as a "fill" value throughout.                                                                                    
                                                                                                                                  
	2) Occasionally,  an erroneous large "number of counts" is recorded                                                              
	in a  sector.	An attempt  has been  made to remove these bad data                                                                
	points, but a few may still remain.                                                                                              
                                                                                                                                  
        ===================================================================                                                       
                                                                                                                                  
        ORIGINAL DATA SAMPLE                                                                                                      
                                                                                                                                  
       1985 251  0 43 22                                                                                                          
       11 10      1.      0.      0.      1.      0.      0.      1.      1.                                                      
       21 10      2.      0.      0.      0.      0.      0.      2.      0.                                                      
       31 10      0.      2.      0.      1.      1.      2.      0.      1.                                                      
       12 10      0.      0.      0.      0.      1.      0.      1.      0.                                                      
       22 10      0.      1.      0.      0.      0.      0.      1.      0.                                                      
       32 10      1.      2.      0.      0.      1.      1.      0.      0.                                                      
       13 10      0.      0.      1.      0.      1.      0.      1.      0.                                                      
       23 10      0.      0.      0.      0.      0.      0.      0.      0.                                                      
       33 10      0.      1.      0.      1.      0.      1.      0.      0.                                                      
       14 10      0.      0.      0.      0.      0.      0.      0.      0.                                                      
       24 10      0.      0.      0.      0.      0.      0.      0.      0.                                                      
       34 10      0.      0.      0.      0.      0.      0.      0.      0.                                                      
       15 10      0.      0.      0.      0.      0.      0.      0.      0.                                                      
       25 10      0.      0.      0.      0.      0.      0.      0.      0.                                                      
       35 10      0.      0.      0.      0.      0.      0.      0.      0.                                                      
         0.11E+00  0.47E-01  0.11E-01  0.00E+00  0.00E+00 -999.0 -999.0                                                           
                                                                                                                                  
       ======================================================================                                                     
                                                                                                                                  
        SAMPLE CALCULATION OF DIRECTION AVERAGED ION INTENSITIES                                                                  
                                                                                                                                  
                                                                                                                                  
       1985 251  0 43 22    Channel 1                                                                                             
                                                                                                                                  
     ------------------------------------------------------------------------                                                     
     Tel.  Ch.  No. of              Ion Counts in Sector               Total                                                      
     No.   No.  spins      1    2    3    4    5    6    7    8     counts (N)                                                    
     -------------------------------------------------------------------------                                                    
                                                                                                                                  
      1     1     10       1.   0.   0.   1.   0.   0.   1.   1.        4                                                         
      2     1     10       2.   0.   0.   0.   0.   0.   2.   0.        4                                                         
      3     1     10       0.   2.   0.   1.   1.   2.   0.   1.        7                                                         
                                                                                                                                  
     -------------------------------------------------------------------------                                                    
                                                                                                                                  
                                                                                                                                  
     Normalized weighting factors (W) for telescopes:                                                                             
                                                                                                                                  
	Telescope 1:  W(1) = -0.0351                                                                                                     
	Telescope 2:  W(2) = +0.6316                                                                                                     
	Telescope 3:  W(3) = +0.4036                                                                                                     
                                                                                                                                  
                                                                                                                                  
     Directional (weighted) average ion counts per telescope for channel 1:                                                       
                                                                                                                                  
	N(1)*W(1) + N(2)*W(2) + N(3)*W(3) =                                                                                              
	4*-0.0351 + 4*0.6316  + 7*0.4036  = 5.2112                                                                                       
                                                                                                                                  
                                                                                                                                  
     Directional averaged ion intensities for channel 1:                                                                          
                                                                                                                                  
                               wtd. avg. ion counts                                                                               
   Ion Intensity = -------------------------------------------------                                                              
                    geometric factor  * integration time * bandwidth                                                              
                                                                                                                                  
                                                                                                                                  
	geometric factor = 0.05 cm2-sr (for each telescope);                                                                             
	integration time = No. of spins * spin period = 10*3.04 = 30.4 s                                                                 
	bandwidth = delta-E = 95-65 = 30 keV for channel 1 (water-gp. ions)                                                              
                                                                                                                                  
                                                                                                                                  
                         5.2112                                                                                                   
    Ion Intensity = -----------------  =  0.114 ions per (cm2-s-sr-keV)                                                           
                     0.05 * 30.4 * 30                                                                                             
                                                                                                                                  
                                                                                                                                  
        3) In a few records at high fluxes, the Telescope 2, sector 1, data                                                       
        for energy channel 1 are set to fill.  This is because an                                                                 
        unexpectedly high particle count caused an integer overflow                                                               
        (count > 32767) during initial data processing.  Unfortunately, the                                                       
        original data points cannot be recovered for this archive.  (The                                                          
        corresponding direction-averaged intensities in EPSUMMRY.TAB have                                                         
        been set to "fill".)                                                                                                      
                                                                                                                                  
                                                                                                                                  
=============================================================================                                                     
                                                                                                                                  
These files were reformatted to allow for PDS to adequately describe the data.                                                    
The original records 1 (time), and 2-16 (sector data) were gathered into                                                          
individual ".tab" files for each appropriate date.   The record 17 data                                                           
(direction averaged ion intensities) along with the corresponding time were                                                       
collected into a separate file as a "summary table" (EPSUMMRY.TAB).                                                               
                                                                                                                                  
                  Sample of Reformatted EPAS Ion Count Data                                                                       
                                                                                                                                  
1985 251  0 43 22 11 10      1.      0.      0.      1.      0.      0.      1.      1.                                           
1985 251  0 43 22 21 10      2.      0.      0.      0.      0.      0.      2.      0.                                           
1985 251  0 43 22 31 10      0.      2.      0.      1.      1.      2.      0.      1.                                           
                                                                                                                                  
                                                                                                                                  
                                                                                                                                  
             Sample of Reformatted Ion Intensities Summary Table                                                                  
                                                                                                                                  
1985 257  0 43 22  1.10E-01  4.70E-02  1.10E-02  0.00E-02  0.00E+00 -999.0 -999.0                                                 
1985 257  0 43 54  1.10E-01  3.50E-02  1.20E-02  0.00E+00  0.00E+00 -999.0 -999.0                                                 
1985 257  0 44 26  0.00E+00  0.00E+00  0.00E+00  0.00E+00  0.00E+00 -999.0 -999.0