To:	Distribution

From:	John R. Hayes

Subject:	CFI Software Requirements

References:	1.	7379-9303, “CONTOUR 1553 Bus Specification”, Version 1.01, March 23, 2001.

- CCSDS 102.0-B-4, “Consultative Committee for Space Data Systems Recommendation for Packet Telemetry”, November, 1995.

- Hayes, J.R., “CONTOUR Imager Common Software Requirements”, SRI-00-TBD, TBD.

John R. Hayes

Distribution:

J.J. Blanchette
J.D. Boldt
A.F. Bowman
S.J. Conard (JHU)
W.F. Dellinger
H. DeWitt (DeWitt Associates)
J.V. Finnigan
D.E. Fort
R.M. Furrow
A. Harch (Cornell)
A.J. Harris
J.R. Hayes
K.J. Heffernan
G.A. Heyler
K.C. Ho
M.E. Holdridge
D.C. Humm
N.R. Izenberg
S.E. Jaskulek
R.L. LeGrys
H. Malcom
W.L. Mitnick
S.L. Murchie
G.K. Oxton
E.J. Sheehi
T.S. Spisz
K. Strohbehn
D.S. Tillman
J.W. Warren
K.E. Whittenburg
D. Williams
R.L. Williams
SRI Files
Archives

Table of Contents:

1.	Introduction	1

1.1	Conventions	1

2.	Sensor Architecture	1

3.	Subsystems	2

3.1	Cover	2

3.2	Imager	2

3.3	Filter Wheel	5

3.4	Cube Mirror	5

3.5	Heaters	6

3.6	Digital Solar Attitude Detector	6

3.7	Dust Shield Monitor	6

3.8	Dosimeter	6

4.	Telemetry Interface	6

4.1	Non-packetized Housekeeping	6

4.2	Packets	7

4.2.1	Subpackets	7

4.2.1.1	Status	8

4.2.1.2	DPU Data Structures	13

4.2.1.3	DSAD Images	13

4.2.1.4	Dust Shield Monitor	13

5.	Command Interface	14

5.1	Command and Macro Processing	15

5.2	Commands	15

5.2.1	CFI_COV_DEPLOY – Deploy the Cover	15

5.2.2	CFI_COV_MODE – Enable/Disable Cover Deployment	17

5.2.3	CFI_DUS_DATA – Collect Dust Shield Data for Downlink	17

5.2.4	CFI_FLT_MOVE – Move Filter Wheel	17

5.2.5	CFI_FLT_PWR – Control Filter Wheel Power	18

5.2.6	CFI_FLT_STEP – Step Filter Wheel	18

5.2.7	CFI_HTR_MODE – Set Heater Control Mode	18

5.2.8	CFI_HTR_SENSOR – Select Heater Control Sensor	19

5.2.9	CFI_HTR_TMP – Set Heater Temperature	19

5.2.10	CFI_IMG_COMP_ALG – Select Image Compression Algorithm	19

5.2.11	CFI_IMG_COMP_MODE – Enable/Disable Image Compression	20

5.2.12	CFI_IMG_EXP – Set Image Exposure Time	20

5.2.13	CFI_IMG_FORMAT – Select Image Format	21

5.2.14	CFI_IMG_IMAGE – Collect Images for Downlink	21

5.2.15	CFI_IMG_PWR – Control Imager Power	22

5.2.16	CFI_IMG_REGION – Select Image Region of Interest	22

5.2.17	CFI_MEM_STR_LOAD – Load Values into a Data Structure	22

5.2.18	CFI_MEM_STR_READ – Read a Data Structure	23

5.2.19	CFI_MIR_MOVE – Move Cube Mirror	23

5.2.20	CFI_MIR_PWR – Control Mirror Power	23

5.2.21	CFI_MIR_STEP – Step Cube Mirror	24

5.2.22	CFI_PWR_PRI – Control Primary Power	24

5.2.23	CFI_SAD_EXP – Set DSAD Image Exposure Time	25

5.2.24	CFI_SAD_IMAGE – Collect DSAD Images for Downlink	25

6.	Support Processing	25

6.1	1553 Bus Management	25

6.2	Inter-Integrated Circuit (I2C) Bus Management	25

6.3	Alarms and Monitoring	26

6.4	Fault Avoidance and Recovery	27

7.	DPU Boot ROM Program	28

Appendix 1 - DPU Data Structures	29

Appendix 2 - Alarm & Result Codes	31

Appendix 3 - Acronyms	32

# Introduction

The COmet Nucleus TOUR (CONTOUR) spacecraft carries two imagers, the CONTOUR Remote Imager/Spectrometer (CRISP) and the CONTOUR Forward Imager (CFI).  This document describes the software features unique to CFI.  Included are descriptions of sensor architecture, major subsystems, telemetry, commands, support processing, and the boot program.

## Conventions

For all multi-bit or multi-byte numbers, the first byte sent has the most numerical significance; this is so-called “big-endian” format.  This convention applies to arguments in commands, data in telemetry, and messages over the 1553 bus.

# Sensor Architecture

The CFI imager collects images up to 1024 pixels square.  The following figure shows a block diagram of the optical path, the major subsystems, and the computer.  The Data Processing Unit (DPU) controls the one-time deployable cover, the cube mirror, and the filter wheel and orchestrates image collection and transmission to the spacecraft computer.

Figure 1. Sensor Block Diagram

# Subsystems

The major subsystems, including the cover, the imager, its filter wheel, the cube mirror, and the heaters are discussed below.

## Cover

The CFI optics are protected during launch by a one-time deployable cover.  The cover is deployed by High Output Paraffin (HOP) actuators.  There are two HOP actuators; each actuator has two heaters.  Any one of the four heaters should be sufficient to release the cover.  Each heater can be commanded on independently (CFI_COV_MODE and CFI_COV_DEPLOY).  A mechanical switch provides a telltale that indicates that the cover mechanism has activated.

## Imager

The imaging subsystem, from the CCD to the software, normally operates at a 1 Hz cadence.  A simplified timing diagram of the CCD is shown below.  The figure shows two seconds elapsing, i.e. two images being exposed.  CCD operations are synchronized to a 1 Hz system clock.  The internal CFI 1 Hz clock lags the system-wide clock by ~7 ms.  Image exposures vary in length, but always end ~40 ms before the next CFI 1 Hz pulse.  For science imaging, the exposure time will normally be under 1 second.  However, additional seconds of exposure time can be commanded, for example, to do comet coma imaging.  The figure shows a normal exposure followed by a minimum length “scrub” exposure.  Scrub exposures are used to fill in time whenever no real image is needed.  This ensures that the CCD is read out every second.  The CCD is a frame-transfer device:  at the end of an exposure, the image is rapidly transferred into a buffer within the CCD.  Then the buffered image is read out of the CCD while the next image is being exposed.  The DPU adds an image header provided by the DPU software.  The read out of the entire image must be complete before the end of the exposure.  The time between the end of exposure and the next CFI 1 Hz pulse is used by the software to configure the image read out (e.g., load the header data) and setup the next exposure.

Figure 2. CCD Timing

Each image collected requires three processing steps.  Each step takes one second, but the process can be pipelined such that one image is taken every second.  The resulting three-stage pipeline is shown below.  For multisecond exposures, the expose stage is stretched out and subsequent processing stages are delayed.

Figure 3. Image Collection and Processing Pipeline

For purposes of command planning, only the first two image processing stages are relevant.  During setup, commands are executed to configure image collection in the following stage.  The following figure shows an example image taking sequence.  The commands that control the sequence are being issued from macros; macros execute at the beginning of each second.  A take image command (CFI_IMG_IMAGE) executed in t will cause the CCD to be exposed in t+1.  Similarly, commands to set the exposure time (CFI_IMG_EXP) and select the filter wheel (CFI_FLT_MOVE) that execute in t will take effect in t+1.  Filter wheel movements begin at the end of exposure; ensuring that the movement is complete before the next exposure is the responsibility of the macro and thus the macro author.

Figure 4. Example Image Sequence

The following figure relates the image on the CCD with the spacecraft’s coordinate system.  The numbers on the pixels in the figure indicate the order in which they are downlinked.  Each pixel is 12 bits.

Figure 5. Visible Image Readout

CFI images come in six possible formats shown in the table below.  The format is selected by command (CFI_IMG_FORMAT).  The formats range from the full size of the CCD (1024x1024) down to smaller and smaller windows into the full image.  A command (CFI_IMG_REGION) selects the origin of the window.  Alternatively, the entire 1024x1024 image can be rebinned into 512x512 or 256x256 images.  The rebinning is done directly in the CCD while the windowing is done by downstream logic.  In all of the formats, each line has an additional four dark calibration pixels and a line of temperatures at the end of the image.  Every data item in the image can be compressed from 12 bits to 8 bits if enabled by command (CFI_IMG_COMP_MODE).  The compression is done via table lookup in hardware; one of eight tables can be selected by command (CFI_IMG_COMP_ALG).  Any of these commands executed at time t affect the image exposed at time t+1.

Table 1.  Image Formats

| Mode | Pixels/line | Lines | Temperatures |
| --- | --- | --- | --- |
| 1024 x 1024 | 4 cal + 1024 pixels | 1024 | 4 cal + 1024 temps |
| 512 x 512 window | 4 cal + 512 pixels | 512 | 4 cal + 512 temps |
| 256 x 256 window | 4 cal + 256 pixels | 256 | 4 cal + 256 temps |
| 128 x 128 window | 4 cal + 128 pixels | 128 | 4 cal + 128 temps |
| 512 x 512 rebinned | 4 cal + 512 pixels | 512 | 4 cal + 512 temps |
| 256 x 256 rebinned | 4 cal + 256 pixels | 256 | 4 cal + 256 temps |

Images are downlinked with a header describing the state of the instrument at the time the image was taken.  The header starts with the time at which the image was exposed and a snapshot of the current DPU status.  For multi-second images, the header corresponds to the last second of exposure.  The header format is shown below:

Table 2. Image Header

| Name | Length (bits) | Value | Description |
| --- | --- | --- | --- |
| Time Tag | 32 | Unsigned integer | Spacecraft MET of exposure |
| Analog | 34 * 16 | See Table 8 | Analog status |
| Digital | 14 * 16 | See Table 9 | Digital status |
| Software | 28 * 8 | See Table 10 | Software status |
| Spare | 896 * 8 |  |  |

The DPU software monitors the Focal Plane Unit’s (FPU) latch-up indicator.  If latch-up is detected, the DPU suspends FPU operations.  The length of the suspension is set by an uploadable parameter.

## Filter Wheel

The filter wheel is controlled by a stepping motor.  The motor phases are controlled directly by the DPU software to move the filter wheel.  The phase pattern can be adjusted by software to move the filter wheel forwards or backwards.  A resolver provides an absolute position reading of the wheel.

The filter move command (CFI_FLT_MOVE) uses the commanded filter number to look up an absolute goal position from a table, reads the current position from the resolver, and computes the number of steps and travel direction needed to arrive at the goal in the least amount of time.  The motor is then stepped to the desired goal.  Alternatively, the filter step command (CFI_FLT_STEP) will move the filter wheel the commanded number of resolver counts forward or backward.  The power to the resolver can be commanded on or off (CFI_FLT_PWR).  If the power to the resolver is turned off, further move commands will be dead-reckoned from the last resolver reading.  The filter wheel is characterized by several uploadable parameters including the motor power level, the scale factor between resolver counts and motor steps, the filter wheel positions, etc.  The filters are listed in the following table.

Table 3.  Filters

| Filter Number | Spectral Band (nm) | Use |
| --- | --- | --- |
| 1 | “clear” | Navigation |
| 2 | 920 | Geology |
| 3 | 840 | Geology |
| 4 | 620 | Red (geology) |
| 5 | 445 | Blue (geology) and backup continuum |
| 6 | 526 | Green (geology) and C2 continuum |
| 7 | 514.1 | C2 emission (coma) |
| 8 | 309 | OH emission (coma) |
| 9 | 344.8 | OH and CN continuum |
| 10 | 387 | CN emission (coma) |

## Cube Mirror

The mirror is controlled by a stepping motor.  The motor phases are controlled directly by the DPU software to move the mirror.  The phase pattern can be adjusted by software to move the mirror forwards or backwards.  A resolver provides an absolute position reading of the mirror.

The mirror move command (CFI_MIR_MOVE) uses the commanded mirror side to look up an absolute goal position from a table, reads the current position from the resolver, and computes the number of steps needed to arrive at the goal traveling in a preferred direction.  The motor is then stepped to the desired goal.  Alternatively, the mirror step command (CFI_MIR_STEP) will move the mirror the commanded number of resolver counts forward or backward.  The power to the resolver can be commanded on or off (CFI_MIR_PWR).  If the power to the resolver is turned off, further move commands will be dead-reckoned from the last resolver reading.  The mirror is characterized by several uploadable parameters including the motor power level, the scale factor between resolver counts and motor steps, the mirror side positions, and the preferred move direction.

## Heaters

The CFI DPU controls the temperature of the radiator used to cool the CCD.  The heater may be commanded off, on, or controlled by software (CFI_HTR_MODE).  If the heater is being controlled by software, it uses the setpoint and hysteresis commanded (CFI_HTR_TMP).  The software uses one of four temperatures sensors to control the heater; the sensor used is commandable (CFI_HTR_SENSOR).  Every second the selected temperature is compared against the limits.  If the temperature is too low, the heater will be turned on.  If the temperature is too high, the heater will be turned off.

## CONTOUR Hardware Experimental Acquisition Package

The CFI DPU monitors the CONTOUR Hardware Experimental Acquisition Package (CHEAP).  CHEAP contains three experiments:  digital solar attitude detectors, a dust shield monitor, and a dosimeter.  These are described below.  Because of CHEAP’s experimental nature, commands are provided for doing raw reads and writes to the hardware (CFI_CHE_PEEK and CFI_CHE_POKE).  CHEAP is present as a flight test and is not an operational part of CONTOUR.

### Digital Solar Attitude Detector

The CFI DPU controls two Digital Solar Attitude Detector (DSAD) imagers.  Each device has a 200 x 200 pixel array; each pixel is ten bits.  The only difference between the DSADs is that one views space through a pinhole and the other views space through a lens.  Image collection is controlled via command (CFI_SAD_IMAGE).  Another command (CFI_SAD_EXP) sets the exposure time for each device.

### Dust Shield Monitor

The CFI DPU monitors degradation of the spacecraft’s dust shield.  Sixteen measurements are taken over different regions of the dust shield; each measurement is ten bits.  Data collection is controlled via command (CFI_DUS_DATA).

### Dosimeter

The CFI DPU monitors the total radiation dose that the spacecraft receives.  A single ten-bit dosimeter measurement is taken on command (CFI_DOS_DATA).

# Telemetry Interface

The spacecraft Command & Data Handling (C&DH) system collects telemetry from CFI over the 1553 bus as non-packetized housekeeping and as CCSDS packets.

## Non-packetized Housekeeping

The C&DH system picks up a 16-byte non-packetized housekeeping record every second.  The contents can be incorporated into C&DH autonomy processing.  The C&DH system also assembles the data into a housekeeping packet.  The format of the non-packetized housekeeping record is shown below.

Table 4.  Non-Packetized Housekeeping Format

| Name | Length (bits) | Value | Description |
| --- | --- | --- | --- |
| Version | 8 | 0 = Boot >0 = Application | Software version |
| Alarm | 8 | See Table 20 | Latest alarm id |
| Alarm Type | 1 | 0 = Persistent 1 = Transient | Latest alarm type |
| Alarms | 7 | Unsigned integer | Count of alarms |
| Executed | 8 | Unsigned integer | Commands executed |
| Rejected | 8 | Unsigned integer | Commands rejected |
| Mac Exec | 8 | Unsigned integer | Macro commands executed |
| Mac Rej | 8 | Unsigned integer | Macro commands rejected |
| Spare | 9 * 8 |  |  |

## Packets

The C&DH system collects up to one packet from CFI every second.  These packets are memory dump and subpacket packets as described in Reference 3.  CFI images are sent directly to the C&DH system for packetization.

Table 5.  Packet Types

| Product | Data Id (binary) | When Sent |
| --- | --- | --- |
| Memory Dump | 000 0000 | On demand |
| Subpacket | 000 0001 | As needed |
| Images | 000 0010 | Commandable interval |

### Subpackets

Instead of coercing imager data to fit into the fixed size CONTOUR packets, the imagers use variable-sized subpackets that “float” through fixed-size packets (see Reference 3).

The subpacket types produced by CFI are listed in the table below.

Table 6.  Subpacket Types

| Product | Subpacket Id (hex) | When Generated |
| --- | --- | --- |
| Boot Status | 0x0000 | Commandable interval |
| Status | 0x0001 | Commandable interval |
| Command Echo | 0x0002 | As needed |
| Alarm | 0x0003 | As needed |
| Memory Checksum | 0x0004 | On demand |
| Monitor Limits | 0x0005 | On demand |
| DPU Parameters | 0x0006 | On demand |
| DSAD Pinhole Summary | 0x0007 | On demand |
| DSAD Lensed Summary | 0x0008 | On demand |
| DSAD Pinhole Image | 0x0009 | On demand |
| DSAD Lensed Image | 0x000a | On demand |
| Dust Shield Data | 0x000b | On demand |
| Dosimeter Data | 0x000c | On demand |
| CHEAP Peek | 0x000d | On demand |
| Flush | 0x3fff | As needed |

#### Status

The DPU generates a status subpacket periodically.  The rate is controlled by a command (see CFI_STAT_INT).  The subpacket consists of a subpacket header and status data; the status includes analog, digital, and DPU software.  The overall subpacket format is shown in the following table; the formats of the individual components are shown in the subsequent tables.

Table 7.  DPU Status Subpacket Format

| Name | Length (bits) | Value | Description |
| --- | --- | --- | --- |
| Time Tag | 32 | Unsigned integer | Spacecraft MET |
| Grouping | 2 | 11 = None | Grouping flags |
| Subpacket Id | 14 | 0x0001 | Identifies subpacket type |
| Length | 16 | 124 | Number of data bytes in subpacket |
| Analog | 34 * 16 | See Table 8 | Analog readings |
| Digital | 14 * 16 | See Table 9 | Digital configuration and feedback |
| Software | 28 * 8 | See Table 10 | Software configuration and status |

Table 8.  Analog Status

| Name | Length (bits) | Value | Description |
| --- | --- | --- | --- |
| Ana DPU/1 | 16 | -8192 – 8191 | CCD heater current |
| Ana DPU/6 | 16 | -8192 – 8191 | DPU current |
| Ana DPU/7 | 16 | -8192 – 8191 | DPU voltage |
| Ana IM/0 | 16 | -8192 – 8191 | Imager converter current |
| Ana IM/1 | 16 | -8192 – 8191 | HOP actuator #1 heater #1 current |
| Ana IM/2 | 16 | -8192 – 8191 | HOP actuator #1 heater #2 current |
| Ana IM/3 | 16 | -8192 – 8191 | Imager current |
| Ana IM/4 | 16 | -8192 – 8191 | HOP actuator #2 heater #1 current |
| Ana IM/5 | 16 | -8192 – 8191 | Imager voltage |
| Ana IM/6 | 16 | -8192 – 8191 | HOP actuator #2 heater #2 current |
| Ana FW/0 | 16 | -8192 – 8191 | FW motor primary current |
| Ana FW/1 | 16 | -8192 – 8191 | FW motor current |
| Ana FW/2 | 16 | -8192 – 8191 | FW motor converter current |
| Ana FW/3 | 16 | -8192 – 8191 | FW 15V current |
| Ana FW/4 | 16 | -8192 – 8191 | FW 15V voltage |
| Ana CM/0 | 16 | -8192 – 8191 | CM motor primary current |
| Ana CM/1 | 16 | -8192 – 8191 | CM motor current |
| Ana CM/2 | 16 | -8192 – 8191 | CM motor converter current |
| Ana CM/3 | 16 | -8192 – 8191 | CM 15V current |
| Ana CM/4 | 16 | -8192 – 8191 | CM 15V voltage |
| Temp 0 | 16 | 0 – 1023 | CCD plate temperature #1 |
| Temp 1 | 16 | 0 – 1023 | CCD plate temperature #2 |
| Temp 2 | 16 | 0 – 1023 | Top bracket temperature |
| Temp 3 | 16 | 0 – 1023 | Bottom bracket temperature |
| Temp 4 | 16 | 0 – 1023 | M1/M2 tube base temperature |
| Temp 5 | 16 | 0 – 1023 | Bench fold cube temperature |
| Temp 6 | 16 | 0 – 1023 | Filter motor temperature |
| Temp 7 | 16 | 0 – 1023 | Cube motor temperature |
| Temp 8 | 16 | 0 – 1023 | Telescope tube bottom temperature |
| Temp 9 | 16 | 0 – 1023 | Telescope tube top temperature |
| Temp 10 | 16 | 0 – 1023 | Radiator temperature #2 |
| Temp 11 | 16 | 0 – 1023 | Radiator temperature #1 |
| Temp 12 | 16 | 0 – 1023 | Cover temperature #2 |
| Temp 13 | 16 | 0 – 1023 | Cover temperature #1 |

Table 9.  Digital Status

| Name | Length (bits) | Value | Description |
| --- | --- | --- | --- |
| Spare | 15 |  |  |
| Telltale | 1 | 0 = Closed 1 = Open | Cover telltale |
| FW Resolver | 16 | Unsigned integer | Filter wheel position |
| Mirror Resolver | 16 | Unsigned integer | Cube mirror position |
| Spare | 1 |  |  |
| CCD Heater | 1 | 0 = Off 1 = On | CCD heater power |
| Spare | 6 |  |  |
| IM Primary | 1 | 0 = Off 1 = On | Imager board primary power |
| HOP #2/2 | 1 | 0 = Off 1 = On | HOP actuator #2 heater #2 power |
| HOP #2/1 | 1 | 0 = Off 1 = On | HOP actuator #2 heater #1 power |
| HOP #1/2 | 1 | 0 = Off 1 = On | HOP actuator #1 heater #2 power |
| HOP #1/1 | 1 | 0 = Off 1 = On | HOP actuator #1 heater #1 power |
| Spare | 2 |  |  |
| IM Power | 1 | 0 = Off 1 = On | Imager focal plane power |
| FW Primary | 1 | 0 = Off 1 = On | FW motor board primary power |
| FW Resolver | 1 | 0 = Off 1 = On | FW resolver power |
| Spare | 6 |  |  |
| CM Primary | 1 | 0 = Off 1 = On | CM motor board primary power |
| CM Resolver | 1 | 0 = Off 1 = On | CM resolver power |
| Spare | 6 |  |  |
| Spare | 1 |  |  |
| FW Level | 3 | Unsigned integer | FW motor power level |
| Spare | 1 |  |  |
| FW Motor | 1 | 0 = Off 1 = On | FW motor current enable |
| FW Phase | 2 | Unsigned integer | FW motor phase drive |
| Spare | 1 |  |  |
| CM Level | 3 | Unsigned integer | CM motor power level |
| Spare | 1 |  |  |
| CM Motor | 1 | 0 = Off 1 = On | CM motor current enable |
| CM Phase | 2 | Unsigned integer | CM motor phase drive |
| DSAD Pinhole Expose Time | 8 | Unsigned integer | DSAD pinhole exposure time (milliseconds) |
| DSAD Lensed Expose Time | 8 | Unsigned integer | DSAD lensed exposure time (milliseconds) |
| Spare | 16 |  |  |
| Spare | 2 |  |  |
| Compress | 1 | 0 = No compression 1 = Compress | Image compression enable |
| Comp. Type | 3 | 0 = High-range identity 1 = Low-end identity 2 = Mid-range identity 3 = DN-weighted SNR 4 = Inverse root 2 power 5 = Linear 6 = SNR proportional 7 = Root 2 power | Image compression type |
| Image X | 10 | Unsigned integer | Image X origin |
| Spare | 3 |  |  |
| Image Downlink | 1 | 0 = No downlink 1 = Downlink | Image downlink enable |
| Image Format | 2 | 0 = 1024 x 1024 1 = 512 x 512 2 = 256 x 256 3 = 128 x 128 | Image format |
| Image Y | 10 | Unsigned integer | Image Y origin |
| Spare | 12 |  |  |
| Binning Enable | 1 | 0 = Disable 1 = Enable | Image binning enable |
| Spare | 1 |  |  |
| Binning Mode | 1 | 0 = 4 x 4 binning 1 = 2 x 2 binning | Image binning mode |
| Binning On/Off | 1 | 0 = Off 1 = On | Image binning on/off |
| Image Expose Time | 7 | Unsigned integer | Additional image exposure time (seconds) |
| Image Start | 9 | Unsigned integer | Image exposure start time |
| Imager Status | 16 |  | Imager FPU status word |
| Spare | 16 |  |  |

Table 10. Software Status

| Name | Length (bits) | Value | Description |
| --- | --- | --- | --- |
| Image Time | 16 | 0 – 65534: Remaining 65535: Forever | Image downlink time remaining (seconds) |
| Image Interval | 16 | Unsigned integer | Interval between downlink images (seconds) |
| Spare | 16 |  |  |
| Spare | 16 |  |  |
| Heater Setpoint | 16 | Unsigned integer | Heater setpoint |
| Heater Hysteresis | 8 | Unsigned integer | Heater hysteresis |
| Heater Mode | 2 | 0 = Off 1 = On 2 = Software control | Heater control mode |
| Heater Sensor | 2 | 0 = CCD plate temp. #1 1 = CCD plate temp. #2 2 = Radiator temp. #1 3 = Radiator temp. #2 | Sensor selected to control heater |
| Filter | 4 | 1 – 10 | Commanded filter number |
| Cover Mode | 1 | 0 = Disable deployment 1 = Enable deployment | Cover deployment mode |
| Cube Side | 2 | 0 – 3 | Commanded cube mirror side |
| Spare | 13 |  |  |
| Macro Blocks | 16 | Unsigned integer | Number of macro blocks free |
| DPU Version | 8 | Unsigned integer | DPU software version number |
| Alarm Id | 8 | See Table 20 | Latest alarm Id |
| Alarm Type | 1 | 0 = Persistent 1 = Transient | Latest alarm type |
| Alarm Count | 7 | Unsigned integer | Count of alarms |
| Cmd Exec | 8 | Unsigned integer | Commands executed |
| Cmd Reject | 8 | Unsigned integer | Commands rejected |
| Mac Exec | 8 | Unsigned integer | Macro commands executed |
| Mac Reject | 8 | Unsigned integer | Macro commands rejected |
| Status Int. | 8 | 1 – 255 (0 = Off) | Status interval (seconds) |
| Macro Id | 8 | Unsigned integer | Id of most recent macro executed |
| Auto Flush | 1 | 0 = Disable 1 = Enable | Automatic telemetry flush |
| Macro Learn | 1 | 0 = Not learning 1 = Learning | Macro learn mode |
| Monitor Response | 1 | 0 = Disable 1 = Enable | Monitor response |
| Spare | 5 |  |  |
| Spare | 16 |  |  |

#### DPU Data Structures

The DPU makes several of its internal data structures available for modification or downlink.  The data structures can be modified by command (CFI_MEM_STR_LOAD).  The current data structures can also be downlinked by command (CFI_MEM_STR_READ).  The data structures are described in Appendix 1.

#### DSAD Data

The DSAD computes the X, Y centroid of the image.  These, along with other analog values, are sent as a summary subpacket in response to a command (CFI_SAD_IMAGE).

Table 11.  DSAD Summary Subpacket Format

| Name | Length (bits) | Value | Description |
| --- | --- | --- | --- |
| Time Tag | 32 | Unsigned integer | Spacecraft MET |
| Grouping | 2 | 11 = None | Grouping flags |
| Subpacket Id | 14 | 0x0007 (or 0x0008) | Identifies subpacket type |
| Length | 16 | 14 | Number of data bytes in subpacket |
| Analog 0 | 16 | 0 – 1023 | Ground |
| Analog 1 | 16 | 0 – 1023 | Vptat |
| Analog 2 | 16 | 0 – 1023 | DAC test point |
| Analog 3 | 16 | 0 – 1023 | Divider test point |
| Analog 4 | 16 | 0 – 1023 | Bandgap |
| Analog 5 | 16 | 0 – 1023 | Vertical (Y) position |
| Analog 6 | 16 | 0 – 1023 | Horizontal (X) position |

The raw image may also be sent in addition to the summary if commanded (CFI_SAD_IMAGE).  Each DSAD image is sent as a series of subpackets. Each subpacket contains a single 200-pixel scan line from the image.  Each line is prefixed with a subheader containing the line number.

Table 12.  DSAD Image Subpacket Format

| Name | Length (bits) | Value | Description |
| --- | --- | --- | --- |
| Time Tag | 32 | Unsigned integer | Spacecraft MET |
| Grouping | 2 | 11 = None | Grouping flags |
| Subpacket Id | 14 | 0x0009 (or 0x000a) | Identifies subpacket type |
| Length | 16 | 402 | Number of data bytes in subpacket |
| Line | 8 | 0 – 199 | Image line number |
| Spare | 8 |  |  |
| Image | 200 * 16 | 0 – 1023 | Image line |

#### Dust Shield Monitor

The DPU generates a dust shield monitor subpacket on command (see CFI_DUS_DATA).  The subpacket consists of a subpacket header and sixteen measurements.

Table 13.  Dust Shield Monitor Subpacket Format

| Name | Length (bits) | Value | Description |
| --- | --- | --- | --- |
| Time Tag | 32 | Unsigned integer | Spacecraft MET |
| Grouping | 2 | 11 = None | Grouping flags |
| Subpacket Id | 14 | 0x000b | Identifies subpacket type |
| Length | 16 | 32 | Number of data bytes in subpacket |
| Data | 16 * 16 | 0 – 1023 | Dust shield measurements |

#### Dosimeter

The DPU generates a dosimeter subpacket on command (see CFI_DOS_DATA).  The subpacket consists of a subpacket header and a single dosimeter measurement.

Table 14.  Dosimeter Subpacket Format

| Name | Length (bits) | Value | Description |
| --- | --- | --- | --- |
| Time Tag | 32 | Unsigned integer | Spacecraft MET |
| Grouping | 2 | 11 = None | Grouping flags |
| Subpacket Id | 14 | 0x000c | Identifies subpacket type |
| Length | 16 | 2 | Number of data bytes in subpacket |
| Data | 16 | 0 – 1023 | Dosimeter measurements |

#### CHEAP Peek

The DPU generates a CHEAP peek subpacket on command (see CFI_CHE_PEEK).  The subpacket consists of a subpacket header and a single CHEAP data value.

Table 15.  CHEAP Peek Subpacket Format

| Name | Length (bits) | Value | Description |
| --- | --- | --- | --- |
| Time Tag | 32 | Unsigned integer | Spacecraft MET |
| Grouping | 2 | 11 = None | Grouping flags |
| Subpacket Id | 14 | 0x000d | Identifies subpacket type |
| Length | 16 | 2 | Number of data bytes in subpacket |
| Data | 16 | Unsigned integer | CHEAP peek data value |

# Command Interface

The DPU receives and processes CCSDS telecommand packets containing one or more commands.  The format of the telecommand packet and constituent commands is described in Reference 3.

## Command and Macro Processing

Most commands are executed as soon as they are received; exceptions are noted in the individual command descriptions.  Each command is echoed after it is executed by the DPU.  A command echo subpacket containing the opcode and some arguments along with a code summarizing the command’s result is downlinked.

Some default macros are available as soon as the DPU is started.  Most of these macros are one or two commands long and are used by the monitoring subsystem to respond to out of limit conditions.  A default macro can be replaced with a new macro via CFI_MAC_DEF and CFI_MAC_ENDEF.  The default macros are shown in the following table.

Table 16.  Default Macros

| ID | Action | Commands |
| --- | --- | --- |
| 0 | No action | CFI_CMD_NULL |
| 1 | Shutdown | CFI_IMG_PWR OFF CFI_FLT_MOVE CLEAR CFI_HTR_MODE OFF |
| 2 | Heater Power Off | CFI_HTR_MODE OFF |
| 3 | Cover HOPS Off | CFI_COV_DEPLOY HOP1/1 OFF CFI_COV_DEPLOY HOP1/2 OFF CFI_COV_DEPLOY HOP2/1 OFF CFI_COV_DEPLOY HOP2/2 OFF |
| 4 | Mirror Power Off | CFI_PWR_PRI CM OFF |
| 5 | Imager Power Off | CFI_IMG_PWR OFF |
| 6 | Filter Power Off | CFI_PWR_PRI FW OFF |
| 7 | Stop Macro Processing | CRS_MON_CNTRL DISABLE CRS_MEM_RUN kill all macros |
| 8 – 63 | Reserved |  |
| 64 – 255 | Reserved for mission operations |  |

## Commands

The CRISP and CFI common commands are described in Reference 3.  CFI-specific commands are defined below.

### CFI_CHE_PEEK – Read CHEAP Hardware

Read a 16-bit data value from the CHEAP hardware and telemeter the result.  Note: only one peek or poke can be commanded per second.

| Name | Length (bits) | Value | Description |
| --- | --- | --- | --- |
| Opcode | 16 | 0x0133 |  |
| Macro? | 1 | 0 = Execute 1 = Append to macro | Macro load bit |
| Length | 15 | 3 | Command length in 32-bit words |
| Board | 8 | 66 = DSAD (FPGA) 67 = Dosimeter (xRIO) 36 = Dust (TRIO) | Board’s I2C address |
| Pad | 24 | 0 | Pad up to 32-bit boundary |
| Checksum | 32 |  | 32 bit XOR |

### CFI_CHE_POKE – Write CHEAP Hardware

Write an 8-bit data value to the CHEAP hardware.  Note: only one peek or poke can be commanded per second.

| Name | Length (bits) | Value | Description |
| --- | --- | --- | --- |
| Opcode | 16 | 0x0130 |  |
| Macro? | 1 | 0 = Execute 1 = Append to macro | Macro load bit |
| Length | 15 | 3 | Command length in 32-bit words |
| Board | 8 | 66 = DSAD (FPGA) 67 = Dosimeter (xRIO) 36 = Dust (TRIO) | Board’s I2C address |
| Address | 8 | Unsigned integer | Register address within board |
| Data | 8 | Unsigned integer | Data to write |
| Pad | 8 | 0 | Pad up to 32-bit boundary |
| Checksum | 32 |  | 32 bit XOR |

### CFI_COV_DEPLOY – Deploy the Cover

Turn power to cover’s HOP actuators off or on.  Turning on the actuator deploys the cover.  With operation 2, the actuator power is removed automatically by the DPU software once the cover is open.  With operation 3, the actuator power is removed after a timeout period; the timeout is a parameter.  With operation 4, the actuator power is removed once the cover is open or the timeout period elapses.  This command will be rejected unless specifically enabled with the CFI_COV_MODE command.  Note: the imager primary power must be turned on for the cover to deploy.

| Name | Length (bits) | Value | Description |
| --- | --- | --- | --- |
| Opcode | 16 | 0x0100 |  |
| Macro? | 1 | 0 = Execute 1 = Append to macro | Macro load bit |
| Length | 15 | 3 | Command length in 32-bit words |
| Operation | 8 | 0 = Off 1 = On 2 = On until deployed 3 = On until timeout 4 = On until deployed or timeout | Operation for the given heater |
| Heater | 8 | 0 = HOP 1, heater 1 1 = HOP 1, heater 2 2 = HOP 2, heater 1 3 = HOP 2, heater 2 | Heater |
| Pad | 16 | 0 | Pad up to 32-bit boundary |
| Checksum | 32 |  | 32 bit XOR |

### CFI_COV_MODE – Enable/Disable Cover Deployment

Enable or disable deployment of the cover.  This is a safety interlock; the actuators must be enabled before actually powering the actuator (with CFI_COV_DEPLOY).

| Name | Length (bits) | Value | Description |
| --- | --- | --- | --- |
| Opcode | 16 | 0x0103 |  |
| Macro? | 1 | 0 = Execute 1 = Append to macro | Macro load bit |
| Length | 15 | 3 | Command length in 32-bit words |
| Mode | 8 | 0 = Disable 1 = Enable | Deployment enable/disable |
| Pad | 24 | 0 | Pad up to 32-bit boundary |
| Checksum | 32 |  | 32 bit XOR |

### CFI_DOS_DATA – Collect Dosimeter Data for Downlink

Collect dosimeter data and downlink it.

| Name | Length (bits) | Value | Description |
| --- | --- | --- | --- |
| Opcode | 16 | 0x12e |  |
| Macro? | 1 | 0 = Execute 1 = Append to macro | Macro load bit |
| Length | 15 | 3 | Command length in 32-bit words |
| Spare | 32 |  |  |
| Checksum | 32 |  | 32 bit XOR |

### CFI_DUS_DATA – Collect Dust Shield Data for Downlink

Collect dust shield data and downlink it.

| Name | Length (bits) | Value | Description |
| --- | --- | --- | --- |
| Opcode | 16 | 0x011d |  |
| Macro? | 1 | 0 = Execute 1 = Append to macro | Macro load bit |
| Length | 15 | 3 | Command length in 32-bit words |
| Spare | 32 |  |  |
| Checksum | 32 |  | 32 bit XOR |

### CFI_FLT_MOVE – Move Filter Wheel

Move filter wheel to indicated position.  The filter movement begins at the end of the current exposure.  Note: the FW motor primary power must be turned on for the filter wheel to move.

| Name | Length (bits) | Value | Description |
| --- | --- | --- | --- |
| Opcode | 16 | 0x0105 |  |
| Macro? | 1 | 0 = Execute 1 = Append to macro | Macro load bit |
| Length | 15 | 3 | Command length in 32-bit words |
| Filter | 8 | 1 – 10 | Filter wheel position |
| Pad | 24 | 0 | Pad up to 32-bit boundary |
| Checksum | 32 |  | 32 bit XOR |

### CFI_FLT_PWR – Control Filter Wheel Power

Turn filter wheel resolver power off or on.  Note: the FW motor primary power must be turned on for the filter wheel resolver to operate.

| Name | Length (bits) | Value | Description |
| --- | --- | --- | --- |
| Opcode | 16 | 0x0106 |  |
| Macro? | 1 | 0 = Execute 1 = Append to macro | Macro load bit |
| Length | 15 | 3 | Command length in 32-bit words |
| Mode | 8 | 0 = Off 1 = On | Filter wheel resolver power off/on |
| Pad | 24 | 0 | Pad up to 32-bit boundary |
| Checksum | 32 |  | 32 bit XOR |

### CFI_FLT_STEP – Step Filter Wheel

Move filter wheel the indicated number of resolver counts.  Note: the FW motor primary power must be turned on for the filter wheel to move.

| Name | Length (bits) | Value | Description |
| --- | --- | --- | --- |
| Opcode | 16 | 0x012d |  |
| Macro? | 1 | 0 = Execute 1 = Append to macro | Macro load bit |
| Length | 15 | 3 | Command length in 32-bit words |
| Counts | 16 | -32768 – 32767 | Filter motion (resolver counts) |
| Pad | 16 | 0 | Pad up to 32-bit boundary |
| Checksum | 32 |  | 32 bit XOR |

### CFI_HTR_MODE – Set Heater Control Mode

Select heater off, on, or controlled by software.

| Name | Length (bits) | Value | Description |
| --- | --- | --- | --- |
| Opcode | 16 | 0x0109 |  |
| Macro? | 1 | 0 = Execute 1 = Append to macro | Macro load bit |
| Length | 15 | 3 | Command length in 32-bit words |
| Mode | 8 | 0 = Off 1 = On 2 = Software control | Control mode |
| Pad | 24 | 0 | Pad up to 32-bit boundary |
| Checksum | 32 |  | 32 bit XOR |

### CFI_HTR_SENSOR – Select Heater Control Sensor

Select the temperature sensor used to control the heater.

| Name | Length (bits) | Value | Description |
| --- | --- | --- | --- |
| Opcode | 16 | 0x010a |  |
| Macro? | 1 | 0 = Execute 1 = Append to macro | Macro load bit |
| Length | 15 | 3 | Command length in 32-bit words |
| Sensor | 8 | 0 = CCD plate temp. #1 1 = CCD plate temp. #2 2 = Radiator temp. #1 3 = Radiator temp. #2 | Temperature sensor |
| Pad | 24 | 0 | Pad up to 32-bit boundary |
| Checksum | 32 |  | 32 bit XOR |

### CFI_HTR_TMP – Set Heater Temperature

Set temperature goal of the heater.  The temperature will be held between the given setpoint and setpoint+hysteresis.

| Name | Length (bits) | Value | Description |
| --- | --- | --- | --- |
| Opcode | 16 | 0x010c |  |
| Macro? | 1 | 0 = Execute 1 = Append to macro | Macro load bit |
| Length | 15 | 3 | Command length in 32-bit words |
| Setpoint | 16 | Unsigned integer | Temperature setpoint (A/D units) |
| Hysteresis | 8 | Unsigned integer | Hysteresis (A/D units) |
| Pad | 8 | 0 | Pad up to 32-bit boundary |
| Checksum | 32 |  | 32 bit XOR |

### CFI_IMG_COMP_ALG – Select Image Compression Algorithm

Select image compression algorithm.  When executed at time t affects the exposure taken at time t+1.

| Name | Length (bits) | Value | Description |
| --- | --- | --- | --- |
| Opcode | 16 | 0x010f |  |
| Macro? | 1 | 0 = Execute 1 = Append to macro | Macro load bit |
| Length | 15 | 3 | Command length in 32-bit words |
| Mode | 8 | 0 = High-range identity 1 = Low-end identity 2 = Mid-range identity 3 = DN-weighted SNR 4 = Inverse root 2 power 5 = Linear 6 = SNR proportional 7 = Root 2 power | Compression algorithm |
| Pad | 24 | 0 | Pad up to 32-bit boundary |
| Checksum | 32 |  | 32 bit XOR |

### CFI_IMG_COMP_MODE – Enable/Disable Image Compression

Enable or disable image compression.  When executed at time t affects the exposure taken at time t+1.

| Name | Length (bits) | Value | Description |
| --- | --- | --- | --- |
| Opcode | 16 | 0x0111 |  |
| Macro? | 1 | 0 = Execute 1 = Append to macro | Macro load bit |
| Length | 15 | 3 | Command length in 32-bit words |
| Mode | 8 | 0 = Disable 1 = Enable | Enable/disable image compression |
| Pad | 24 | 0 | Pad up to 32-bit boundary |
| Checksum | 32 |  | 32 bit XOR |

### CFI_IMG_EXP – Set Image Exposure Time

Set image exposure time.  An exposure time set at time t effects the exposure taken at t+1.  The exposure time is specified in two pieces.  The first argument how long to expose in the first second; this can range from 2.048 ms to 958.464 ms.  The second argument specifies additional whole seconds of exposure.  Note: If the commanded exposure time is greater than the commanded collection interval (see CFI_IMG_IMAGE), the exposure time is reduced to match the collection interval.

| Name | Length (bits) | Value | Description |
| --- | --- | --- | --- |
| Opcode | 16 | 0x0112 |  |
| Macro? | 1 | 0 = Execute 1 = Append to macro | Macro load bit |
| Length | 15 | 3 | Command length in 32-bit words |
| Time | 16 | 1 – 468 | Exposure time in 2.048 ms units |
| Seconds | 16 | 0 – 127 | Additional exposure time in seconds |
| Checksum | 32 |  | 32 bit XOR |

### CFI_IMG_FORMAT – Select Image Format

Select the format of the images to be telemetered.  When executed at time t affects the exposure taken at time t+1.

| Name | Length (bits) | Value | Description |
| --- | --- | --- | --- |
| Opcode | 16 | 0x0114 |  |
| Macro? | 1 | 0 = Execute 1 = Append to macro | Macro load bit |
| Length | 15 | 3 | Command length in 32-bit words |
| Format | 8 | 0 = 1024 x 1024 1 = 512 x 512 window 2 = 256 x 256 window 3 = 128 x 128 window 4 = 512 x 512 rebin 5 = 256 x 256 rebin | Image format |
| Pad | 24 | 0 | Pad up to 32-bit boundary |
| Checksum | 32 |  | 32 bit XOR |

### CFI_IMG_IMAGE – Collect Images for Downlink

Collect a series of images and downlink them.  An exposure requested at time t is taken at t+1.  If an image collection series is in progress and a new CFI_IMG_IMAGE is issued, the new command supersedes the old command.

| Name | Length (bits) | Value | Description |
| --- | --- | --- | --- |
| Opcode | 16 | 0x0117 |  |
| Macro? | 1 | 0 = Execute 1 = Append to macro | Macro load bit |
| Length | 15 | 3 | Command length in 32-bit words |
| Time | 16 | 0 – 65534 = Duration 65535 = Forever | Time in which to collect images (seconds) |
| Interval | 16 | 1 – 65535 | Interval between images (seconds) |
| Checksum | 32 |  | 32 bit XOR |

### CFI_IMG_PWR – Control Imager Power

Turn imager FPU power off or on.  Note: the imager primary power must be turned on for the imager FPU to activate.

| Name | Length (bits) | Value | Description |
| --- | --- | --- | --- |
| Opcode | 16 | 0x0118 |  |
| Macro? | 1 | 0 = Execute 1 = Append to macro | Macro load bit |
| Length | 15 | 3 | Command length in 32-bit words |
| Mode | 8 | 0 = Off 1 = On | Imager power off/on |
| Pad | 24 | 0 | Pad up to 32-bit boundary |
| Checksum | 32 |  | 32 bit XOR |

### CFI_IMG_REGION – Select Image Region of Interest

Set the origin of the image to be telemetered.  When executed at time t affects the exposure taken at time t+1.

| Name | Length (bits) | Value | Description |
| --- | --- | --- | --- |
| Opcode | 16 | 0x011b |  |
| Macro? | 1 | 0 = Execute 1 = Append to macro | Macro load bit |
| Length | 15 | 3 | Command length in 32-bit words |
| X | 16 | 0 – 1023 | X origin |
| Y | 16 | 0 – 1023 | Y origin |
| Checksum | 32 |  | 32 bit XOR |

### CFI_MEM_STR_LOAD – Load Values into a Data Structure

Load the data values into the identified data structure at the location denoted by the offset.  The byte count determines how many load bytes follow and may be up to 128 bytes.  The padding after the data forces the size of the load to be a multiple of 4 bytes; M+N is always a multiple of 4.

| Name | Length (bits) | Value | Description |
| --- | --- | --- | --- |
| Opcode | 16 | 0x0023 |  |
| Macro? | 1 | 0 = Execute 1 = Append to macro | Macro load bit |
| Length | 15 | 4 – 35 | Command length in 32-bit words |
| Id | 8 | 0 = Monitor limits 1 = DPU parameters | Id of data structure |
| Byte Count | 8 | 0 – 128 (M) | Number of bytes in data field |
| Offset | 16 | Unsigned integer | Byte offset into data structure |
| Data | M * 8 |  | Load data |
| Pad | N * 8 | 0 | Pad up to 32-bit boundary |
| Checksum | 32 |  | 32 bit XOR |

### CFI_MEM_STR_READ – Read a Data Structure

Dump the identified data structure.

| Name | Length (bits) | Value | Description |
| --- | --- | --- | --- |
| Opcode | 16 | 0x0025 |  |
| Macro? | 1 | 0 = Execute 1 = Append to macro | Macro load bit |
| Length | 15 | 3 | Command length in 32-bit words |
| Id | 8 | 0 = Monitor limits 1 = DPU parameters | Id of data structure |
| Pad | 24 | 0 | Pad up to 32-bit boundary |
| Checksum | 32 |  | 32 bit XOR |

### CFI_MIR_MOVE – Move Cube Mirror

Move cube mirror to use the indicated side.  Note: the CM motor primary power must be turned on for the cube mirror to move.

| Name | Length (bits) | Value | Description |
| --- | --- | --- | --- |
| Opcode | 16 | 0x0121 |  |
| Macro? | 1 | 0 = Execute 1 = Append to macro | Macro load bit |
| Length | 15 | 3 | Command length in 32-bit words |
| Side | 8 | 0 – 3 | Mirror side |
| Pad | 24 | 0 | Pad up to 32-bit boundary |
| Checksum | 32 |  | 32 bit XOR |

### CFI_MIR_PWR – Control Mirror Power

Turn cube mirror resolver power off or on.  Note: the CM motor primary power must be turned on for the cube mirror resolver to operate.

| Name | Length (bits) | Value | Description |
| --- | --- | --- | --- |
| Opcode | 16 | 0x0122 |  |
| Macro? | 1 | 0 = Execute 1 = Append to macro | Macro load bit |
| Length | 15 | 3 | Command length in 32-bit words |
| Mode | 8 | 0 = Off 1 = On | Mirror power off/on |
| Pad | 24 | 0 | Pad up to 32-bit boundary |
| Checksum | 32 |  | 32 bit XOR |

### CFI_MIR_STEP – Step Cube Mirror

Move cube mirror the indicated number of resolver counts.  Note: the CM motor primary power must be turned on for the cube mirror to move.

| Name | Length (bits) | Value | Description |
| --- | --- | --- | --- |
| Opcode | 16 | 0x0124 |  |
| Macro? | 1 | 0 = Execute 1 = Append to macro | Macro load bit |
| Length | 15 | 3 | Command length in 32-bit words |
| Counts | 16 | -32768 – 32767 | Mirror motion (resolver counts) |
| Pad | 16 | 0 | Pad up to 32-bit boundary |
| Checksum | 32 |  | 32 bit XOR |

### CFI_PWR_PRI – Control Primary Power

Turn primary power off or on to a selected subsystem.

| Name | Length (bits) | Value | Description |
| --- | --- | --- | --- |
| Opcode | 16 | 0x012b |  |
| Macro? | 1 | 0 = Execute 1 = Append to macro | Macro load bit |
| Length | 15 | 3 | Command length in 32-bit words |
| Mode | 8 | 0 = Off 1 = On | Primary power off/on |
| Board | 8 | 0 = Imager 1 = CM Motor 2 = FW Motor 255 = All | Power board |
| Pad | 16 | 0 | Pad up to 32-bit boundary |
| Checksum | 32 |  | 32 bit XOR |

### CFI_SAD_EXP – Set DSAD Image Exposure Time

Set DSAD image exposure time.

| Name | Length (bits) | Value | Description |
| --- | --- | --- | --- |
| Opcode | 16 | 0x0127 |  |
| Macro? | 1 | 0 = Execute 1 = Append to macro | Macro load bit |
| Length | 15 | 3 | Command length in 32-bit words |
| Time | 8 | 1 – 255 | Exposure time (36+8(n-1) seconds) |
| DSAD | 8 | 0 = Pinhole 1 = Lensed 255 = Both | DSAD |
| Spare | 16 |  |  |
| Checksum | 32 |  | 32 bit XOR |

### CFI_SAD_IMAGE – Collect DSAD Data for Downlink

Take a DSAD image, collect data, and downlink it.  Summary data is collected from the indicated DSAD and telemetered.  If requested, the associated raw image is also sent.

| Name | Length (bits) | Value | Description |
| --- | --- | --- | --- |
| Opcode | 16 | 0x0128 |  |
| Macro? | 1 | 0 = Execute 1 = Append to macro | Macro load bit |
| Length | 15 | 4 | Command length in 32-bit words |
| Spare | 32 |  |  |
| DSAD | 8 | 0 = Pinhole 1 = Lensed | DSAD |
| Image | 8 | 0 = No image 1 = Image | Send image too? |
| Spare | 16 |  |  |
| Checksum | 32 |  | 32 bit XOR |

# Support Processing

## 1553 Bus Management

CFI communicates with the C&DH system over a 1553B bus.  The DPU acts as a remote terminal (RT) with the active C&DH system acting as the bus controller (BC).  The traffic on the 1553B bus is periodic, repeating every one second major frame.  The major frame is divided into 25 minor frames, numbered 0 to 24.  Individual messages are distinguished by their transmit or receive subaddress.  CFI handles only the messages described in Reference 3.

## Inter-Integrated Circuit (I2C) Bus Management

A collection of environmental data is collected by the DPU.  There are analogs including voltages and currents read via one of the DPU’s two Inter-Integrated Circuit (I2C) buses.  A second I2C bus is used to collect temperatures.  The data collected is included in the status subpacket and image headers.  Each analog is also monitored when it is read (see below).  Collection and monitoring occur once per second.

## Alarms and Monitoring

Alarms report problems found by the DPU software.  Each alarm is described by an ID, two values, and a flag.  The ID identifies the problem that has occurred and the accompanying values offer additional information.  The flag indicates whether the alarm was caused by a transient or a persistent condition.  See Appendix 2 for a list of alarms.

The alarms are divided into two groups: one for reporting internal software problems and another for reporting out-of-limit conditions for monitored data.  Software problems are all reported as transient alarms.  When the problem occurs, the alarm is generated and the software recovers from the problem as best it can.

Values read from the I2C buses are monitored by the DPU The monitoring is event driven: a monitor cycle is performed on each item as it becomes available.  For example, each I2C analog is monitored when it is read.  The monitoring algorithm is described in more detail in Reference 3.

The monitored data is summarized in the following table.  The monitor class is encoded as S=shutdown, N=nop, and R=redo.  The reported alarm Ids are for low and high excursions; similarly there are low and high response macro Ids.

Table 17.  Monitored Data

| Source | Class | Alarm Ids Low / High | Macro Ids Low / High |
| --- | --- | --- | --- |
| CCD heater current | N | 128 | 192 | 0 | 2 |
| DPU current | S | 129 | 193 | 1 | 1 |
| DPU voltage | S | 130 | 194 | 1 | 1 |
| Imager converter current | S | 131 | 195 | 5 | 5 |
| HOP actuator #1 heater #1 current | N | 132 | 196 | 0 | 3 |
| HOP actuator #1 heater #2 current | N | 133 | 197 | 0 | 3 |
| Imager current | S | 134 | 198 | 5 | 5 |
| HOP actuator #2 heater #1 current | N | 135 | 199 | 0 | 3 |
| Imager voltage | S | 136 | 200 | 5 | 5 |
| HOP actuator #2 heater #2 current | N | 137 | 201 | 0 | 3 |
| FW motor primary current | N | 138 | 202 | 0 | 6 |
| FW motor current | N | 139 | 203 | 0 | 6 |
| FW motor converter current | N | 140 | 204 | 0 | 6 |
| FW 15V current | N | 141 | 205 | 0 | 6 |
| FW 15V voltage | S | 142 | 206 | 6 | 6 |
| CM motor primary current | N | 143 | 207 | 0 | 4 |
| CM motor current | N | 144 | 208 | 0 | 4 |
| CM motor converter current | N | 145 | 209 | 0 | 4 |
| CM 15V current | N | 146 | 210 | 0 | 4 |
| CM 15V voltage | S | 147 | 211 | 4 | 4 |
| CCD plate temperature #1 | N | 148 | 212 | 0 | 2 |
| CCD plate temperature #2 | N | 149 | 213 | 0 | 2 |
| Top bracket temperature | N | 150 | 214 | 0 | 0 |
| Bottom bracket temperature | N | 151 | 215 | 0 | 0 |
| M1/M2 tube base temperature | N | 152 | 216 | 0 | 0 |
| Bench fold cube temperature | N | 153 | 217 | 0 | 0 |
| Filter motor temperature | N | 154 | 218 | 0 | 0 |
| Cube motor temperature | N | 155 | 219 | 0 | 0 |
| Telescope tube bottom temperature | N | 156 | 220 | 0 | 0 |
| Telescope tube top temperature | N | 157 | 221 | 0 | 0 |
| Radiator temperature #2 | N | 158 | 222 | 0 | 2 |
| Radiator temperature #1 | N | 159 | 223 | 0 | 2 |
| Cover temperature #2 | N | 160 | 224 | 0 | 0 |
| Cover temperature #1 | N | 161 | 225 | 0 | 0 |

## Fault Avoidance and Recovery

Many of the DPU’s hardware control registers contain triple redundancy and voting logic for each bit.  The DPU software periodically rewrites these registers to correct single bit errors.

The DPU has a watchdog timer.  If the watchdog timer is not tickled from time to time, the processor is reset.  The watchdog timeout is 2.95 seconds.  The watchdog does not run until it has been enabled; once enabled, it can never by disabled except by processor reset, watchdog or otherwise.  The DPU monitors all periodic processes every second.  If they are all running, the watchdog is tickled.  Some aperiodic processes do not participate.

# DPU Boot ROM Program

The DPU boot ROM program operates as described in Reference 3.

# Appendix 1 - DPU Data Structures

Monitor limits consists of lower and upper limits of each monitored value; the lower limit is first followed by the upper limit.  Each limit is an eight bit unsigned integer; the monitored value is scaled accordingly before being monitored.

Table 18.  Monitor Limits Subpacket Format

| Name | Length (bits) | Value | Description |
| --- | --- | --- | --- |
| Time Tag | 32 | Unsigned integer | Spacecraft MET |
| Grouping | 2 | 11 = None | Grouping flags |
| Subpacket Id | 14 | 0x0005 | Identifies subpacket type |
| Length | 16 | 68 | Number of data bytes in subpacket |
| Ana DPU/1 | 2 * 8 | Unsigned integer | CCD heater current |
| Ana DPU/6 | 2 * 8 | Unsigned integer | DPU current |
| Ana DPU/7 | 2 * 8 | Unsigned integer | DPU voltage |
| Ana IM/0 | 2 * 8 | Unsigned integer | Imager converter current |
| Ana IM/1 | 2 * 8 | Unsigned integer | HOP actuator #1 heater #1 current |
| Ana IM/2 | 2 * 8 | Unsigned integer | HOP actuator #1 heater #2 current |
| Ana IM/3 | 2 * 8 | Unsigned integer | Imager current |
| Ana IM/4 | 2 * 8 | Unsigned integer | HOP actuator #2 heater #1 current |
| Ana IM/5 | 2 * 8 | Unsigned integer | Imager voltage |
| Ana IM/6 | 2 * 8 | Unsigned integer | HOP actuator #2 heater #2 current |
| Ana FW/0 | 2 * 8 | Unsigned integer | FW motor primary current |
| Ana FW/1 | 2 * 8 | Unsigned integer | FW motor current |
| Ana FW/2 | 2 * 8 | Unsigned integer | FW motor converter current |
| Ana FW/3 | 2 * 8 | Unsigned integer | FW 15V current |
| Ana FW/4 | 2 * 8 | Unsigned integer | FW 15V voltage |
| Ana CM/0 | 2 * 8 | Unsigned integer | CM motor primary current |
| Ana CM/1 | 2 * 8 | Unsigned integer | CM motor current |
| Ana CM/2 | 2 * 8 | Unsigned integer | CM motor converter current |
| Ana CM/3 | 2 * 8 | Unsigned integer | CM 15V current |
| Ana CM/4 | 2 * 8 | Unsigned integer | CM 15V voltage |
| Temp 0 | 2 * 8 | Unsigned integer | CCD plate temperature #1 |
| Temp 1 | 2 * 8 | Unsigned integer | CCD plate temperature #2 |
| Temp 2 | 2 * 8 | Unsigned integer | Top bracket temperature |
| Temp 3 | 2 * 8 | Unsigned integer | Bottom bracket temperature |
| Temp 4 | 2 * 8 | Unsigned integer | M1/M2 tube base temperature |
| Temp 5 | 2 * 8 | Unsigned integer | Bench fold cube temperature |
| Temp 6 | 2 * 8 | Unsigned integer | Filter motor temperature |
| Temp 7 | 2 * 8 | Unsigned integer | Cube motor temperature |
| Temp 8 | 2 * 8 | Unsigned integer | Telescope tube bottom temperature |
| Temp 9 | 2 * 8 | Unsigned integer | Telescope tube top temperature |
| Temp 10 | 2 * 8 | Unsigned integer | Radiator temperature #2 |
| Temp 11 | 2 * 8 | Unsigned integer | Radiator temperature #1 |
| Temp 12 | 2 * 8 | Unsigned integer | Cover temperature #2 |
| Temp 13 | 2 * 8 | Unsigned integer | Cover temperature #1 |

Table 19.  DPU Parameter Subpacket Format

| Name | Length (bits) | Value | Description |
| --- | --- | --- | --- |
| Time Tag | 32 | Unsigned integer | Spacecraft MET |
| Grouping | 2 | 11 = None | Grouping flags |
| Subpacket Id | 14 | 0x0006 | Identifies subpacket type |
| Length | 16 | 56 | Number of data bytes in subpacket |
| HOP On | 16 | Unsigned integer | HOP on time (seconds) |
| FW Power | 16 | Unsigned integer | FW motor power level |
| FW Mult | 16 | Signed integer | FW motor steps per resolver counts |
| FW Div | 16 | Unsigned integer |  |
| FW Pos | 10 * 16 | Unsigned integer | FW positions (resolver counts) |
| CM Power | 16 | Unsigned integer | CM motor power level |
| CM Mult | 16 | Signed integer | CM motor steps per resolver counts |
| CM Div | 16 | Unsigned integer |  |
| CM Pos | 4 * 16 | Unsigned integer | CM positions (resolver counts) |
| CM Dir | 16 | 0xffff = Increasing 0 = Decreasing | CM preferred direction of resolver counts |
| CM Divide | 16 | Unsigned integer | CM control I2C rate divider |
| Image Latch | 16 | Unsigned integer | Imager FPU latch recovery (seconds) |
| Spare | 4 * 16 |  |  |

# Appendix 2 - Alarm & Result Codes

Table 20.  Alarms

| ID | Description | Information |
| --- | --- | --- |
| 0 | Unused |  |
| 1 | Bad command checksum |  |
| 2 | Out of macro contexts | Macro Id |
| 128-191 | Monitored value is too low | Value and limit |
| 192-255 | Monitored value is too high | Value and limit |

Table 21.  Results

| Result Code (hex) | Description |
| --- | --- |
| 0x00 | No error, command executed |
| 0x01 | No error, command appended to macro |
| 0x02 | Unknown opcode |
| 0x03 | Bad argument |
| 0x04 | Cannot run macro; no contexts |
| 0x05 | Cannot be used outside of a macro |
| 0x06 | Macro compilation error |
| 0x07 | Macro not killed (not running?) |
| 0x08 | Bad EEPROM program |
| 0x09 | Cannot restore macros; bad checksum |
| 0x0a … 0x0f | reserved for common software |
| 0x10 | Cannot move cover, actuator disabled |

# Appendix 3 - Acronyms

Table 22.  Acronyms

| Acronym | Definition |
| --- | --- |
| BC | Bus Controller |
| CCD | Charge-Coupled Device |
| CCSDS | Consultative Committee for Space Data Systems |
| C&DH | Command & Data Handling |
| CFI | CONTOUR Forward Imager |
| CHEAP | CONTOUR Hardware Experimental Acquisition Package |
| CM | Cube Mirror |
| CONTOUR | COmet Nucleus TOUR |
| CRISP | CONTOUR Remote Imager/Spectrometer |
| DPU | Data Processing Unit |
| DSAD | Digital Solar Attitude Detector |
| EEPROM | Electrically Erasable Programmable ROM |
| FPGA | Field-Programmable Gate Array |
| FPU | Focal Plane Unit |
| FW | Filter Wheel |
| HOP | High Output Paraffin |
| I2C | Inter-Integrated Circuit |
| MET | Mission Elapsed Time |
| RAM | Random Access Memory |
| RIO | Remote I/O |
| ROM | Read Only Memory |
| RT | Remote Terminal |
| S/C | Spacecraft |
| TBD | To Be Determined |
| TRIO | Temperature RIO |
| XOR | eXclusive OR |