To:	Distribution

From:	John R. Hayes

Subject:	CRISP Software Requirements

References:	1.	7379-9303, “CONTOUR 1553 Bus Specification”, Version 1.05, September 20, 2001.

- CCSDS 102.0-B-4, “Consultative Committee for Space Data Systems Recommendation for Packet Telemetry”, November, 1995.

- Hayes, J.R., “CONTOUR Imager Common Software Requirements”, SRI-00-TBD, TBD.

John R. Hayes

Distribution:

J.J. Blanchette
J.D. Boldt
A.F. Bowman
S.J. Conard (JHU)
W.F. Dellinger
H. DeWitt (DeWitt Associates)
J.V. Finnigan
D.E. Fort
R.M. Furrow
A. Harch (Cornell)
A.J. Harris
J.R. Hayes
K.J. Heffernan
G.A. Heyler
K.C. Ho
M.E. Holdridge
D.C. Humm
N.R. Izenberg
S.E. Jaskulek
R.L. LeGrys
H. Malcom
W.L. Mitnick
S.L. Murchie
G.K. Oxton
E.J. Sheehi
T.S. Spisz
K. Strohbehn
D.S. Tillman
J.W. Warren
K.E. Whittenburg
D. Williams
R.L. Williams
SRI Files
Archives

Table of Contents:

1.	Introduction	1

1.1	Conventions	1

2.	Sensor Architecture	1

3.	Subsystems	2

3.1	Cover	2

3.2	Imager	2

3.3	Filter Wheel	6

3.4	Tracking Processor Unit (TPU)	6

3.4.1	Tracking	6

3.4.2	Mirror Control	7

3.5	Spectrometer	8

3.6	Heaters	10

4.	Telemetry Interface	11

4.1	Non-packetized Housekeeping	11

4.2	Packets	12

4.2.1	TPU Memory Dump	13

4.2.2	Subpackets	13

4.2.2.1	Status	14

4.2.2.2	TPU Memory Checksum	22

4.2.2.3	TPU Tracking Results	22

4.2.2.4	DPU Data Structures	23

4.2.2.5	TPU Data Structures	24

5.	Command Interface	24

5.1	Command and Macro Processing	24

5.2	Commands	25

5.2.1	CRS_CA_START – Start Closest Approach	25

5.2.2	CRS_COV_DEPLOY – Deploy the Cover	25

5.2.3	CRS_COV_LED – Control Cover LED Power	26

5.2.4	CRS_COV_MODE – Enable/Disable Cover Deployment	26

5.2.5	CRS_FLT_MOVE – Move Filter Wheel	26

5.2.6	CRS_FLT_PWR – Control Filter Wheel Power	27

5.2.7	CRS_FLT_STEP – Step Filter Wheel	27

5.2.8	CRS_HTR_MODE – Set Heater Control Mode	27

5.2.9	CRS_HTR_TMP – Set Heater Temperature	28

5.2.10	CRS_IMG_COMP_ALG – Select Image Compression Algorithm	28

5.2.11	CRS_IMG_COMP_MODE – Enable/Disable Image Compression	29

5.2.12	CRS_IMG_EXP – Set Image Exposure Time	29

5.2.13	CRS_IMG_FORMAT – Select Image Format	30

5.2.14	CRS_IMG_IMAGE – Collect Images for Downlink	30

5.2.15	CRS_IMG_PWR – Control Imager Power	30

5.2.16	CRS_IMG_REGION – Select Image Region of Interest	31

5.2.17	CRS_IMG_TRACK – Collect Tracking Images	31

5.2.18	CRS_MEM_STR_LOAD – Load Values into a Data Structure	31

5.2.19	CRS_MEM_STR_READ – Read a Data Structure	32

5.2.20	CRS_PWR_PRI – Control Primary Power	32

5.2.21	CRS_SPC_CAL_LEVEL – Set Spectrometer Calibrator Level	33

5.2.22	CRS_SPC_CAL_PWR – Control Spectrometer Calibrator Power	33

5.2.23	CRS_SPC_COOL – Control Spectrometer Cooler Power	33

5.2.24	CRS_SPC_FORMAT – Select Spectrometer Image Format	34

5.2.25	CRS_SPC_PWR – Control Spectrometer Power	34

5.2.26	CRS_SPC_RANGE – Select Spectrometer Image Range	35

5.2.27	CRS_SPC_RATE – Control Spectrometer Collection Rate	35

5.2.28	CRS_SPC_REGION – Select Spectrometer Image Region of Interest	35

5.2.29	CRS_SPC_SPECTRA – Collect Spectra	35

5.2.30	CRS_SPC_TMP – Enable/Disable Spectrometer Temperature Monitoring	36

5.2.31	CRS_TPU_AIM_ALG – Select Aim Algorithm	36

5.2.32	CRS_TPU_ATT_RESET – Reset Attitude Algorithm	36

5.2.33	CRS_TPU_IMG_REGION – Select Tracking Image Region of Interest	37

5.2.34	CRS_TPU_IMG_ZOOM – Select Tracking Image Zoom	37

5.2.35	CRS_TPU_MEM_CHECK – Check TPU Memory	37

5.2.36	CRS_TPU_MEM_COPY – Copy TPU Memory	38

5.2.37	CRS_TPU_MEM_LOAD – Load TPU Memory	38

5.2.38	CRS_TPU_MEM_READ – Read TPU Memory	39

5.2.39	CRS_TPU_MEM_READ_ABT – Abort TPU Memory Read	39

5.2.40	CRS_TPU_MEM_RUN – Run a TPU Program	39

5.2.41	CRS_TPU_MEM_STR_LOAD – Load Values into TPU Data Structure	39

5.2.42	CRS_TPU_MEM_STR_READ – Read TPU Data Structure	40

5.2.43	CRS_TPU_MIR_ANGLE – Set the Slew Mode Target Angle	41

5.2.44	CRS_TPU_MIR_HOME – Find Mirror Home Position	41

5.2.45	CRS_TPU_MIR_MODE – Set the Mirror Mode	42

5.2.46	CRS_TPU_MIR_PWR – Control Mirror Motor Power	42

5.2.47	CRS_TPU_MIR_SIDE – Select Mirror Side	42

5.2.48	CRS_TPU_MOTION – Enable/Disable S/C Motion Compensation	43

5.2.49	CRS_TPU_OFF_ANGLE – Set the Target Offset Angle	43

5.2.50	CRS_TPU_OFF_MODE – Enable/Disable Automatic Offset Adjustment	43

5.2.51	CRS_TPU_OFF_RATE – Set the Automatic Offset Rate	44

5.2.52	CRS_TPU_TEST – Enable/Disable Test Mode	44

5.2.53	CRS_TPU_TLM_FLUSH – Flush TPU Telemetry Subpackets	45

5.2.54	CRS_TPU_TLM_FLUSH_AUTO – Enable/Disable Automatic Flush	45

5.2.55	CRS_TPU_TRK_ALG – Select Tracking Algorithm	45

5.2.56	CRS_TPU_TRK_GOAL – Set Tracker Goal	46

5.2.57	CRS_TPU_TRK_LOOP – Enable/Disable Closed-Loop Tracking	46

5.2.58	CRS_TPU_TRK_TLM – Enable/Disable Tracking Telemetry	46

6.	Support Processing	47

6.1	1553 Bus Management	47

6.2	Inter-Integrated Circuit (I2C) Bus Management	48

6.3	Alarms and Monitoring	48

6.4	Fault Avoidance and Recovery	49

6.5	Closest Approach	50

7.	DPU Boot ROM Program	50

7.1.1	CRS_TPU_ROM_BOOT – Boot Default TPU Program	50

7.1.2	CRS_TPU_ROM_GO – Boot a Selected TPU Program	51

8.	TPU Boot ROM Program	51

Appendix 1 - DPU Data Structures	52

Appendix 2 - TPU Data Structures	53

Appendix 3 - Alarm & Result Codes	58

Appendix 4 - Acronyms	59

# Introduction

The COmet Nucleus TOUR (CONTOUR) spacecraft carries two imagers, the CONTOUR Remote Imager/Spectrometer (CRISP) and the CONTOUR Forward Imager (CFI).  This document describes the software features unique to the CRISP DPU.  Included are descriptions of sensor architecture, major subsystems, telemetry, commands, support processing, and the boot programs.

## Conventions

For all multi-bit or multi-byte numbers, the first byte sent has the most numerical significance; this is so-called “big-endian” format.  This convention applies to arguments in commands, data in telemetry, and messages over the 1553 bus.

# Sensor Architecture

The CRISP imagers consists of two imaging subsystems.  A two-dimensional optical imager collects images up to 1024 pixels square.  An infrared spectrometer/imager also collects two-dimensional images up to 256 pixels square; one dimension is spatial and the other is spectral.  The following figure shows a block diagram of the optical path, the major subsystems, and the computer.  The computer consists of two processors.  The Tracking Processor Unit (TPU) controls a scan mirror.  The TPU’s software keeps a target within the field of view.  A second processor, the Data Processing Unit (DPU) controls everything else.  The DPU controls the one-time deployable cover, the filter wheel in the optical image path, the cooler and calibration lamps of IR spectrometer, and orchestrates image collection and transmission to the spacecraft computer.

Figure 1. Sensor Block Diagram

# Subsystems

The major subsystems, including the cover, the imager, its filter wheel, the tracker and mirror, the spectrometer, and the heaters are discussed below.

## Cover

The CRISP optics are protected during launch by a one-time deployable cover.  The cover is deployed by High Output Paraffin (HOP) actuators.  There are two HOP actuators; each actuator has two heaters.  Any one of the four heaters should be sufficient to release the cover.  Each heater can be commanded on independently (CRS_COV_MODE and CRS_COV_DEPLOY).  Each HOP has a photodiode telltale that activates when the HOP is extended.  To read these telltales, power must be commanded (CRS_COV_LED) to a pair of Light-Emitting Diodes (LEDs).

## Imager

The visible imaging subsystem, from the CCD to the software, operates at a 1 Hz cadence.  A simplified timing diagram of the CCD is shown below.  The figure shows two seconds elapsing, i.e. two images being exposed.  CCD operations are synchronized to a 1 Hz system clock.  The internal CRISP 1 Hz clock lags the system-wide clock by ~7 ms.  Image exposures vary in length, but always end 20 ms before the next CRISP 1 Hz pulse.  Consequently, the maximum image exposure time is 980 ms.  The figure shows a normal exposure followed by a minimum length “scrub” exposure.  Scrub exposures are used to fill in time whenever no real image is needed.  This ensures that the CCD is read out every second.  The CCD is a frame-transfer device:  at the end of an exposure, the image is rapidly transferred into a buffer within the CCD.  Then the buffered image is read out of the CCD while the next image is being exposed.  The DPU adds an image header and trailer provided by the DPU software.  The read out of the entire image, including the trailer, must be complete before the end of the exposure.  The time between the end of exposure and the next CRISP 1 Hz pulse is used by the software to configure the image read out (e.g., load the header data) and setup the next exposure.

Figure 2. CCD Timing

Each image collected requires five processing steps.  Each step takes one second, but the process can be pipelined such that one image is taken every second.  The resulting five-stage pipeline is shown below.

Figure 3. Image Collection and Processing Pipeline

For purposes of command planning, only the first two image processing stages are relevant.  During setup, commands are executed to configure image collection in the following stage.  The following figure shows an example image taking sequence.  The commands that control the sequence are being issued from macros; macros execute at the beginning of each second.  A take image command (CRS_IMG_IMAGE) executed in t will cause the CCD to be exposed in t+1.  Similarly, commands to set the exposure time (CRS_IMG_EXP) and select the filter wheel (CRS_FLT_MOVE) that execute in t will take effect in t+1.  Filter wheel movements begin at the end of exposure; ensuring that the movement is complete before the next exposure is the responsibility of the macro and thus the macro author.

Figure 4. Example Image Sequence

The following figure relates the image on the CCD with the instrument’s coordinate system.  The numbers on the pixels in the figure indicate the order in which they are downlinked.  Each pixel is 12 bits.

Figure 5. Visible Image Readout

CRISP images come in four possible formats shown in the table below.  The format is selected by command (CRS_IMG_FORMAT).  The formats range from the full size of the CCD (1024x1024) down to smaller and smaller windows into the full image.  A command (CRS_IMG_REGION) selects the origin of the window.  In all of the formats, each line has an additional four dark calibration pixels and a line of temperatures at the end of the image.  Every data item in the image can be compressed from 12 bits to 8 bits if enabled by command (CRS_IMG_COMP_MODE).  The compression is done via table lookup in hardware; one of eight tables can be selected by command (CRS_IMG_COMP_ALG).  Any of these commands executed at time t affect the image exposed at time t+1.

Table 1.  Image Formats

| Mode | Pixels/line | Lines | Temperatures |
| --- | --- | --- | --- |
| 1024 x 1024 | 4 cal + 1024 pixels | 1024 | 4 cal + 1024 temps |
| 512 x 512 | 4 cal + 512 pixels | 512 | 4 cal + 512 temps |
| 256 x 256 | 4 cal + 256 pixels | 256 | 4 cal + 256 temps |
| 128 x 128 | 4 cal + 128 pixels | 128 | 4 cal + 128 temps |

Images are downlinked with a header describing the state of the instrument at the time the image was taken.  The header starts with the time at which the image was collected.  The header includes a snapshot of the current DPU status.  The header also includes the mirror position and velocity profile that was followed during this image’s exposure.  The header format is shown below:

Table 2. Image Header

| Name | Length (bits) | Value | Description |
| --- | --- | --- | --- |
| Time Tag | 32 | Unsigned integer | Spacecraft MET of exposure |
| Analog | 42 * 16 | See Table 13 | Analog status |
| Digital | 16 * 16 | See Table 14 | Digital status |
| Software | 88 * 8 | See Table 15 | Software status |
| Spare | 16 * 8 |  |  |
| Mirror Pos. | 100 * 32 |  | Mirror goal positions |
| Mirror Vel. | 100 * 32 |  | Mirror goal velocities |

Images are also downlinked with a trailer that contains the actual mirror motor command and status words over the exposure.  (This data is in a trailer instead of the header because not all of the data is available when the header is built.)  The trailer format is shown below:

Table 3. Image Trailer

| Name | Length (bits) | Value | Description |
| --- | --- | --- | --- |
| Mirror Status | 100 * 32 |  | Mirror motor status |
| Mirror Command | 100 * 32 |  | Mirror motor command |
| Spare | 224 * 8 |  |  |

The DPU software monitors the Focal Plane Unit’s (FPU) latch-up indicator.  If latch-up is detected, the DPU suspends FPU operations.  The length of the suspension is set by an uploadable parameter.

## Filter Wheel

The filter wheel is controlled by a stepping motor.  The motor phases are controlled directly by the DPU software to move the filter wheel.  The phase pattern can be adjusted by software to move the filter wheel forwards or backwards.  A resolver provides an absolute position reading of the wheel.

The filter move command (CRS_FLT_MOVE) uses the commanded filter number to look up an absolute goal position from a table, reads the current position from the resolver, and computes the number of steps and travel direction needed to arrive at the goal in the least amount of time.  The motor is then stepped to the desired goal.  The power to the resolver can be commanded on or off (CRS_FLT_PWR).  Alternatively, the filter step command (CRS_FLT_STEP) will move the filter wheel the commanded number of resolver counts forward or backward.  If the power to the resolver is turned off, further move commands will be dead-reckoned from the last resolver reading.  The filter wheel is characterized by several uploadable parameters including the motor power level, the scale factor between resolver counts and motor steps, the filter wheel positions, etc.  The filters are listed in the following table.

Table 4.  Filters

| Filter Number | Spectral Band (nm) |
| --- | --- |
| 1 | “clear” |
| 2 | 450 |
| 3 | 490 |
| 4 | 530 |
| 5 | 570 |
| 6 | 610 |
| 7 | 650 |
| 8 | 690 |
| 9 | 730 |
| 10 | 770 |

## Tracking Processor Unit (TPU)

The Tracking Processor Unit (TPU) is a computer attached to the DPU as a peripheral.  The TPU controls a mirror.  Four independent modes determine how the mirror is controlled.  Configurations range from completely manual control via ground command to fully automatic modes that keep the comet in the center of the field of view during an encounter.  The different modes are discussed below.

### Tracking

The TPU can track either fixed or moving targets.  An alpha-beta tracker is used for fixed targets such as stars used as calibration sources.  A Kalman filter is used to track moving targets such as a comet.  Which tracking algorithm to use is selected by command (CRS_TPU_TRK_ALG).  Each tracking algorithm can be run open-loop or closed-loop.  Images are selectively forwarded to the TPU at a commandable rate (CRS_IMG_TRACK); if closed-loop tracking is enabled, TPU software finds the comet in the image and incorporates this information into the tracking calculation.  If closed-loop tracking is disabled or there is no image to process, the last solution is propagated.  Closed-loop tracking can be enabled or disabled by command (CRS_TPU_TRK_LOOP).

The raw 1024x1024 image is reduced to a 128x128 format for image processing.  The origin or a window in the raw image and the number of pixels to rebin can be commanded (CRS_TPU_IMG_REGION and CRS_TPU_IMG_ZOOM).  The image processing algorithm used to find the comet is also selected by command (CRS_TPU_AIM_ALG).

The tracker tries to place the target at a commandable location on the CCD (CRS_TPU_TRK_GOAL).  The tracker also produces a target angle, angular rate, and a roll; the roll is sent to the G&C system and the angle and rate can be used to compute a mirror scan profile to follow the comet.  The tracker also produces an estimate of the time to closest approach (CA) and the miss distance between the spacecraft and the comet.

The TPU computes an estimate of the spacecraft attitude; the attitude when the image was taken is used by the Kalman filter.  The G&C system sends the current MIMU gyroscope angles to the TPU 100 times per second.  The TPU integrates the angles into its current attitude estimate.  At the start of every second, the TPU sends its idea of the current attitude along with the roll correction and the time to closest approach back to the G&C system.  At the end of the second, the G&C sends a correction to CRISP’s attitude estimate and the spacecraft’s commanded attitude.  All of these exchanges go through the DPU and over the 1553 bus.

### Mirror Control

The mirror controller can be commanded (CRS_TPU_MIR_MODE) into several modes.  Every second, the TPU computes a table of 100 mirror positions and rates.  The table will be used over the following second to update the mirror motor every 10 ms.  When the mirror mode is off, the mirror motor is not driven.  In hold mode, the mirror is held at the current position.  In slew mode, the mirror is held at a commanded angle (CRS_TPU_MIR_ANGLE).  In scan mode, the mirror follows the angle and angular rate computed by the tracker; the table is computed such that the mirror follows the comet motion, but uses a constant rate during image exposure.  There is also a command to control which side of the mirror to use (CRS_TPU_MIR_SIDE).  The selected side is incorporated into the table computed for slew or scan modes.  Finally, there is a command to initialize the mirror (CRS_TPU_MIR_HOME).

There is an additional mode that allows the mirror to be offset by a commanded angle (CRS_TPU_OFF_ANGLE).  This angle is added to any angle computed by the tracker or commanded to the slew mode mirror (CRS_TPU_MIR_ANGLE).  The offset angle can also be automatically adjusted (CRS_TPU_OFF_MODE) at a commandable rate (CRS_TPU_OFF_RATE).  If automatic adjustment is enabled, the offset angle is modified every second.  The adjustment proceeds continuously until it is disabled; re-enabling adjustment causes the offset to pick up where it left off.  Alternatively, the adjustment can be stopped by setting a zero rate.  Or, setting a negative rate will send the offset moving in the opposite direction.

The commands that set mirror angles, e.g. CRS_TPU_MIR_ANGLE, identify the angle from the S/C +Z axis (and usually the velocity vector) to the target (see following figure).  An angle of 0º indicates a target dead ahead, an angle of 90º indicates a target perpendicularly to the right of the spacecraft, etc.  Valid line-of-sight target angles range from –180º to 180º; the mirror will be positioned appropriately even if the spacecraft blocks the view.  The actual mirror shaft angle will be computed from the target angle and the currently commanded mirror side.  In the figure the shaft angle shown at 135º uses mirror side A to direct a target at 0º into the telescope.  Mirror shaft angles are constrained to keep side A of the mirror out of the dust as the spacecraft flies by the comet.  The extent of the dust keep-out zone is defined by uploadable parameters.

Figure 6. Mirror Angles

## Spectrometer

The imaging spectrometer subsystem operates at a commandable rate.  The rate can be commanded (CRS_SPC_RATE) to be 1, 2, 3, 4, or 5 Hz.  The exposure time is dictated by the rate; see the following table.  Unlike the imager CCD, the spectrometer detector is not a frame-transfer device.  The detector is exposed continuously and readouts must be done while exposing.  The software implication of this is that changing the spectrometer rate will cause the exposure time of one image to vary through the image; in other words, some pixels of the image will be exposed for the old exposure time and some will be exposed for the new exposure time.  The spectrometer is read at the commanded rate, even if no spectra are being collected, thus continually scrubbing the detector.  Spectra can be read for a commanded number of seconds (CRS_SPC_SPECTRA).

Table 5.  Spectrometer Exposure Times

| Rate | Exposure Time |
| --- | --- |
| 1 Hz | 999.1 ms |
| 2 Hz | 499.1 ms |
| 3 Hz | 332.4 ms |
| 4 Hz | 249.1 ms |
| 5 Hz | 199.1 ms |

A simplified timing diagram of the last two frames at the highest spectrometer rate (i.e. 5 Hz) is shown below.  The spectrometer rate clock is synchronized to a 1 Hz system clock.  The internal CRISP 1 Hz clock lags the system-wide clock by ~7 ms.  The DPU generates frames pulses at the commanded rate.  A frame pulse triggers image readout.  The DPU adds an image header provided by the DPU software.  The read out of the entire image, including the header, must be complete before the next frame pulse.  The time between the end of the read out and the next frame pulse is used by the software to configure the next image read out (e.g., load the header data).

Figure 7. Spectrometer Timing

Two infra-red (IR) lamps are available for testing the spectrometer.  Each lamp can be commanded off or on independently (CRS_SPC_CAL_PWR) and commanded to 256 brightness levels (CRS_SPC_CAL_LEVEL).  The lamps are only partially redundant in that a single lamp does not illuminate the entire detector.  Due to self-heating, there are some constraints in how the lamps can be used.  The software implements the following safety rules:

- Only one lamp may be on at a time.

- A lamp may be on for no more than 1 minute.

- After a lamp is turned off, the lamp must be off for for at least 1 minute before the other lamp is turned on.

- After a lamp is turned off, both lamps must be off for at least 10 minutes before the same lamp is turned back on.

(Note: the times are all uploadable parameters.)

To operate properly, the IR detector must be cooled.  There is a Stirling cooler that can be commanded (CRS_SPC_COOL) off or to two different low temperature setpoints.  The IR detector does not operate until it is powered (CRS_SPC_PWR).  The software will not apply the power until the cooler has been on for a time set by an uploadable parameter.

There are several temperature sensors in the spectrometer’s FPU.  Reading these temperatures can be enabled or disabled by command (CRS_SPC_TMP).  It my be necessary to disable them in the event that reading these temperatures introduces noise into the spectra.

The IR detector is divided into four quadrants.  The four quadrants are read out concurrently and merged.  Consequently, the image is not downlinked in a typical rasterized pattern.  Instead pixels from each quadrant are interspersed as shown in the following figure.  The numbers on the pixels in the figure indicate the order in which they are downlinked.  Note that the spectral dimension is read first.  Each raw pixel is 14 bits; a command (CRS_SPC_RANGE) selects a range of bits within the pixel to telemeter; the resulting pixel is 12 bits.  The DPU adds an offset of 64 to each 14-bit pixel; this will have to be removed in ground processing.  The value to subtract will be 64, 32, or 16 depending on the commanded range.

Figure 8. Spectrometer Image Readout

CRISP spectra come in four possible formats shown in the table below.  The format is selected by command (CRS_SPC_FORMAT).  The formats range from the full size of the detector (256x256) down to smaller and smaller windows into the full image.  Only the spatial dimension is reduced; the full spectral dimension is always sent.  A command (CRS_SPC_REGION) selects the origin of the window.

Table 6.  Spectrometer Image Formats

| Mode | Pixels/line | Lines |
| --- | --- | --- |
| 256 x 256 | 256 pixels | 256 |
| 128 x 256 | 256 pixels | 128 |
| 64 x 256 | 256 pixels | 64 |
| 32 x 256 | 256 pixels | 32 |

Spectrometer images are downlinked with a header describing the state of the instrument at the time the image was taken.  The header starts with a subheader that includes the time at which the image was collected.  The header also includes a snapshot of the current DPU status.  The header format is shown below:

Table 7.  Spectrometer Image Header

| Name | Length (bits) | Value | Description |
| --- | --- | --- | --- |
| Time Tag | 32 | Unsigned integer | Spacecraft MET of exposure |
| Analog | 42 * 16 | See Table 13 | Analog status |
| Digital | 16 * 16 | See Table 14 | Digital status |
| Software | 88 * 8 | See Table 15 | Software status |
| Spare | 48 * 8 |  |  |

## Heaters

The CRISP DPU controls the temperature of five zones of the instrument.  The heater in each zone may be commanded off, on, or controlled by software (CRS_HTR_MODE).  If a heater is being controlled by software, it uses the setpoint and hysteresis commanded for that zone (CRS_HTR_TMP).  Every second the zone’s temperature is compared against its limits.  If the temperature is too low, the heater will be turned on.  If the temperature is too high, the heater will be turned off.  The five zones and the temperature sensors used to control them are listed in the table below.

Table 8.  Heaters

| Zone Number | Zone | Sensor |
| --- | --- | --- |
| 0 | Star camera 1 | Star camera 1 temperature |
| 1 | Star camera 2 | Star camera 2 temperature |
| 2 | Diaphragm | Diaphragm temperature |
| 3 | Mirror motor | Mirror motor temperature |
| 4 | Bulk (upper housing) | Radiator temperature |

# Telemetry Interface

The spacecraft Command & Data Handling (C&DH) system collects telemetry from CRISP over the 1553 bus as non-packetized housekeeping and as CCSDS packets.

## Non-packetized Housekeeping

The C&DH system picks up a 16-byte non-packetized housekeeping record every second.  The contents can be incorporated into C&DH autonomy processing.  The C&DH system also assembles the data into a housekeeping packet.  The format of the non-packetized housekeeping record is shown below.

Table 9.  Non-Packetized Housekeeping Format

| Name | Length (bits) | Value | Description |
| --- | --- | --- | --- |
| Version | 8 | 0 = Boot >0 = Application | Software version |
| Alarm | 8 | See Table 37 | Latest alarm id |
| Alarm Type | 1 | 0 = Persistent 1 = Transient | Latest alarm type |
| Alarms | 7 | Unsigned integer | Count of alarms |
| Executed | 8 | Unsigned integer | Commands executed |
| Rejected | 8 | Unsigned integer | Commands rejected |
| Mac Exec | 8 | Unsigned integer | Macro commands executed |
| Mac Rej | 8 | Unsigned integer | Macro commands rejected |
| Spare | 8 |  |  |
| CA Mode | 1 | 0 = Good targeting 1 = Bad targeting | Closest approach mode |
| CA State | 3 | 0 = Idle 1 = Search 2 = Inbound imaging 3 = Closest approach | Closest approach processing state |
| CA Valid | 1 | 0 = Invalid 1 = Valid | Validity of CA time, miss distance, miss distance summary, and target angle |
| CA Distance Summary | 3 | 0 = Very near 1 = Near 2 = Nominal 3 = Far 4 = Very far 5 = Too far #1 6 = Too far #2 7 = Too far #3 | Miss distance summary for closest approach processing |
| CA Target Angle | 3 | 0 = Inbound 1 = Inbound imaging 2 = Closest approach 3 = Outbound imaging | Target angle for closest approach processing |
| Spare | 5 |  |  |
| CA Distance | 16 | Unsigned integer | Miss distance (km) |
| CA Time | 32 | Signed integer | Time to closest approach (seconds) |

## Packets

The C&DH system collects up to one packet from CRISP every second.  These packets are memory dump and subpacket packets as described in Reference 3.  In addition, CRISP can generate memory dump and subpacket packets from the TPU.  CRISP images and spectra are sent directly to the C&DH system for packetization.

Table 10.  Packet Types

| Product | Data Id (binary) | When Sent |
| --- | --- | --- |
| Memory Dump | 000 0000 | On demand |
| Subpacket | 000 0001 | As needed |
| Images | 000 0010 | Commandable interval |
| Spectra | 000 0011 | Commandable interval |
| TPU Memory Dump | 000 0100 | On demand |
| TPU Subpacket | 000 0101 | As needed |

### TPU Memory Dump

TPU memory dump packets consist of CONTOUR CCSDS headers, a dump start address, dump length, and dump data.  The TPU memory dump has an identical format to DPU memory dumps except that the data ids in the packet header differ.

### Subpackets

Instead of coercing imager data to fit into the fixed size CONTOUR packets, the imagers use variable-sized subpackets that “float” through fixed-size packets (see Reference 3).

The subpacket types produced by CRISP are listed in the table below.  Subpackets can be produced by the DPU or the TPU.  DPU subpackets are always placed in DPU subpacket packets and TPU subpackets are always placed in TPU subpacket packets.  Some of the subpackets are described in Reference 3.  The subpackets unique to CRISP are described below.

Table 11.  Subpacket Types

| Product | Subpacket Id (hex) | When Generated |
| --- | --- | --- |
| Boot Status | 0x0000 | Commandable interval |
| Status | 0x0001 | Commandable interval |
| Command Echo | 0x0002 | As needed |
| Alarm | 0x0003 | As needed |
| Memory Checksum | 0x0004 | On demand |
| Monitor Limits | 0x0005 | On demand |
| DPU Parameters | 0x0006 | On demand |
| TPU Alarm | 0x0010 | As needed |
| TPU Memory Checksum | 0x0011 | On demand |
| TPU Mirror Parameters | 0x0012 | On demand |
| TPU Aim Parameters | 0x0013 | On demand |
| TPU CA Parameters | 0x0014 | On demand |
| TPU Tracker Offset | 0x0015 | On demand |
| TPU Tracker Control | 0x0016 | On demand |
| TPU Tracker Target | 0x0017 | On demand |
| TPU Tracker EKF | 0x0018 | On demand |
| TPU Tracker Cheby #1 | 0x0019 | On demand |
| TPU Tracker Cheby #2 | 0x001a | On demand |
| TPU Tracker Cheby #3 | 0x001b | On demand |
| TPU Tracker Mirror | 0x001c | On demand |
| TPU Tracker Gate | 0x001d | On demand |
| TPU Tracker Align | 0x001e | On demand |
| TPU Tracking Results | 0x001f | Every second, if enabled |
| Flush | 0x3fff | As needed |

#### Status

The DPU generates a status subpacket periodically.  The rate is controlled by a command (see CRS_STAT_INT).  The subpacket consists of a subpacket header and status data; the status includes analog, digital, DPU software, and TPU software data.  The overall subpacket format is shown in the following table; the formats of the individual components are shown in the subsequent tables.

Table 12.  DPU Status Subpacket Format

| Name | Length (bits) | Value | Description |
| --- | --- | --- | --- |
| Time Tag | 32 | Unsigned integer | Spacecraft MET |
| Grouping | 2 | 11 = None | Grouping flags |
| Subpacket Id | 14 | 0x0001 | Identifies subpacket type |
| Length | 16 | 204 | Number of data bytes in subpacket |
| Analog | 42 * 16 | See Table 13 | Analog readings |
| Digital | 16 * 16 | See Table 14 | Digital configuration and feedback |
| Software | 88 * 8 | See Table 15 | Software configuration and status |

Table 13.  Analog Status

| Name | Length (bits) | Value | Description |
| --- | --- | --- | --- |
| Ana DPU/0 | 16 | -8192 – 8191 | Mirror motor current |
| Ana DPU/1 | 16 | -8192 – 8191 | Star camera #1 heater current |
| Ana DPU/2 | 16 | -8192 – 8191 | Star camera #2 heater current |
| Ana DPU/3 | 16 | -8192 – 8191 | Diaphragm heater current |
| Ana DPU/4 | 16 | -8192 – 8191 | Mirror motor heater current |
| Ana DPU/5 | 16 | -8192 – 8191 | Bulk heater current |
| Ana DPU/6 | 16 | -8192 – 8191 | DPU current |
| Ana DPU/7 | 16 | -8192 – 8191 | DPU voltage |
| Ana IM/0 | 16 | -8192 – 8191 | Imager converter current |
| Ana IM/1 | 16 | -8192 – 8191 | HOP actuator #1 heater #1 current |
| Ana IM/2 | 16 | -8192 – 8191 | HOP actuator #1 heater #2 current |
| Ana IM/3 | 16 | -8192 – 8191 | Imager current |
| Ana IM/4 | 16 | -8192 – 8191 | HOP actuator #2 heater #1 current |
| Ana IM/5 | 16 | -8192 – 8191 | Imager voltage |
| Ana IM/6 | 16 | -8192 – 8191 | HOP actuator #2 heater #2 current |
| Ana SP/0 | 16 | -8192 – 8191 | Spectrometer primary current |
| Ana SP/1 | 16 | -8192 – 8191 | Spectrometer converter current |
| Ana SP/2 | 16 | -8192 – 8191 | Cooler converter current |
| Ana SP/3 | 16 | -8192 – 8191 | Cooler current |
| Ana SP/4 | 16 | -8192 – 8191 | Spectrometer current |
| Ana SP/5 | 16 | -8192 – 8191 | Cooler voltage |
| Ana SP/6 | 16 | -8192 – 8191 | Spectrometer voltage |
| Ana FW/0 | 16 | -8192 – 8191 | FW motor primary current |
| Ana FW/1 | 16 | -8192 – 8191 | FW motor current |
| Ana FW/2 | 16 | -8192 – 8191 | FW motor converter current |
| Ana FW/3 | 16 | -8192 – 8191 | FW 15V current |
| Ana FW/4 | 16 | -8192 – 8191 | FW 15V voltage |
| Temp 0 | 16 | 0 – 1023 | Spectrometer housing temperature |
| Temp 1 | 16 | 0 – 1023 | Mirror motor elec. temperature |
| Temp 2 | 16 | 0 – 1023 | Cryo cooler temperature |
| Temp 3 | 16 | 0 – 1023 | Fold mirror temperature |
| Temp 4 | 16 | 0 – 1023 | Housing rear temperature |
| Temp 5 | 16 | 0 – 1023 | M2 temperature |
| Temp 6 | 16 | 0 – 1023 | M1 temperature |
| Temp 7 | 16 | 0 – 1023 | Diaphragm temperature |
| Temp 8 | 16 | 0 – 1023 | Mirror motor temperature |
| Temp 9 | 16 | 0 – 1023 | Star camera #2 temperature |
| Temp 10 | 16 | 0 – 1023 | Star camera #1 temperature |
| Temp 11 | 16 | 0 – 1023 | HOPS actuator #1 temperature |
| Temp 12 | 16 | 0 – 1023 | Housing top temperature |
| Temp 13 | 16 | 0 – 1023 | Radiator temperature |
| Temp 14 | 16 | 0 – 1023 | Deck temperature |

Table 14.  Digital Status

| Name | Length (bits) | Value | Description |
| --- | --- | --- | --- |
| Spare | 14 |  |  |
| Telltale 2 | 1 | 0 = Extended (deployed) 1 = Not extended | HOP #2 telltale |
| Telltale 1 | 1 | 0 = Extended (deployed) 1 = Not extended | HOP #1 telltale |
| FW Position | 16 | Unsigned integer | Filter wheel position |
| Mirror Power | 1 | 0 = Off 1 = On | Tracking mirror power |
| Star Camera 1 Heater | 1 | 0 = Off 1 = On | Star camera #1 heater power |
| Star Camera 2 Heater | 1 | 0 = Off 1 = On | Star camera #2 heater power |
| Diaphragm Heater | 1 | 0 = Off 1 = On | Diaphragm heater power |
| Mirror Heater | 1 | 0 = Off 1 = On | Mirror motor heater power |
| Bulk Heater | 1 | 0 = Off 1 = On | Bulk (upper housing) heater power |
| Spare | 2 |  |  |
| IM Primary | 1 | 0 = Off 1 = On | Imager board primary power |
| HOP #2/2 | 1 | 0 = Off 1 = On | HOP actuator #2 heater #2 power |
| HOP #2/1 | 1 | 0 = Off 1 = On | HOP actuator #2 heater #1 power |
| HOP #1/2 | 1 | 0 = Off 1 = On | HOP actuator #1 heater #2 power |
| HOP #1/1 | 1 | 0 = Off 1 = On | HOP actuator #1 heater #1 power |
| Spare | 2 |  |  |
| IM Power | 1 | 0 = Off 1 = On | Imager focal plane power |
| Spare | 6 |  |  |
| IM LED 2 | 1 | 0 = Off 1 = On | Imager cover LED #2 |
| IM LED 1 | 1 | 0 = Off 1 = On | Imager cover LED #1 |
| SP Primary | 1 | 0 = Off 1 = On | Spectrometer board primary power |
| Spare | 4 |  |  |
| Cooler Hi/Lo | 1 | 0 = Low 1 = High | Spectrometer cooler temperature |
| Cooler Power | 1 | 0 = Off 1 = On | Spectrometer cooler power |
| SP Power | 1 | 0 = Off 1 = On | Spectrometer focal plane power |
| FW Primary | 1 | 0 = Off 1 = On | FW motor board primary power |
| FW Resolver | 1 | 0 = Off 1 = On | FW resolver power |
| Spare | 6 |  |  |
| Spare | 1 |  |  |
| FW Level | 3 | Unsigned integer | FW motor power level |
| Spare | 1 |  |  |
| FW Motor | 1 | 0 = Off 1 = On | FW motor current enable |
| FW Phase | 2 | Unsigned integer | FW motor phase drive |
| Spare | 2 |  |  |
| Compress | 1 | 0 = No compression 1 = Compress | Image compression enable |
| Comp. Type | 3 | 0 = High-range identity 1 = Low-end identity 2 = Mid-range identity 3 = DN-weighted SNR 4 = Inverse root 2 power 5 = Linear 6 = SNR proportional 7 = Root 2 power | Image compression type |
| Image X | 10 | Unsigned integer | Image X origin |
| Spare | 3 |  |  |
| Image Downlink | 1 | 0 = No downlink 1 = Downlink | Image downlink enable |
| Image Format | 2 | 0 = 1024 x 1024 1 = 512 x 512 2 = 256 x 256 3 = 128 x 128 | Image format |
| Image Y | 10 | Unsigned integer | Image Y origin |
| Spare | 3 |  |  |
| Image Start | 13 | Unsigned integer | Image exposure start time |
| Imager Status | 16 |  | Imager FPU status word |
| Spare | 5 |  |  |
| Cal Lamp #2 | 1 | 0 = Off 1 = On | IR calibration lamp #2 |
| Cal Lamp #1 | 1 | 0 = Off 1 = On | IR calibration lamp #1 |
| IR Temp. Monitor | 1 | 0 = Off 1 = On | Temperature monitor enable/disable |
| Cal Level | 8 | Unsigned integer | IR calibration level for both lamps |
| Spect. Range | 2 | 0 = Bits 12..1 1 = Bits 13..2 2 = Bits 11..0 | Spectrometer pixels bits telemetered |
| Spare | 1 |  |  |
| Spect. Downlink | 1 | 0 = No downlink 1 = Downlink | Spectrometer downlink enable |
| Spect. Format | 2 | 0 = 256 x 256 1 = 128 x 256 2 = 64 x 256 3 = 32 x 256 | Spectrometer format |
| Spare | 2 |  |  |
| Spect. Origin | 8 | Unsigned integer | Spectrometer origin in spatial dimension |
| Spect. Status | 16 |  | Spectrometer FPU status word |
| Spect. FPU Temp. #1 | 16 | Unsigned integer | Spectrometer FPU temperature #1 |
| Spect. FPU Temp. #2 | 16 | Unsigned integer | Spectrometer FPU temperature #2 |
| Spect. FPU Board Temp. | 16 | Unsigned integer | Spectrometer FPU board temperature |
| Spare | 16 |  |  |

Table 15. Software Status

| Name | Length (bits) | Value | Description |
| --- | --- | --- | --- |
| Image Time | 16 | 0 – 65534: Remaining 65535: Forever | Image downlink time remaining (seconds) |
| Image Interval | 16 | Unsigned integer | Interval between downlink images (seconds) |
| Track Time | 16 | 0 – 65534: Remaining 65535: Forever | Tracking image collection time remaining (seconds) |
| Track Interval | 16 | Unsigned integer | Interval between tracking images (seconds) |
| Spect. Time | 16 | 0 – 65534: Remaining 65535: Forever | Spectra collection time remaining (seconds) |
| Heater #0 Setpoint | 16 | Unsigned integer | Heater #0 setpoint |
| Heater #1 Setpoint | 16 | Unsigned integer | Heater #1 setpoint |
| Heater #2 Setpoint | 16 | Unsigned integer | Heater #2 setpoint |
| Heater #3 Setpoint | 16 | Unsigned integer | Heater #3 setpoint |
| Heater #4 Setpoint | 16 | Unsigned integer | Heater #4 setpoint |
| Heater #0 Hysteresis | 8 | Unsigned integer | Heater #0 hysteresis |
| Heater #1 Hysteresis | 8 | Unsigned integer | Heater #1 hysteresis |
| Heater #2 Hysteresis | 8 | Unsigned integer | Heater #2 hysteresis |
| Heater #3 Hysteresis | 8 | Unsigned integer | Heater #3 hysteresis |
| Heater #4 Hysteresis | 8 | Unsigned integer | Heater #4 hysteresis |
| Heater #0 Mode | 2 | 0 = Off 1 = On 2 = Software control | Heater #0 control mode |
| Heater #1 Mode | 2 | 0 = Off 1 = On 2 = Software control | Heater #1 control mode |
| Heater #2 Mode | 2 | 0 = Off 1 = On 2 = Software control | Heater #2 control mode |
| Heater #3 Mode | 2 | 0 = Off 1 = On 2 = Software control | Heater #3 control mode |
| Heater #4 Mode | 2 | 0 = Off 1 = On 2 = Software control | Heater #4 control mode |
| Spect. Rate | 3 | 1 – 5 | Spectrometer rate (Hz) |
| Cover Mode | 1 | 0 = Disable deployment 1 = Enable deployment | Cover deployment mode |
| Spare | 2 |  |  |
| CA Mode | 1 | 0 = Good targeting 1 = Bad targeting | Closest approach mode |
| CA State | 3 | 0 = Idle 1 = Search 2 = Inbound imaging 3 = Closest approach | Closest approach processing state |
| Filter | 4 | 1 – 10 | Commanded filter number |
| Macro Blocks | 16 | Unsigned integer | Number of macro blocks free |
| DPU Version | 8 | Unsigned integer | DPU software version number |
| Alarm Id | 8 | See Table 37 | Latest alarm Id |
| Alarm Type | 1 | 0 = Persistent 1 = Transient | Latest alarm type |
| Alarm Count | 7 | Unsigned integer | Count of alarms |
| Cmd Exec | 8 | Unsigned integer | Commands executed |
| Cmd Reject | 8 | Unsigned integer | Commands rejected |
| Mac Exec | 8 | Unsigned integer | Macro commands executed |
| Mac Reject | 8 | Unsigned integer | Macro commands rejected |
| Status Int. | 8 | 1 – 255 (0 = Off) | Status interval (seconds) |
| Macro Id | 8 | Unsigned integer | Id of most recent macro executed |
| Auto Flush | 1 | 0 = Disable 1 = Enable | Automatic telemetry flush |
| Macro Learn | 1 | 0 = Not learning 1 = Learning | Macro learn mode |
| Monitor Response | 1 | 0 = Disable 1 = Enable | Monitor response |
| Spare | 5 |  |  |
| Mirror Pos. | 32 |  | Mirror motor position |
| Spare | 32 |  |  |
| Tracker X | 32 | IEEE-754 single | X goal position (pixels) |
| Tracker Y | 32 | IEEE-754 single | Y goal position (pixels) |
| Slew Angle | 32 | IEEE-754 single | Slew target angle (degrees) |
| Offset Angle | 32 | IEEE-754 single | Target offset angle (degrees) |
| Offset Rate | 32 | IEEE-754 single | Target offset rate (degrees/s) |
| CA Time | 32 | Signed integer | Time to closest approach (seconds) |
| CA Distance | 16 | Unsigned integer | Miss distance (km) of closest approach |
| CA Valid | 1 | 0 = Invalid 1 = Valid | Validity of CA time, miss distance, miss distance summary, and target angle |
| CA Distance Summary | 3 | 0 = Very near 1 = Near 2 = Nominal 3 = Far 4 = Very far 5 = Too far #1 6 = Too far #2 7 = Too far #3 | Miss distance summary for closest approach processing |
| CA Target Angle | 3 | 0 = Inbound 1 = Inbound imaging 2 = Closest approach 3 = Outbound imaging | Target angle for closest approach processing |
| Spare | 9 |  |  |
| Tracking Algorithm | 2 | 0 = Off 1 = Fixed target 2 = Moving target | Tracking algorithm |
| Tracking Loop | 1 | 0 = Disable 1 = Enable | Closed-loop Tracking |
| Aim Algorithm | 1 | 0 = Comet 1 = Brightest object | Aim algorithm |
| Offset Adjustment | 1 | 0 = Disable 1 = Enable | Mirror offset adjustment |
| Mirror Mode | 3 | 0 = Off 1 = Hold 2 = Slew 3 = Scan 4 = Home | Mirror control mode (commanded) |
| Mirror Side | 1 | 0 = A (science) 1 = B (tracking) | Mirror side |
| Spare | 1 |  |  |
| Auto Flush TPU | 1 | 0 = Disable 1 = Enable | Automatic telemetry flush in TPU |
| TPU Test Mode | 1 | 0 = Disable 1 = Enable | TPU test mode |
| TPU Tracking Tlm | 1 | 0 = Disable 1 = Enable | TPU tracking telemetry production |
| Spare | 3 |  |  |
| TPU Version | 8 | Unsigned integer | TPU software version number |
| Spare | 8 |  |  |
| Actual Mirror Mode | 8 | 0 = Off 1 = Hold 2 = Slew 3 = Scan 4 = Home 5 = Search 6 = Found 7 = Verify | Mirror control mode (actual) |
| Spare | 24 |  |  |
| Spare | 10 |  |  |
| Track Image Zoom | 2 | 0 = 8x8 rebin 1 = 4x4 rebin 2 = 2x2 rebin 3 = 1x1 rebin | Tracking image zoom |
| Track Img X | 10 | 0 – 1023 | Tracking image X region (pixels) |
| Track Img Y | 10 | 0 – 1023 | Tracking image Y region (pixels) |

#### TPU Memory Checksum

TPU memory checksum subpackets consist of a subpacket header and checksum data.  The checksum is the 32-bit two’s complement sum of the indicated memory region.

Table 16.  TPU Memory Checksum Subpacket Format

| Name | Length (bits) | Value | Description |
| --- | --- | --- | --- |
| Time Tag | 32 | Unsigned integer | Spacecraft MET |
| Grouping | 2 | 11 = None | Grouping flags |
| Subpacket Id | 14 | 0x0011 | Identifies subpacket type |
| Length | 16 | 12 | Number of data bytes in subpacket |
| Address | 32 | Unsigned integer | Address of region checked |
| Length | 32 | Unsigned integer | Length of region checked in bytes |
| Checksum | 32 | Unsigned integer | Computed checksum |

#### TPU Tracking Results

The results of the TPU’s tracking algorithm can be telemetered in a subpacket.  TPU tracking results subpackets consist of a subpacket header and tracking data.  If enabled by command (CRS_TPU_TRK_TLM) the subpacket will be sent every second.

Table 17.  TPU Tracking Results Subpacket Format

| Name | Length (bits) | Value | Description |
| --- | --- | --- | --- |
| Time Tag | 32 | Unsigned integer | Spacecraft MET |
| Grouping | 2 | 11 = None | Grouping flags |
| Subpacket Id | 14 | 0x001f | Identifies subpacket type |
| Length | 16 | 112 | Number of data bytes in subpacket |
| Time | 64 | IEEE-754 double | Time tracking done (TDT) |
| Attitude | 4 * 32 | IEEE-754 single | Estimated CRISP attitude |
| Correction | 4 * 32 | IEEE-754 single | Attitude correction from G&C |
| Centroid | 2 * 32 | IEEE-754 single | Centroid (pixels) |
| Mirror Pos | 32 | IEEE-754 single | Mirror position (degrees) |
| Mirror Cmd | 2 * 32 | IEEE-754 single | Mirror command (degrees, d/s) |
| CA | 32 | IEEE-754 single | Time to closest approach (seconds) |
| Miss | 32 | IEEE-754 single | Miss distance (km) |
| Roll Z | 32 | IEEE-754 single | Delta roll z component |
| Gate | 2 * 32 | IEEE-754 single | Gate location (pixels) |
| Trajectory | 6 * 32 | IEEE-754 single | Filter trajectory |
| Proc Time | 16 |  | Processing time (ms) |
| Filter Flag | 1 | 0 = Invalid 1 = Valid | Filter valid |
| Used Flag | 1 | 0 = Invalid 1 = Valid | Used |
| Gate Flag | 1 | 0 = Invalid 1 = Valid | Gate initialized |
| Z Flag | 1 | 0 = Invalid 1 = Valid | Z stable |
| Attitude Flag | 1 | 0 = Invalid 1 = Valid | Attitude valid |
| Tracking Loop | 1 | 0 = Disable 1 = Enable | Closed loop track enable |
| Centroid Flag | 1 | 0 = Invalid 1 = Valid | Centroid valid |
| Correction Flag | 1 | 0 = Invalid 1 = Valid | Attitude correction valid |
| Mirror Flag | 1 | 0 = Invalid 1 = Valid | Mirror position valid |
| Spare | 7 |  |  |
| Spare | 4 * 8 |  |  |

#### DPU Data Structures

The DPU makes several of its internal data structures available for modification or downlink.  The data structures can be modified by command (CRS_MEM_STR_LOAD).  The current data structures can also be downlinked by command (CRS_MEM_STR_READ).  The data structures are described in Appendix 1.

#### TPU Data Structures

The TPU makes several of its internal data structures available for modification or downlink.  The data structures can be modified by command (CRS_TPU_MEM_STR_LOAD).  The current data structures can also be downlinked by command (CRS_TPU_MEM_STR_READ).  The data structures are described in Appendix 2.

# Command Interface

The DPU receives and processes CCSDS telecommand packets containing one or more commands.  The format of the telecommand packet and constituent commands is described in Reference 3.

## Command and Macro Processing

Most commands are executed as soon as they are received; exceptions are noted in the individual command descriptions.  Each command is echoed after it is executed by the DPU.  A command echo subpacket containing the opcode and some arguments along with a code summarizing the command’s result is downlinked.  Most TPU commands are not executed by the DPU but are forwarded to the TPU.  The DPU echoes the command after it has been executed by the TPU.

Some default macros are available as soon as the DPU is started.  Most of these macros are one or two commands long and are used by the monitoring subsystem to respond to out of limit conditions.  A default macro can be replaced with a new macro via CRS_MAC_DEF and CRS_MAC_ENDEF.  The default macros are shown in the following table.

Table 18.  Default Macros

| ID | Action | Commands |
| --- | --- | --- |
| 0 | No action | CRS_CMD_NULL |
| 1 | Shutdown | CRS_SPC_PWR OFF CRS_SPC_COOL OFF CRS_IMG_PWR OFF CRS_TPU_MIR_HOME CRS_FLT_MOVE CLEAR CRS_MAC_DELAY 10 CRS_FLT_PWR OFF CRS_MAC_DELAY 10 CRS_TPU_MIR_PWR OFF CRS_PWR_PRI OFF ALL CRS_HTR_MODE OFF ALL |
| 2 | Imaging – Very Near | CRS_CMD_NULL |
| 3 | Imaging – Near | CRS_CMD_NULL |
| 4 | Imaging – Nominal | CRS_CMD_NULL |
| 5 | Imaging – Far | CRS_CMD_NULL |
| 6 | Imaging – Very Far | CRS_CMD_NULL |
| 7 | Imaging – “Bad” Targeting #1 | CRS_CMD_NULL |
| 8 | Imaging – “Bad” Targeting #2 | CRS_CMD_NULL |
| 9 | Imaging – “Bad” Targeting #3 | CRS_CMD_NULL |
| 10 | Closest Approach | CRS_CMD_NULL |
| 11 | Post Encounter | CRS_CMD_NULL |
| 12 | Stop Macro Processing | CRS_MON_CNTRL DISABLE CRS_CA_RESET CRS_MEM_RUN kill all macros |
| 13 | Heaters Off | CRS_HTR_MODE OFF ALL |
| 14 | Cover HOPS Off | CRS_COV_DEPLOY OFF 1/1 CRS_COV_DEPLOY OFF 1/2 CRS_COV_DEPLOY OFF 2/1 CRS_COV_DEPLOY OFF 2/2 CRS_COV_MODE DISABLE |
| 15 | Filter Wheel Off | CRS_FLT_PWR OFF CRS_PWR_PRI OFF FW |
| 16 | Imager Off | CRS_IMG_PWR OFF CRS_PWR_PRI OFF IM |
| 17 | Spectrometer Off | CRS_SPC_PWR OFF CRS_SPC_COOL OFF CRS_PWR_PRI OFF SP |
| 18 | Tracking Mirror Off | CRS_TPU_MIR_PWR OFF |
| 19 – 63 | Reserved |  |
| 64 – 255 | Reserved for mission operations |  |

## Commands

The CRISP and CFI common commands are described in Reference 3.  CRISP-specific commands are defined below.

### CRS_CA_RESET – Reset Closest Approach

Reset closest approach processing logic.

| Name | Length (bits) | Value | Description |
| --- | --- | --- | --- |
| Opcode | 16 | 0x0174 |  |
| Macro? | 1 | 0 = Execute 1 = Append to macro | Macro load bit |
| Length | 15 | 2 | Command length in 32-bit words |
| Checksum | 32 |  | 32 bit XOR |

### CRS_CA_START – Start Closest Approach

Start closest approach processing logic.  Also, enable or disable selection of backup closest approach macro.

| Name | Length (bits) | Value | Description |
| --- | --- | --- | --- |
| Opcode | 16 | 0x014e |  |
| Macro? | 1 | 0 = Execute 1 = Append to macro | Macro load bit |
| Length | 15 | 3 | Command length in 32-bit words |
| Mode | 8 | 0 = Good targeting 1 = Bad targeting | Closest approach mode |
| Pad | 24 | 0 | Pad up to 32-bit boundary |
| Checksum | 32 |  | 32 bit XOR |

### CRS_COV_DEPLOY – Deploy the Cover

Turn power to cover’s HOP actuators off or on.  Turning on the actuator deploys the cover.  With operation 2, the power is removed automatically from all of the actuators by the DPU software ten seconds after the cover is open; “open” is defined as either HOP telltale indicating “extended”.  With operation 3, the actuator power is removed after a timeout period; the timeout is a parameter.  With operation 4, the actuator power is removed once the cover is open or the timeout period elapses.  This command will be rejected unless specifically enabled with the CRS_COV_MODE command.  Note: the imager primary power must be turned on for the cover to deploy.

| Name | Length (bits) | Value | Description |
| --- | --- | --- | --- |
| Opcode | 16 | 0x0100 |  |
| Macro? | 1 | 0 = Execute 1 = Append to macro | Macro load bit |
| Length | 15 | 3 | Command length in 32-bit words |
| Operation | 8 | 0 = Off 1 = On 2 = On until deployed 3 = On until timeout 4 = On until deployed or timeout | Operation for the given heater |
| Heater | 8 | 0 = HOP 1, heater 1 1 = HOP 1, heater 2 2 = HOP 2, heater 1 3 = HOP 2, heater 2 | Heater |
| Pad | 16 | 0 | Pad up to 32-bit boundary |
| Checksum | 32 |  | 32 bit XOR |

### CRS_COV_LED – Control Cover LED Power

Turn cover’s telltale LED power off or on.  Note: the imager primary power must be turned on for the LEDs to light.

| Name | Length (bits) | Value | Description |
| --- | --- | --- | --- |
| Opcode | 16 | 0x0103 |  |
| Macro? | 1 | 0 = Execute 1 = Append to macro | Macro load bit |
| Length | 15 | 3 | Command length in 32-bit words |
| Mode | 8 | 0 = Off 1 = On | LED off/on |
| LED | 8 | 0 = LED 1 1 = LED 2 255 = both LEDs | LED |
| Pad | 16 | 0 | Pad up to 32-bit boundary |
| Checksum | 32 |  | 32 bit XOR |

### CRS_COV_MODE – Enable/Disable Cover Deployment

Enable or disable deployment of the cover.  This is a safety interlock; the actuators must be enabled before actually powering the actuator (with CRS_COV_DEPLOY).

| Name | Length (bits) | Value | Description |
| --- | --- | --- | --- |
| Opcode | 16 | 0x0105 |  |
| Macro? | 1 | 0 = Execute 1 = Append to macro | Macro load bit |
| Length | 15 | 3 | Command length in 32-bit words |
| Mode | 8 | 0 = Disable 1 = Enable | Deployment enable/disable |
| Pad | 24 | 0 | Pad up to 32-bit boundary |
| Checksum | 32 |  | 32 bit XOR |

### CRS_FLT_MOVE – Move Filter Wheel

Move filter wheel to indicated position.  The filter movement begins at the end of the current exposure.  Note: the FW motor primary power must be turned on for the filter wheel to move.

| Name | Length (bits) | Value | Description |
| --- | --- | --- | --- |
| Opcode | 16 | 0x0106 |  |
| Macro? | 1 | 0 = Execute 1 = Append to macro | Macro load bit |
| Length | 15 | 3 | Command length in 32-bit words |
| Filter | 8 | 1 – 10 | Filter wheel position |
| Pad | 24 | 0 | Pad up to 32-bit boundary |
| Checksum | 32 |  | 32 bit XOR |

### CRS_FLT_PWR – Control Filter Wheel Power

Turn filter wheel resolver power off or on.  Note: the FW motor primary power must be turned on for the filter wheel resolver to operate.

| Name | Length (bits) | Value | Description |
| --- | --- | --- | --- |
| Opcode | 16 | 0x0109 |  |
| Macro? | 1 | 0 = Execute 1 = Append to macro | Macro load bit |
| Length | 15 | 3 | Command length in 32-bit words |
| Mode | 8 | 0 = Off 1 = On | Filter wheel resolver power off/on |
| Pad | 24 | 0 | Pad up to 32-bit boundary |
| Checksum | 32 |  | 32 bit XOR |

### CRS_FLT_STEP – Step Filter Wheel

Move filter wheel the indicated number of resolver counts.  Note: the FW motor primary power must be turned on for the filter wheel to move.

| Name | Length (bits) | Value | Description |
| --- | --- | --- | --- |
| Opcode | 16 | 0x0169 |  |
| Macro? | 1 | 0 = Execute 1 = Append to macro | Macro load bit |
| Length | 15 | 3 | Command length in 32-bit words |
| Counts | 16 | -32768 – 32767 | Filter motion (resolver counts) |
| Pad | 16 | 0 | Pad up to 32-bit boundary |
| Checksum | 32 |  | 32 bit XOR |

### CRS_HTR_MODE – Set Heater Control Mode

Select heater off, on, or controlled by software.

| Name | Length (bits) | Value | Description |
| --- | --- | --- | --- |
| Opcode | 16 | 0x010a |  |
| Macro? | 1 | 0 = Execute 1 = Append to macro | Macro load bit |
| Length | 15 | 3 | Command length in 32-bit words |
| Mode | 8 | 0 = Off 1 = On 2 = Software control | Control mode |
| Zone | 8 | 0 = Star camera 1 1 = Star camera 2 2 = Diaphragm 3 = Mirror motor 4 = Bulk 255 = All | Heater control zone |
| Pad | 16 | 0 | Pad up to 32-bit boundary |
| Checksum | 32 |  | 32 bit XOR |

### CRS_HTR_TMP – Set Heater Temperature

Set temperature goal of the heater in the indicated zone.  The temperature will be held between the given setpoint and setpoint+hysteresis.

| Name | Length (bits) | Value | Description |
| --- | --- | --- | --- |
| Opcode | 16 | 0x010c |  |
| Macro? | 1 | 0 = Execute 1 = Append to macro | Macro load bit |
| Length | 15 | 3 | Command length in 32-bit words |
| Setpoint | 16 | Unsigned integer | Temperature setpoint (A/D units) |
| Hysteresis | 8 | Unsigned integer | Hysteresis (A/D units) |
| Zone | 8 | 0 = Star camera 1 1 = Star camera 2 2 = Diaphragm 3 = Mirror motor 4 = Bulk 255 = All | Heater control zone |
| Checksum | 32 |  | 32 bit XOR |

### CRS_IMG_COMP_ALG – Select Image Compression Algorithm

Select image compression algorithm.  When executed at time t affects the exposure taken at time t+1.

| Name | Length (bits) | Value | Description |
| --- | --- | --- | --- |
| Opcode | 16 | 0x0156 |  |
| Macro? | 1 | 0 = Execute 1 = Append to macro | Macro load bit |
| Length | 15 | 3 | Command length in 32-bit words |
| Mode | 8 | 0 = High-range identity 1 = Low-end identity 2 = Mid-range identity 3 = DN-weighted SNR 4 = Inverse root 2 power 5 = Linear 6 = SNR proportional 7 = Root 2 power | Compression algorithm |
| Pad | 24 | 0 | Pad up to 32-bit boundary |
| Checksum | 32 |  | 32 bit XOR |

### CRS_IMG_COMP_MODE – Enable/Disable Image Compression

Enable or disable image compression.  When executed at time t affects the exposure taken at time t+1.

| Name | Length (bits) | Value | Description |
| --- | --- | --- | --- |
| Opcode | 16 | 0x010f |  |
| Macro? | 1 | 0 = Execute 1 = Append to macro | Macro load bit |
| Length | 15 | 3 | Command length in 32-bit words |
| Mode | 8 | 0 = Disable 1 = Enable | Enable/disable image compression |
| Pad | 24 | 0 | Pad up to 32-bit boundary |
| Checksum | 32 |  | 32 bit XOR |

### CRS_IMG_EXP – Set Image Exposure Time

Set image exposure time.  An exposure time set at time t effects the exposure taken at t+1.  Exposure times can range from 128 µs to 979.968 ms.

| Name | Length (bits) | Value | Description |
| --- | --- | --- | --- |
| Opcode | 16 | 0x0111 |  |
| Macro? | 1 | 0 = Execute 1 = Append to macro | Macro load bit |
| Length | 15 | 3 | Command length in 32-bit words |
| Time | 16 | 1 – 7656 | Exposure time in 128 µs units |
| Pad | 16 | 0 | Pad up to 32-bit boundary |
| Checksum | 32 |  | 32 bit XOR |

### CRS_IMG_FORMAT – Select Image Format

Select the format of the images to be telemetered.  When executed at time t affects the exposure taken at time t+1.

| Name | Length (bits) | Value | Description |
| --- | --- | --- | --- |
| Opcode | 16 | 0x0112 |  |
| Macro? | 1 | 0 = Execute 1 = Append to macro | Macro load bit |
| Length | 15 | 3 | Command length in 32-bit words |
| Format | 8 | 0 = 1024 x 1024 1 = 512 x 512 2 = 256 x 256 3 = 128 x 128 | Image format |
| Pad | 24 | 0 | Pad up to 32-bit boundary |
| Checksum | 32 |  | 32 bit XOR |

### CRS_IMG_IMAGE – Collect Images for Downlink

Collect a series of images and downlink them.  An exposure requested at time t is taken at t+1.  If an image collection series is in progress and a new CRS_IMG_IMAGE is issued, the new command supersedes the old command.

| Name | Length (bits) | Value | Description |
| --- | --- | --- | --- |
| Opcode | 16 | 0x0150 |  |
| Macro? | 1 | 0 = Execute 1 = Append to macro | Macro load bit |
| Length | 15 | 3 | Command length in 32-bit words |
| Time | 16 | 0 – 65534 = Duration 65535 = Forever | Time in which to collect images (seconds) |
| Interval | 16 | 1 – 65535 | Interval between images (seconds) |
| Checksum | 32 |  | 32 bit XOR |

### CRS_IMG_PWR – Control Imager Power

Turn imager FPU power off or on.  Note: the imager primary power must be turned on for the imager FPU to activate.

| Name | Length (bits) | Value | Description |
| --- | --- | --- | --- |
| Opcode | 16 | 0x0114 |  |
| Macro? | 1 | 0 = Execute 1 = Append to macro | Macro load bit |
| Length | 15 | 3 | Command length in 32-bit words |
| Mode | 8 | 0 = Off 1 = On | Imager power off/on |
| Pad | 24 | 0 | Pad up to 32-bit boundary |
| Checksum | 32 |  | 32 bit XOR |

### CRS_IMG_REGION – Select Image Region of Interest

Set the origin of the image to be telemetered.  When executed at time t affects the exposure taken at time t+1.

| Name | Length (bits) | Value | Description |
| --- | --- | --- | --- |
| Opcode | 16 | 0x0117 |  |
| Macro? | 1 | 0 = Execute 1 = Append to macro | Macro load bit |
| Length | 15 | 3 | Command length in 32-bit words |
| X | 16 | 0 – 1023 | X origin |
| Y | 16 | 0 – 1023 | Y origin |
| Checksum | 32 |  | 32 bit XOR |

### CRS_IMG_TRACK – Collect Tracking Images

Collect a series of images for the TPU.  An exposure requested at time t is taken at t+1.  If an image collection series is in progress and a new CRS_IMG_TRACK is issued, the new command supersedes the old command.

| Name | Length (bits) | Value | Description |
| --- | --- | --- | --- |
| Opcode | 16 | 0x0118 |  |
| Macro? | 1 | 0 = Execute 1 = Append to macro | Macro load bit |
| Length | 15 | 3 | Command length in 32-bit words |
| Time | 16 | 0 – 65534 = Duration 65535 = Forever | Time in which to collect images (seconds) |
| Interval | 16 | 1 – 65535 | Interval between images (seconds) |
| Checksum | 32 |  | 32 bit XOR |

### CRS_MEM_STR_LOAD – Load Values into a Data Structure

Load the data values into the identified data structure at the location denoted by the offset.  The byte count determines how many load bytes follow and may be up to 128 bytes.  The padding after the data forces the size of the load to be a multiple of 4 bytes; M+N is always a multiple of 4.

| Name | Length (bits) | Value | Description |
| --- | --- | --- | --- |
| Opcode | 16 | 0x0023 |  |
| Macro? | 1 | 0 = Execute 1 = Append to macro | Macro load bit |
| Length | 15 | 4 – 35 | Command length in 32-bit words |
| Id | 8 | 0 = Monitor limits 1 = DPU parameters | Id of data structure |
| Byte Count | 8 | 0 – 128 (M) | Number of bytes in data field |
| Offset | 16 | Unsigned integer | Byte offset into data structure |
| Data | M * 8 |  | Load data |
| Pad | N * 8 | 0 | Pad up to 32-bit boundary |
| Checksum | 32 |  | 32 bit XOR |

### CRS_MEM_STR_READ – Read a Data Structure

Dump the identified data structure.

| Name | Length (bits) | Value | Description |
| --- | --- | --- | --- |
| Opcode | 16 | 0x0025 |  |
| Macro? | 1 | 0 = Execute 1 = Append to macro | Macro load bit |
| Length | 15 | 3 | Command length in 32-bit words |
| Id | 8 | 0 = Monitor limits 1 = DPU parameters | Id of data structure |
| Pad | 24 | 0 | Pad up to 32-bit boundary |
| Checksum | 32 |  | 32 bit XOR |

### CRS_PWR_PRI – Control Primary Power

Turn primary power off or on to a selected subsystem.

| Name | Length (bits) | Value | Description |
| --- | --- | --- | --- |
| Opcode | 16 | 0x0165 |  |
| Macro? | 1 | 0 = Execute 1 = Append to macro | Macro load bit |
| Length | 15 | 3 | Command length in 32-bit words |
| Mode | 8 | 0 = Off 1 = On | Primary power off/on |
| Board | 8 | 0 = Imager 1 = Spectrometer 2 = FW Motor 255 = All | Power board |
| Pad | 16 | 0 | Pad up to 32-bit boundary |
| Checksum | 32 |  | 32 bit XOR |

### CRS_SPC_CAL_LEVEL – Set Spectrometer Calibrator Level

Set the level, and consequently the brightness, of the spectrometer’s IR calibration lamps.

| Name | Length (bits) | Value | Description |
| --- | --- | --- | --- |
| Opcode | 16 | 0x0155 |  |
| Macro? | 1 | 0 = Execute 1 = Append to macro | Macro load bit |
| Length | 15 | 3 | Command length in 32-bit words |
| Level | 8 | 0 = Dimmest … 255 = Brightest | Lamp brightness level |
| Lamp | 8 | 0 = Lamp 1 1 = Lamp 2 255 = Both lamps | Lamp |
| Pad | 16 | 0 | Pad up to 32-bit boundary |
| Checksum | 32 |  | 32 bit XOR |

### CRS_SPC_CAL_PWR – Control Spectrometer Calibrator Power

Calibrate spectrometer by turning two IR calibration lamps off or on.

| Name | Length (bits) | Value | Description |
| --- | --- | --- | --- |
| Opcode | 16 | 0x011b |  |
| Macro? | 1 | 0 = Execute 1 = Append to macro | Macro load bit |
| Length | 15 | 3 | Command length in 32-bit words |
| Mode | 8 | 0 = Off 1 = On for 1 minute | Lamp power off/on |
| Lamp | 8 | 0 = Lamp 1 1 = Lamp 2 255 = Both lamps | Lamp |
| Pad | 16 | 0 | Pad up to 32-bit boundary |
| Checksum | 32 |  | 32 bit XOR |

### CRS_SPC_COOL – Control Spectrometer Cooler Power

Turn spectrometer cooler power off or on.  There are two possible temperatures to select when the cooler is on.  Note: the spectrometer primary power must be turned on for the cooler to operate.

| Name | Length (bits) | Value | Description |
| --- | --- | --- | --- |
| Opcode | 16 | 0x011d |  |
| Macro? | 1 | 0 = Execute 1 = Append to macro | Macro load bit |
| Length | 15 | 3 | Command length in 32-bit words |
| Mode | 8 | 0 = Off 1 = Low (90 K) 2 = High (103 K) | Cooler power off/on and goal |
| Pad | 24 | 0 | Pad up to 32-bit boundary |
| Checksum | 32 |  | 32 bit XOR |

### CRS_SPC_FORMAT – Select Spectrometer Image Format

Select the format of the spectrometer images to be telemetered.

| Name | Length (bits) | Value | Description |
| --- | --- | --- | --- |
| Opcode | 16 | 0x011e |  |
| Macro? | 1 | 0 = Execute 1 = Append to macro | Macro load bit |
| Length | 15 | 3 | Command length in 32-bit words |
| Format | 8 | 0 = 256 x 256 1 = 128 x 256 2 = 64 x 256 3 = 32 x 256 | Image format |
| Pad | 24 | 0 | Pad up to 32-bit boundary |
| Checksum | 32 |  | 32 bit XOR |

### CRS_SPC_PWR – Control Spectrometer Power

Turn spectrometer FPU power off or on.  Note: the spectrometer primary power must be turned on for the spectrometer FPU to operate.

| Name | Length (bits) | Value | Description |
| --- | --- | --- | --- |
| Opcode | 16 | 0x0121 |  |
| Macro? | 1 | 0 = Execute 1 = Append to macro | Macro load bit |
| Length | 15 | 3 | Command length in 32-bit words |
| Mode | 8 | 0 = Off 1 = On | Spectrometer power off/on |
| Pad | 24 | 0 | Pad up to 32-bit boundary |
| Checksum | 32 |  | 32 bit XOR |

### CRS_SPC_RANGE – Select Spectrometer Image Range

Select a range of bits within each spectrometer pixel; these are the bits that will be telemetered.

| Name | Length (bits) | Value | Description |
| --- | --- | --- | --- |
| Opcode | 16 | 0x016a |  |
| Macro? | 1 | 0 = Execute 1 = Append to macro | Macro load bit |
| Length | 15 | 3 | Command length in 32-bit words |
| Range | 8 | 0 = Bits 12..1 1 = Bits 13..2 2 = Bits 11..0 | Image range |
| Pad | 24 | 0 | Pad up to 32-bit boundary |
| Checksum | 32 |  | 32 bit XOR |

### CRS_SPC_RATE – Control Spectrometer Collection Rate

Control the spectrometer collection rate.  Note: even if no spectra are being telemetered, the spectrometer will be cycled at this rate.

| Name | Length (bits) | Value | Description |
| --- | --- | --- | --- |
| Opcode | 16 | 0x0122 |  |
| Macro? | 1 | 0 = Execute 1 = Append to macro | Macro load bit |
| Length | 15 | 3 | Command length in 32-bit words |
| Mode | 8 | 1 – 5 | Collection rate (Hz) |
| Pad | 24 | 0 | Pad up to 32-bit boundary |
| Checksum | 32 |  | 32 bit XOR |

### CRS_SPC_REGION – Select Spectrometer Image Region of Interest

Set the origin of the spectrometer image to be telemetered.

| Name | Length (bits) | Value | Description |
| --- | --- | --- | --- |
| Opcode | 16 | 0x0124 |  |
| Macro? | 1 | 0 = Execute 1 = Append to macro | Macro load bit |
| Length | 15 | 3 | Command length in 32-bit words |
| Origin | 8 | 0 – 255 | Origin in spatial dimension |
| Pad | 24 | 0 | Pad up to 32-bit boundary |
| Checksum | 32 |  | 32 bit XOR |

### CRS_SPC_SPECTRA – Collect Spectra

Collect spectra.  The collection will occur for the indicated time; a special value will produce continuous collection.  A request for spectra made at time t starts at t+1.  The number of spectra actually taken depends on the commanded spectrometer rate (CRS_SPC_RATE).

| Name | Length (bits) | Value | Description |
| --- | --- | --- | --- |
| Opcode | 16 | 0x0127 |  |
| Macro? | 1 | 0 = Execute 1 = Append to macro | Macro load bit |
| Length | 15 | 3 | Command length in 32-bit words |
| Time | 16 | 0 – 65534 = Duration 65535 = Forever | Time in which to collect spectra (seconds) |
| Pad | 16 | 0 | Pad up to 32-bit boundary |
| Checksum | 32 |  | 32 bit XOR |

### CRS_SPC_TMP – Enable/Disable Spectrometer Temperature Monitoring

Enable or disable temperature monitoring in the spectrometer front end.

| Name | Length (bits) | Value | Description |
| --- | --- | --- | --- |
| Opcode | 16 | 0x0163 |  |
| Macro? | 1 | 0 = Execute 1 = Append to macro | Macro load bit |
| Length | 15 | 3 | Command length in 32-bit words |
| Mode | 8 | 0 = Disable 1 = Enable | Enable/disable spectrometer temperature monitoring |
| Pad | 24 | 0 | Pad up to 32-bit boundary |
| Checksum | 32 |  | 32 bit XOR |

### CRS_TPU_AIM_ALG – Select Aim Algorithm

Select the aim algorithm used by TPU image processing to find the comet.

| Name | Length (bits) | Value | Description |
| --- | --- | --- | --- |
| Opcode | 16 | 0x014d |  |
| Macro? | 1 | 0 = Execute 1 = Append to macro | Macro load bit |
| Length | 15 | 3 | Command length in 32-bit words |
| Mode | 8 | 0 = Comet 1 = Brightest object | Aim algorithm |
| Pad | 24 | 0 | Pad up to 32-bit boundary |
| Checksum | 32 |  | 32 bit XOR |

### CRS_TPU_ATT_RESET – Reset Attitude Algorithm

Reset the TPU’s attitude estimation algorithm.

| Name | Length (bits) | Value | Description |
| --- | --- | --- | --- |
| Opcode | 16 | 0x016c |  |
| Macro? | 1 | 0 = Execute 1 = Append to macro | Macro load bit |
| Length | 15 | 2 | Command length in 32-bit words |
| Checksum | 32 |  | 32 bit XOR |

### CRS_TPU_IMG_REGION – Select Tracking Image Region of Interest

Set the origin of the region interest in the tracking image.

| Name | Length (bits) | Value | Description |
| --- | --- | --- | --- |
| Opcode | 16 | 0x0171 |  |
| Macro? | 1 | 0 = Execute 1 = Append to macro | Macro load bit |
| Length | 15 | 3 | Command length in 32-bit words |
| X | 16 | 0 – 1023 | X origin |
| Y | 16 | 0 – 1023 | Y origin |
| Checksum | 32 |  | 32 bit XOR |

### CRS_TPU_IMG_ZOOM – Select Tracking Image Zoom

Set the zoom mode of the tracking image.

| Name | Length (bits) | Value | Description |
| --- | --- | --- | --- |
| Opcode | 16 | 0x0172 |  |
| Macro? | 1 | 0 = Execute 1 = Append to macro | Macro load bit |
| Length | 15 | 3 | Command length in 32-bit words |
| Zoom | 8 | 0 = 8x8 rebin 1 = 4x4 rebin 2 = 2x2 rebin 3 = 1x1 rebin | Zoom mode |
| Pad | 24 | 0 | Pad up to 32-bit boundary |
| Checksum | 32 |  | 32 bit XOR |

### CRS_TPU_MEM_CHECK – Check TPU Memory

Calculate the checksum of TPU memory at given address.  The checksum is the 32-bit two’s complement sum of the memory indicated.  The results are downlinked in a subpacket.

| Name | Length (bits) | Value | Description |
| --- | --- | --- | --- |
| Opcode | 16 | 0x0128 |  |
| Macro? | 1 | 0 = Execute 1 = Append to macro | Macro load bit |
| Length | 15 | 4 | Command length in 32-bit words |
| Source | 32 | Unsigned integer | Source address |
| Byte Count | 32 | Unsigned integer | Number of bytes to check |
| Checksum | 32 |  | 32 bit XOR |

### CRS_TPU_MEM_COPY – Copy TPU Memory

Copy TPU memory from source to destination.  The source or destination can be either RAM or EEPROM.  The result is undefined if the source and destination regions overlap.

| Name | Length (bits) | Value | Description |
| --- | --- | --- | --- |
| Opcode | 16 | 0x012b |  |
| Macro? | 1 | 0 = Execute 1 = Append to macro | Macro load bit |
| Length | 15 | 5 | Command length in 32-bit words |
| Source | 32 | Unsigned integer | Source address |
| Destination | 32 | Unsigned integer | Destination address |
| Byte Count | 32 | Unsigned integer | Number of bytes to copy |
| Checksum | 32 |  | 32 bit XOR |

### CRS_TPU_MEM_LOAD – Load TPU Memory

Load memory to the TPU.  The byte count determines how many load bytes follow and may be up to 128 bytes.  The padding after the data forces the size of the load to be a multiple of 4 bytes; M+N is always a multiple of 4.

| Name | Length (bits) | Value | Description |
| --- | --- | --- | --- |
| Opcode | 16 | 0x012d |  |
| Macro? | 1 | 0 = Execute 1 = Append to macro | Macro load bit |
| Length | 15 | 4 – 36 | Command length in 32-bit words |
| Address | 32 | Unsigned integer | Starting address |
| Byte Count | 8 | 0 – 128 (M) | Number of bytes in data field |
| Spare | 24 |  |  |
| Data | M * 8 |  | Load data |
| Pad | N * 8 | 0 | Pad up to 32-bit boundary |
| Checksum | 32 |  | 32 bit XOR |

### CRS_TPU_MEM_READ – Read TPU Memory

Dump TPU memory from given address.

| Name | Length (bits) | Value | Description |
| --- | --- | --- | --- |
| Opcode | 16 | 0x012e |  |
| Macro? | 1 | 0 = Execute 1 = Append to macro | Macro load bit |
| Length | 15 | 4 | Command length in 32-bit words |
| Source | 32 | Unsigned integer | Source address |
| Byte Count | 32 | Unsigned integer | Number of bytes to dump |
| Checksum | 32 |  | 32 bit XOR |

### CRS_TPU_MEM_READ_ABT – Abort TPU Memory Read

Abort the current TPU memory dump.

| Name | Length (bits) | Value | Description |
| --- | --- | --- | --- |
| Opcode | 16 | 0x0130 |  |
| Macro? | 1 | 0 = Execute 1 = Append to macro | Macro load bit |
| Length | 15 | 2 | Command length in 32-bit words |
| Checksum | 32 |  | 32 bit XOR |

### CRS_TPU_MEM_RUN – Run a TPU Program

Run a program at the given TPU address.  The program must either execute very quickly (so as not to hold up the command handler) or must take over completely.

| Name | Length (bits) | Value | Description |
| --- | --- | --- | --- |
| Opcode | 16 | 0x0133 |  |
| Macro? | 1 | 0 = Execute 1 = Append to macro | Macro load bit |
| Length | 15 | 3 | Command length in 32-bit words |
| Address | 32 | Unsigned integer | Program start address |
| Checksum | 32 |  | 32 bit XOR |

### CRS_TPU_MEM_STR_LOAD – Load Values into TPU Data Structure

Load the data values into the identified data structure at the location denoted by the offset.  The byte count determines how many load bytes follow and may be up to 128 bytes.  The padding after the data forces the size of the load to be a multiple of 4 bytes; M+N is always a multiple of 4.

| Name | Length (bits) | Value | Description |
| --- | --- | --- | --- |
| Opcode | 16 | 0x0135 |  |
| Macro? | 1 | 0 = Execute 1 = Append to macro | Macro load bit |
| Length | 15 | 4 – 35 | Command length in 32-bit words |
| Id | 8 | 0 = Mirror parameters 1 = Aim parameters 2 = CA parameters 3 = Tracker offset 4 = Tracker control 5 = Tracker target 6 = Tracker EKF 7 = Tracker Cheby #1 8 = Tracker Cheby #2 9 = Tracker Cheby #3 10 = Tracker mirror 11 = Tracker gate 12 = Tracker align | Id of data structure |
| Byte Count | 8 | 0 – 128 (M) | Number of bytes in data field |
| Offset | 16 | Unsigned integer | Byte offset into data structure |
| Data | M * 8 |  | Load data |
| Pad | N * 8 | 0 | Pad up to 32-bit boundary |
| Checksum | 32 |  | 32 bit XOR |

### CRS_TPU_MEM_STR_READ – Read TPU Data Structure

Dump the identified data structure.

| Name | Length (bits) | Value | Description |
| --- | --- | --- | --- |
| Opcode | 16 | 0x0136 |  |
| Macro? | 1 | 0 = Execute 1 = Append to macro | Macro load bit |
| Length | 15 | 3 | Command length in 32-bit words |
| Id | 8 | 0 = Mirror parameters 1 = Aim parameters 2 = CA parameters 3 = Tracker offset 4 = Tracker control 5 = Tracker target 6 = Tracker EKF 7 = Tracker Cheby #1 8 = Tracker Cheby #2 9 = Tracker Cheby #3 10 = Tracker mirror 11 = Tracker gate 12 = Tracker align | Id of data structure |
| Pad | 24 | 0 | Pad up to 32-bit boundary |
| Checksum | 32 |  | 32 bit XOR |

### CRS_TPU_MIR_ANGLE – Set the Slew Mode Target Angle

Sets the angle of the target to use when in slew mode (see CRS_TPU_MIR_MODE).  The angle specifies the imager’s look direction; a zero angle looks along the nose of the instrument.  Note that this is not the same as the mirror shaft angle.  The actual mirror shaft angle used will depend on the commanded angle and mirror side (see CRS_TPU_MIR_SIDE).

| Name | Length (bits) | Value | Description |
| --- | --- | --- | --- |
| Opcode | 16 | 0x0139 |  |
| Macro? | 1 | 0 = Execute 1 = Append to macro | Macro load bit |
| Length | 15 | 3 | Command length in 32-bit words |
| Angle | 32 | IEEE-754 single | Slew target angle (degrees) |
| Checksum | 32 |  | 32 bit XOR |

### CRS_TPU_MIR_HOME – Find Mirror Home Position

Search for mirror home fiducial.  Once found, move the mirror to 90º, and set the mirror mode to “hold”.

| Name | Length (bits) | Value | Description |
| --- | --- | --- | --- |
| Opcode | 16 | 0x013a |  |
| Macro? | 1 | 0 = Execute 1 = Append to macro | Macro load bit |
| Length | 15 | 2 | Command length in 32-bit words |
| Checksum | 32 |  | 32 bit XOR |

### CRS_TPU_MIR_MODE – Set the Mirror Mode

Sets the control mode of the tracking mirror.  When off, the mirror motor is not driven.  In hold mode, the mirror is held at the current position.  In slew mode, the mirror is held at a commanded angle (see CRS_TPU_MIR_ANGLE).  In scan mode, the mirror follows a profile computed by the tracker.  Whenever the mirror mode is commanded, the mirror controller is reset.

| Name | Length (bits) | Value | Description |
| --- | --- | --- | --- |
| Opcode | 16 | 0x013c |  |
| Macro? | 1 | 0 = Execute 1 = Append to macro | Macro load bit |
| Length | 15 | 3 | Command length in 32-bit words |
| Mode | 8 | 0 = Off 1 = Hold 2 = Slew 3 = Scan | Mirror mode |
| Pad | 24 | 0 | Pad up to 32-bit boundary |
| Checksum | 32 |  | 32 bit XOR |

### CRS_TPU_MIR_PWR – Control Mirror Motor Power

Turn mirror motor power off or on.  Turning off the motor power also sets the mirror control mode to “off” (see CRS_TPU_MIR_MODE).

| Name | Length (bits) | Value | Description |
| --- | --- | --- | --- |
| Opcode | 16 | 0x0159 |  |
| Macro? | 1 | 0 = Execute 1 = Append to macro | Macro load bit |
| Length | 15 | 3 | Command length in 32-bit words |
| Mode | 8 | 0 = Off 1 = On | Mirror motor power off/on |
| Pad | 24 | 0 | Pad up to 32-bit boundary |
| Checksum | 32 |  | 32 bit XOR |

### CRS_TPU_MIR_SIDE – Select Mirror Side

Selects which side of the mirror to use.

| Name | Length (bits) | Value | Description |
| --- | --- | --- | --- |
| Opcode | 16 | 0x013f |  |
| Macro? | 1 | 0 = Execute 1 = Append to macro | Macro load bit |
| Length | 15 | 3 | Command length in 32-bit words |
| Side | 8 | 0 = A (science) 1 = B (tracking) | Mirror side |
| Pad | 24 | 0 | Pad up to 32-bit boundary |
| Checksum | 32 |  | 32 bit XOR |

### CRS_TPU_OFF_ANGLE – Set the Target Offset Angle

Set the target offset angle.  If automatic offset adjustment is enabled (see CRS_TPU_OFF_MODE), the angle will be modified at a commandable rate (see CRS_TPU_OFF_RATE).  Note that the angle corresponds to the line-of-sight target angle rather than the mirror shaft angle.

| Name | Length (bits) | Value | Description |
| --- | --- | --- | --- |
| Opcode | 16 | 0x0142 |  |
| Macro? | 1 | 0 = Execute 1 = Append to macro | Macro load bit |
| Length | 15 | 3 | Command length in 32-bit words |
| Angle | 32 | IEEE-754 single | Target offset angle (degrees) |
| Checksum | 32 |  | 32 bit XOR |

### CRS_TPU_OFF_MODE – Enable/Disable Automatic Offset Adjustment

Enable or disable automatic offset adjustment.  When enabled the offset is adjusted based on the last commanded initial angle (CRS_TPU_OFF_ANGLE) and the rate (CRS_TPU_OFF_RATE).  When disabled, the offset is held at the last computed offset; when re-enabled, the offset adjust will pick up where it left off.  While disabled, the offset can be commanded to a fixed position via CRS_TPU_OFF_ANGLE).

| Name | Length (bits) | Value | Description |
| --- | --- | --- | --- |
| Opcode | 16 | 0x0144 |  |
| Macro? | 1 | 0 = Execute 1 = Append to macro | Macro load bit |
| Length | 15 | 3 | Command length in 32-bit words |
| Mode | 8 | 0 = Disable 1 = Enable | Enable/disable automatic offset adjustment |
| Pad | 24 | 0 | Pad up to 32-bit boundary |
| Checksum | 32 |  | 32 bit XOR |

### CRS_TPU_OFF_RATE – Set the Automatic Offset Rate

Set the automatic offset rate.  The mirror is adjusted by the commanded rate.  This rate is only used when automatic offset adjustment is commanded (CRS_TPU_OFF_MODE).  Note that this rate applies to the line-of-sight target angle and not the mirror shaft angle.

| Name | Length (bits) | Value | Description |
| --- | --- | --- | --- |
| Opcode | 16 | 0x0147 |  |
| Macro? | 1 | 0 = Execute 1 = Append to macro | Macro load bit |
| Length | 15 | 3 | Command length in 32-bit words |
| Rate | 32 | IEEE-754 single | Target offset rate (degrees/second) |
| Checksum | 32 |  | 32 bit XOR |

### CRS_TPU_TEST – Enable/Disable Test Mode

Enable or disable test mode.  In test mode, the tracking image is loaded from a test port rather the FPU.  This is only useful during testing on the ground.

| Name | Length (bits) | Value | Description |
| --- | --- | --- | --- |
| Opcode | 16 | 0x0166 |  |
| Macro? | 1 | 0 = Execute 1 = Append to macro | Macro load bit |
| Length | 15 | 3 | Command length in 32-bit words |
| Mode | 8 | 0 = Disable 1 = Enable | Test mode enable/disable |
| Pad | 24 | 0 | Pad up to 32-bit boundary |
| Checksum | 32 |  | 32 bit XOR |

### CRS_TPU_TLM_FLUSH – Flush TPU Telemetry Subpackets

If there is a partially filled subpacket packet in the TPU, generate a flush subpacket so that the packet will be downlinked.

| Name | Length (bits) | Value | Description |
| --- | --- | --- | --- |
| Opcode | 16 | 0x015a |  |
| Macro? | 1 | 0 = Execute 1 = Append to macro | Macro load bit |
| Length | 15 | 2 | Command length in 32-bit words |
| Checksum | 32 |  | 32 bit XOR |

### CRS_TPU_TLM_FLUSH_AUTO – Enable/Disable Automatic Flush

Enable or disable automatic flushing of partially filled subpacket packets in the TPU.  If enabled, the TPU will try to send a subpacket packet every other second, even if the packet has not been completely filled.  This is most useful during ground testing since it gives a low-latency response.

| Name | Length (bits) | Value | Description |
| --- | --- | --- | --- |
| Opcode | 16 | 0x015c |  |
| Macro? | 1 | 0 = Execute 1 = Append to macro | Macro load bit |
| Length | 15 | 3 | Command length in 32-bit words |
| Mode | 8 | 0 = Disable 1 = Enable | Enable/disable automatic flush |
| Pad | 24 | 0 | Pad up to 32-bit boundary |
| Checksum | 32 |  | 32 bit XOR |

### CRS_TPU_TRK_ALG – Select Tracking Algorithm

Select tracking algorithm.

| Name | Length (bits) | Value | Description |
| --- | --- | --- | --- |
| Opcode | 16 | 0x0148 |  |
| Macro? | 1 | 0 = Execute 1 = Append to macro | Macro load bit |
| Length | 15 | 3 | Command length in 32-bit words |
| Mode | 8 | 0 = Off 1 = Fixed target 2 = Moving target | Tracking algorithm |
| Pad | 24 | 0 | Pad up to 32-bit boundary |
| Checksum | 32 |  | 32 bit XOR |

### CRS_TPU_TRK_GOAL – Set Tracker Goal

Set desired target position on CCD.  The tracker tries to place the target at the specified position.

| Name | Length (bits) | Value | Description |
| --- | --- | --- | --- |
| Opcode | 16 | 0x0153 |  |
| Macro? | 1 | 0 = Execute 1 = Append to macro | Macro load bit |
| Length | 15 | 4 | Command length in 32-bit words |
| X | 32 | IEEE-754 single | X goal position (pixels) |
| Y | 32 | IEEE-754 single | Y goal position (pixels) |
| Checksum | 32 |  | 32 bit XOR |

### CRS_TPU_TRK_LOOP – Enable/Disable Closed-Loop Tracking

Enable or disable closed-loop tracking.

| Name | Length (bits) | Value | Description |
| --- | --- | --- | --- |
| Opcode | 16 | 0x014b |  |
| Macro? | 1 | 0 = Execute 1 = Append to macro | Macro load bit |
| Length | 15 | 3 | Command length in 32-bit words |
| Mode | 8 | 0 = Disable 1 = Enable | Enable/disable closed-loop tracking |
| Pad | 24 | 0 | Pad up to 32-bit boundary |
| Checksum | 32 |  | 32 bit XOR |

### CRS_TPU_TRK_TLM – Enable/Disable Tracking Telemetry

Enable or disable tracking telemetry production.

| Name | Length (bits) | Value | Description |
| --- | --- | --- | --- |
| Opcode | 16 | 0x016f |  |
| Macro? | 1 | 0 = Execute 1 = Append to macro | Macro load bit |
| Length | 15 | 3 | Command length in 32-bit words |
| Mode | 8 | 0 = Disable 1 = Enable | Enable/disable tracking telemetry |
| Pad | 24 | 0 | Pad up to 32-bit boundary |
| Checksum | 32 |  | 32 bit XOR |

# Support Processing

## 1553 Bus Management

CRISP communicates with the C&DH system over a 1553B bus.  The DPU acts as a remote terminal (RT) with the active C&DH system acting as the bus controller (BC).  The traffic on the 1553B bus is periodic, repeating every one second major frame.  The major frame is divided into 25 minor frames, numbered 0 to 24.  Individual messages are distinguished by their transmit or receive subaddress.  In addition to the messages described in Reference 3, CRISP handles the messages shown in the following table.

Table 19.  1553 Bus Usage

| Message | Subaddress | Minor Frame | Size (Words) |
| --- | --- | --- | --- |
| MIMU Angles and Status | R3 | All | 13 |
| G & C Delta Quaternion and Commanded Attitude | R22 | 24 | 41 |
| CRISP Attitude, Roll, and Closest Approach | T22 | 0 | 41 |

Four times per minor frame, the current MIMU gyro angles are sent to CRISP.  CRISP immediately forwards these to the TPU.  At the end of the major frame an attitude correction and the commanded attitude are sent to CRISP from G&C.  These are also forwarded to the TPU.  At the beginning of the major frame CRISP provides its estimate of the current attitude and time to closest approach.  The formats of these messages are shown in the following tables.

Table 20.  MIMU Angles and Status

| Name | Length (bits) | Value | Description |
| --- | --- | --- | --- |
| Time Tag | 32 |  | MET |
| Frame Timer | 16 |  | Frame timer 200 Hz |
| Frame Count | 16 |  | Frame counter 1 Hz |
| IRU Status | 16 |  | IRU status word |
| X | 16 |  | Incremental angle X |
| Y | 16 |  | Incremental angle Y |
| Z | 16 |  | Incremental angle Z |
| X DeltaT | 16 |  | Average X gyro delta temperature |
| Y DeltaT | 16 |  | Average Y gyro delta temperature |
| Z DeltaT | 16 |  | Average Z gyro delta temperature |
| Block T | 16 |  | Average sensor block temperature |
| Checksum | 16 |  | Arithmetic checksum |

Table 21.  G&C Delta Quaternion and Commanded Attitude to CRISP

| Name | Length (bits) | Value | Description |
| --- | --- | --- | --- |
| DeltaQ | 4 * 64 | IEEE-754 double | Correction to CRISP attitude |
| Qcmd | 4 * 64 | IEEE-754 double | Commanded attitude |
| TDT Offset | 64 | IEEE-754 double | Offset from MET to TDT |
| Time Tag | 32 | Unsigned integer | MET |
| DeltaQ Flag | 16 | 0 = Valid 1 = Invalid | DeltaQ invalid flag |
| Qcmd Flag | 16 | 0 = Valid 1 = Invalid | Qcmd invalid flag |
| Flag | 16 | 0 = Not relative to CRISP 1 = Relative to CRISP | Attitude correction flag |

Table 22. CRISP Attitude, Roll, and Closest Approach to G&C

| Name | Length (bits) | Value | Description |
| --- | --- | --- | --- |
| Time Tag | 32 | Unsigned integer | MET |
| CA | 32 | 0 = Now 99998 = Future | Time to closest approach |
| MET Offset | 64 | IEEE-754 double | Time offset from MET to attitude estimate |
| Qroll | 4 * 64 | IEEE-754 double | Roll correction |
| QCRISP | 4 * 64 | IEEE-754 double | CRISP attitude estimate |
| Flag | 16 | 0 = All valid 1 = One or more invalid | Message invalid flag |

## Inter-Integrated Circuit (I2C) Bus Management

A collection of environmental data is collected by the DPU.  There are analogs including voltages and currents read via one of the DPU’s two Inter-Integrated Circuit (I2C) buses.  A second I2C bus is used to collect temperatures.  The data collected is included in the status subpacket and image headers.  Each analog is also monitored when it is read (see below).  Collection and monitoring occur once per second.

## Alarms and Monitoring

Alarms report problems found by the DPU software.  Each alarm is described by an ID, two values, and a flag.  The ID identifies the problem that has occurred and the accompanying values offer additional information.  The flag indicates whether the alarm was caused by a transient or a persistent condition.  See Appendix 3 for a list of alarms.

The alarms are divided into two groups: one for reporting internal software problems and another for reporting out-of-limit conditions for monitored data.  Software problems are all reported as transient alarms.  When the problem occurs, the alarm is generated and the software recovers from the problem as best it can.

Values read from the I2C buses are monitored by the DPU The monitoring is event driven: a monitor cycle is performed on each item as it becomes available.  For example, each I2C analog is monitored when it is read.  The monitoring algorithm is described in more detail in Reference 3.

The monitored data is summarized in the following table.  The monitor class is encoded as S=shutdown, N=nop, and R=redo.  The reported alarm Ids are for low and high excursions; similarly there are low and high response macro Ids.

Table 23.  Monitored Data

| Source | Class | Alarm Ids Low / High | Macro Ids Low / High |
| --- | --- | --- | --- |
| Mirror motor current | N | 128 | 192 | 0 | 18 |
| Star camera #1 heater current | N | 129 | 193 | 0 | 2 |
| Star camera #2 heater current | N | 130 | 194 | 0 | 2 |
| Diaphragm heater current | N | 131 | 195 | 0 | 2 |
| Mirror motor heater current | N | 132 | 196 | 0 | 2 |
| Bulk heater current | N | 133 | 197 | 0 | 2 |
| DPU current | N | 134 | 198 | 1 | 1 |
| DPU voltage | N | 135 | 199 | 1 | 1 |
| Imager converter current | N | 136 | 200 | 0 | 16 |
| HOP actuator #1 heater #1 current | N | 137 | 201 | 0 | 14 |
| HOP actuator #1 heater #2 current | N | 138 | 202 | 0 | 14 |
| Imager current | N | 139 | 203 | 0 | 16 |
| HOP actuator #2 heater #1 current | N | 140 | 204 | 0 | 14 |
| Imager voltage | N | 141 | 205 | 0 | 16 |
| HOP actuator #2 heater #2 current | N | 142 | 206 | 0 | 14 |
| Spectrometer primary current | N | 143 | 207 | 0 | 17 |
| Spectrometer converter current | N | 144 | 208 | 0 | 17 |
| Cooler converter current | N | 145 | 209 | 0 | 17 |
| Cooler current | N | 146 | 210 | 0 | 17 |
| Spectrometer current | N | 147 | 211 | 0 | 17 |
| Cooler voltage | N | 148 | 212 | 0 | 17 |
| Spectrometer voltage | N | 149 | 213 | 0 | 17 |
| FW motor primary current | N | 150 | 214 | 0 | 15 |
| FW motor current | N | 151 | 215 | 0 | 15 |
| FW motor converter current | N | 152 | 216 | 0 | 15 |
| FW 15V current | N | 153 | 217 | 0 | 15 |
| FW 15V voltage | N | 154 | 218 | 0 | 15 |
| Spectrometer housing temperature | N | 155 | 219 | 0 | 13 |
| Mirror motor elec. temperature | N | 156 | 220 | 0 | 13 |
| Cryo cooler temperature | N | 157 | 221 | 0 | 13 |
| Fold mirror temperature | N | 158 | 222 | 0 | 13 |
| Housing rear temperature | N | 159 | 223 | 0 | 13 |
| M2 temperature | N | 160 | 224 | 0 | 13 |
| M1 temperature | N | 161 | 225 | 0 | 13 |
| Diaphragm temperature | N | 162 | 226 | 0 | 13 |
| Mirror motor temperature | N | 163 | 227 | 0 | 13 |
| Star camera #2 temperature | N | 164 | 228 | 0 | 13 |
| Star camera #1 temperature | N | 165 | 229 | 0 | 13 |
| HOPS actuator #1 temperature | N | 166 | 230 | 0 | 13 |
| Housing top temperature | N | 167 | 231 | 0 | 13 |
| Radiator temperature | N | 168 | 232 | 0 | 13 |
| Deck temperature | N | 169 | 233 | 0 | 13 |

## Fault Avoidance and Recovery

Many of the DPU’s hardware control registers contain triple redundancy and voting logic for each bit.  The DPU software periodically rewrites these registers to correct single bit errors.

The DPU has a watchdog timer.  If the watchdog timer is not tickled from time to time, the processor is reset.  The watchdog timeout is 2.95 seconds.  The watchdog does not run until it has been enabled; once enabled, it can never by disabled except by processor reset, watchdog or otherwise.  The DPU monitors all periodic processes every second.  If they are all running, the watchdog is tickled.  Some aperiodic processes do not participate.

## Closest Approach

The DPU will automatically select and run a macro to orchestrate data collection during closest approach.  The tracker estimates the time to closest approach, the miss distance between the spacecraft and the comet, and the angle from the spacecraft to the comet.  The TPU uses a set of thresholds to categorize the comet angle into either “inbound”, “inbound imaging”, “closest approach”, or “outbound imaging”.  The TPU also categorizes the miss distance as either “very near”, “near”, “nominal”, “far”, “very far”, “too far #1”, “too far #2”, or “too far #3”.  Once the DPU is commanded to monitor the closest approach data (CRS_CA_START), it watches the angle until “inbound imaging” is detected.  Then the DPU starts the closest approach imaging macro.  The miss distance category is used to select the macro.  The macro chosen depends on whether “good” targeting or “bad” targeting was selected (an argument to CRS_CA_START).  In “good” targeting mode, miss distances from “very near” to “very far” cause the corresponding “very near” to “very far” macro to be run; miss distances that are “too far” cause the “very far” macro to be run.  In “bad” targeting mode, the “too far” miss distances will cause corresponding “bad targeting” macros to be run.  Once one of the imaging macros has been selected, no other closest approach macro will be started.  The DPU continues to monitor the comet angle.  Once the “closest approach” stage is reached, a closest approach macro will be run.

The DPU will automatically run a post-encounter macro.  The macro is started once the comet angle reaches “outbound imaging”.  The macro will be allowed to run to completion.  Then the DPU closest approach monitor enters an idle state; another command (CRS_CA_START) is required before it will start monitoring the comet angle again.  The closest approach monitor can be commanded to the idle state at any time (CRS_CA_RESET).  The comet angle and miss distance thresholds are all TPU parameters.

# DPU Boot ROM Program

The DPU boot ROM program operates as described in Reference 3 with the addition of the following features for supporting the TPU.  In addition to the common boot telemetry, the CRISP DPU boot program also generates TPU memory dump packets and TPU memory checksum subpackets.  In addition to the common boot commands, the CRISP DPU boot program accepts the following TPU commands:

- CRS_TPU_MEM_CHECK, CRS_TPU_MEM_COPY, CRS_TPU_MEM_LOAD, CRS_TPU_MEM_READ, CRS_TPU_MEM_READ_ABT, and CRS_TPU_MEM_RUN

- CRS_TPU_TLM_FLUSH and CRS_TPU_TLM_FLUSH_AUTO

- CRS_TPU_ROM_BOOT and CRS_TPU_ROM_GO (see below)

### CRS_TPU_ROM_BOOT – Boot Default TPU Program

Boot the default TPU program from EEPROM (address = 0x9d000000).  See CRS_TPU_ROM_GO below.

| Name | Length (bits) | Value | Description |
| --- | --- | --- | --- |
| Opcode | 16 | 0x015f |  |
| Macro? | 1 | 0 = Execute 1 = Append to macro | Macro load bit |
| Length | 15 | 2 | Command length in 32-bit words |
| Checksum | 32 |  | 32 bit XOR |

### CRS_TPU_ROM_GO – Boot a Selected TPU Program

Boot a TPU program.  The address identifies a boot header (described below).  The program must either execute very quickly (so as not to hold up the command handler) or take over completely.

| Name | Length (bits) | Value | Description |
| --- | --- | --- | --- |
| Opcode | 16 | 0x0160 |  |
| Macro? | 1 | 0 = Execute 1 = Append to macro | Macro load bit |
| Length | 15 | 3 | Command length in 32-bit words |
| Address | 32 | Unsigned integer | Program header address |
| Checksum | 32 |  | 32 bit XOR |

# TPU Boot ROM Program

The TPU boot ROM program first initializes the hardware.  The program determines the cause of the reset.  On power-up reset, the program zeroes the entire contents of RAM; this takes several seconds.  On any other type of reset, the RAM is left untouched so that the corpse of a crashed program can be examined.  After initializing the hardware the boot program copies itself into RAM occupying addresses ranging from 0x901f0000 through 0x901fffff.  From this point on, the program runs in RAM.  The boot program stack grows down from address 0x901f0000.

Next, the boot program establishes communication with the DPU.  The program waits for commands from the DPU, executing the TPU memory commands described above.  The program can generate TPU memory dump packets and TPU subpacket packets. TPU alarm and TPU memory checksum subpackets can be produced.

The boot program can be commanded to run programs stored in EEPROM.  A program stored in EEPROM must be prefixed by a by a boot header:

| address | start address | length | checksum |
| --- | --- | --- | --- |

The address is a destination address for the program.  The start address is the entry point of the program.  The length is the total length including the header (measured in 32-bit words).  The checksum is the negation of the word-wise two’s complement sum of the rest of the header and the program; therefore, the checksum of the header and program should be zero.

# Appendix 1 - DPU Data Structures

Monitor limits consists of lower and upper limits of each monitored value; the lower limit is first followed by the upper limit.  Each limit is an eight bit unsigned integer; the monitored value is scaled accordingly before being monitored.

Table 24.  Monitor Limits Subpacket Format

| Name | Length (bits) | Value | Description |
| --- | --- | --- | --- |
| Time Tag | 32 | Unsigned integer | Spacecraft MET |
| Grouping | 2 | 11 = None | Grouping flags |
| Subpacket Id | 14 | 0x0005 | Identifies subpacket type |
| Length | 16 | 84 | Number of data bytes in subpacket |
| Ana DPU/0 | 2 * 8 | Unsigned integer | Mirror motor current |
| Ana DPU/1 | 2 * 8 | Unsigned integer | Star camera #1 heater current |
| Ana DPU/2 | 2 * 8 | Unsigned integer | Star camera #2 heater current |
| Ana DPU/3 | 2 * 8 | Unsigned integer | Diaphragm heater current |
| Ana DPU/4 | 2 * 8 | Unsigned integer | Mirror motor heater current |
| Ana DPU/5 | 2 * 8 | Unsigned integer | Bulk heater current |
| Ana DPU/6 | 2 * 8 | Unsigned integer | DPU current |
| Ana DPU/7 | 2 * 8 | Unsigned integer | DPU voltage |
| Ana IM/0 | 2 * 8 | Unsigned integer | Imager converter current |
| Ana IM/1 | 2 * 8 | Unsigned integer | HOP actuator #1 heater #1 current |
| Ana IM/2 | 2 * 8 | Unsigned integer | HOP actuator #1 heater #2 current |
| Ana IM/3 | 2 * 8 | Unsigned integer | Imager current |
| Ana IM/4 | 2 * 8 | Unsigned integer | HOP actuator #2 heater #1 current |
| Ana IM/5 | 2 * 8 | Unsigned integer | Imager voltage |
| Ana IM/6 | 2 * 8 | Unsigned integer | HOP actuator #2 heater #2 current |
| Ana SP/0 | 2 * 8 | Unsigned integer | Spectrometer primary current |
| Ana SP/1 | 2 * 8 | Unsigned integer | Spectrometer converter current |
| Ana SP/2 | 2 * 8 | Unsigned integer | Cooler converter current |
| Ana SP/3 | 2 * 8 | Unsigned integer | Cooler current |
| Ana SP/4 | 2 * 8 | Unsigned integer | Spectrometer current |
| Ana SP/5 | 2 * 8 | Unsigned integer | Cooler voltage |
| Ana SP/6 | 2 * 8 | Unsigned integer | Spectrometer voltage |
| Ana FW/0 | 2 * 8 | Unsigned integer | FW motor primary current |
| Ana FW/1 | 2 * 8 | Unsigned integer | FW motor current |
| Ana FW/2 | 2 * 8 | Unsigned integer | FW motor converter current |
| Ana FW/3 | 2 * 8 | Unsigned integer | FW 15V current |
| Ana FW/4 | 2 * 8 | Unsigned integer | FW 15V voltage |
| Temp 0 | 2 * 8 | Unsigned integer | Spectrometer housing temperature |
| Temp 1 | 2 * 8 | Unsigned integer | Mirror motor elec. temperature |
| Temp 2 | 2 * 8 | Unsigned integer | Cryo cooler temperature |
| Temp 3 | 2 * 8 | Unsigned integer | Fold mirror temperature |
| Temp 4 | 2 * 8 | Unsigned integer | Housing rear temperature |
| Temp 5 | 2 * 8 | Unsigned integer | M2 temperature |
| Temp 6 | 2 * 8 | Unsigned integer | M1 temperature |
| Temp 7 | 2 * 8 | Unsigned integer | Diaphragm temperature |
| Temp 8 | 2 * 8 | Unsigned integer | Mirror motor temperature |
| Temp 9 | 2 * 8 | Unsigned integer | Star camera #2 temperature |
| Temp 10 | 2 * 8 | Unsigned integer | Star camera #1 temperature |
| Temp 11 | 2 * 8 | Unsigned integer | HOPS actuator #1 temperature |
| Temp 12 | 2 * 8 | Unsigned integer | Housing top temperature |
| Temp 13 | 2 * 8 | Unsigned integer | Radiator temperature |
| Temp 14 | 2 * 8 | Unsigned integer | Deck temperature |

Parameters are constants that describe different characteristics of the system.  In recognition of the fact that we may not know these “constants” exactly and may want to change them after launch, the parameters are grouped together in a parameter database.

Table 25.  DPU Parameter Subpacket Format

| Name | Length (bits) | Value | Description |
| --- | --- | --- | --- |
| Time Tag | 32 | Unsigned integer | Spacecraft MET |
| Grouping | 2 | 11 = None | Grouping flags |
| Subpacket Id | 14 | 0x0006 | Identifies subpacket type |
| Length | 16 | 48 | Number of data bytes in subpacket |
| Cal On | 16 | Unsigned integer | Time of cal. lamp on (seconds) |
| Cal Off | 16 | Unsigned integer | Time between cal. lamps on (s) |
| Cal Both | 16 | Unsigned integer | Time cal. lamps both off (s) |
| Cool Time | 16 | Unsigned integer | Cool time before spect. on (s) |
| HOP On | 16 | Unsigned integer | HOP on time (s) |
| FW Power | 16 | Unsigned integer | FW motor power level |
| FW Mult | 16 | Signed integer | FW motor steps per resolver counts |
| FW Div | 16 | Unsigned integer |  |
| FW Pos | 10 * 16 | Unsigned integer | FW positions (resolver counts) |
| Image Latch | 16 | Unsigned integer | Imager FPU latch recovery (seconds) |
| Spare | 5 * 16 |  |  |

# Appendix 2 - TPU Data Structures

There are a number of TPU parameter data structures.  There are parameters for the mirror control algorithm, the aim algorithm, and the closest approach logic.  There are many parameter structures for controlling the tracker.

Table 26.  Mirror Control Parameters

| Name | Length (bits) | Value | Description |
| --- | --- | --- | --- |
| Time Tag | 32 | Unsigned integer | Spacecraft MET |
| Grouping | 2 | 11 = None | Grouping flags |
| Subpacket Id | 14 | 0x0012 | Identifies subpacket type |
| Length | 16 | 92 | Number of data bytes in subpacket |
| Max Drive | 32 | Signed integer | Maximum DAC value |
| Tcr | 32 | Signed integer | Time of constant rate (ticks) |
| Tend | 32 | Signed integer | Time from end of exposure to end of frame (ticks) |
| Max Rate | 32 | Signed integer | Maximum output rate (counts/tick) |
| Error Rate | 32 | Signed integer | Maximum input rate (counts/tick) |
| Slew Rate | 32 | Signed integer | Slew rate (counts/tick) |
| Home Rate | 32 | Signed integer | Home rate (counts/tick) |
| Home Offset | 32 | Signed integer | Offset 0º to home (counts) |
| Kloop | 32 | Signed integer | Loop gain multiplier |
| Dloop | 32 | Signed integer | Loop gain divider |
| Kp | 32 | Signed integer | Proportional gain multiplier |
| Dp | 32 | Signed integer | Proportional gain divider |
| Ki | 32 | Signed integer | Integral gain multiplier |
| Di | 32 | Signed integer | Integral gain divider |
| Kd | 32 | Signed integer | Derivative gain multiplier |
| Dd | 32 | Signed integer | Derivative gain divider |
| Kl | 32 | Signed integer | Last drive gain multiplier |
| Dl | 32 | Signed integer | Last drive gain divider |
| Integ. Clamp | 32 | Signed integer | Limit of position error to integrate |
| Integ. Limit | 32 | Signed integer | Limit of integrated position error |
| Max Hall | 32 | Signed integer | Maximum Hall transitions (/second) |
| Min Angle | 32 | IEEE-754 single | Minimum mirror angle (degrees) |
| Max Angle | 32 | IEEE-754 single | Maximum mirror angle (degrees) |

Table 27.  Aim Parameters

| Name | Length (bits) | Value | Description |
| --- | --- | --- | --- |
| Time Tag | 32 | Unsigned integer | Spacecraft MET |
| Grouping | 2 | 11 = None | Grouping flags |
| Subpacket Id | 14 | 0x0013 | Identifies subpacket type |
| Length | 16 | 12 | Number of data bytes in subpacket |
| Contrast | 16 | Unsigned integer | Minimum image contrast |
| Spare | 16 |  |  |
| Pixels | 32 | Signed integer | Minimum number of pixels for comet blob |
| Spare | 32 |  |  |

Table 28.  Closest Approach Parameters

| Name | Length (bits) | Value | Description |
| --- | --- | --- | --- |
| Time Tag | 32 | Unsigned integer | Spacecraft MET |
| Grouping | 2 | 11 = None | Grouping flags |
| Subpacket Id | 14 | 0x0014 | Identifies subpacket type |
| Length | 16 | 80 | Number of data bytes in subpacket |
| Dist Thresh | 7 * 64 | IEEE-754 double | Miss distance thresholds (km) |
| Ang Thresh | 3 * 64 | IEEE-754 double | Target angle thresholds (degrees) |

Table 29.  Tracker Offset Parameters

| Name | Length (bits) | Value | Description |
| --- | --- | --- | --- |
| Time Tag | 32 | Unsigned integer | Spacecraft MET |
| Grouping | 2 | 11 = None | Grouping flags |
| Subpacket Id | 14 | 0x0015 | Identifies subpacket type |
| Length | 16 | 72 | Number of data bytes in subpacket |
| Offset Matrix | 9 * 64 | IEEE-754 double | 3x3 reference coordinate system transformation matrix |

Table 30.  Tracker Control Parameters

| Name | Length (bits) | Value | Description |
| --- | --- | --- | --- |
| Time Tag | 32 | Unsigned integer | Spacecraft MET |
| Grouping | 2 | 11 = None | Grouping flags |
| Subpacket Id | 14 | 0x0016 | Identifies subpacket type |
| Length | 16 | 72 | Number of data bytes in subpacket |
| Mirror Ang Thresh | 64 | IEEE-754 double | Actual/commanded mirror angle tolerance (degrees) |
| Mirror FF | 64 | IEEE-754 double | Time from last timing pulse to end of mirror command interval (seconds) |
| Filter Lag | 64 | IEEE-754 double | Time tracking filter “lags” behind current time (seconds) |
| Alpha R | 64 | IEEE-754 double | Roll correction gain |
| Alpha K | 64 | IEEE-754 double | Alpha-beta tracker gain |
| X Goal | 64 | IEEE-754 double | X goal position (pixels) |
| Y Goal | 64 | IEEE-754 double | Y goal position (pixels) |
| SFL | 64 | IEEE-754 double | System focal length (m) |
| G&C Rate | 16 | Unsigned integer | G&C message usage rate (s) |
| Spare | 48 |  |  |

Table 31.  Tracker Target Parameters

| Name | Length (bits) | Value | Description |
| --- | --- | --- | --- |
| Time Tag | 32 | Unsigned integer | Spacecraft MET |
| Grouping | 2 | 11 = None | Grouping flags |
| Subpacket Id | 14 | 0x0017 | Identifies subpacket type |
| Length | 16 | 24 | Number of data bytes in subpacket |
| Star Target | 3 * 64 | IEEE-754 double | Star target unit vector |

Table 32.  Tracker EKF Parameters

| Name | Length (bits) | Value | Description |
| --- | --- | --- | --- |
| Time Tag | 32 | Unsigned integer | Spacecraft MET |
| Grouping | 2 | 11 = None | Grouping flags |
| Subpacket Id | 14 | 0x0018 | Identifies subpacket type |
| Length | 16 | 104 | Number of data bytes in subpacket |
| Noise | 64 | IEEE-754 double | Filter measurement noise (one sigma) |
| Po | 6 * 64 | IEEE-754 double | Initial state covariance, HLC coords |
| Sys Q | 6 * 64 | IEEE-754 double | Kalman filter system noise, HLC coords |

Table 33.  Tracker Cheby Parameters

| Name | Length (bits) | Value | Description |
| --- | --- | --- | --- |
| Time Tag | 32 | Unsigned integer | Spacecraft MET |
| Grouping | 2 | 11 = None | Grouping flags |
| Subpacket Id | 14 | Cheby #1 = 0x0019 Cheby #2 = 0x001a Cheby #3 = 0x001b | Identifies subpacket type |
| Length | 16 | 384 | Number of data bytes in subpacket |
| Spans | 32 | Signed integer | Number of spans |
| Coord Id | 32 | Signed integer | Coord Id |
| Start | 64 | IEEE-754 double | Start time (seconds) |
| Stop | 64 | IEEE-754 double | Stop time (seconds) |
| X Coeff | 15 * 64 | IEEE-754 double | X Coefficients (km) |
| Y Coeff | 15 * 64 | IEEE-754 double | Y Coefficients (km) |
| Z Coeff | 15 * 64 | IEEE-754 double | Z Coefficients (km) |

Table 34.  Tracker Mirror Parameters

| Name | Length (bits) | Value | Description |
| --- | --- | --- | --- |
| Time Tag | 32 | Unsigned integer | Spacecraft MET |
| Grouping | 2 | 11 = None | Grouping flags |
| Subpacket Id | 14 | 0x001c | Identifies subpacket type |
| Length | 16 | 640 | Number of data bytes in subpacket |
| Coeff AA X | 10 * 64 | IEEE-754 double | Mirror coefficients, aft, side A, X |
| Coeff AA Y | 10 * 64 | IEEE-754 double | Mirror coefficients, aft, side A, Y |
| Coeff AB X | 10 * 64 | IEEE-754 double | Mirror coefficients, aft, side B, X |
| Coeff AB Y | 10 * 64 | IEEE-754 double | Mirror coefficients, aft, side B, Y |
| Coeff FA X | 10 * 64 | IEEE-754 double | Mirror coefficients, fore, side A, X |
| Coeff FA Y | 10 * 64 | IEEE-754 double | Mirror coefficients, fore, side A, Y |
| Coeff FB X | 10 * 64 | IEEE-754 double | Mirror coefficients, fore, side B, X |
| Coeff FB Y | 10 * 64 | IEEE-754 double | Mirror coefficients, fore, side B, Y |

Table 35.  Tracker Gate Parameters

| Name | Length (bits) | Value | Description |
| --- | --- | --- | --- |
| Time Tag | 32 | Unsigned integer | Spacecraft MET |
| Grouping | 2 | 11 = None | Grouping flags |
| Subpacket Id | 14 | 0x001d | Identifies subpacket type |
| Length | 16 | 24 | Number of data bytes in subpacket |
| Size | 64 | IEEE-754 double | Gate diameter |
| Alpha | 64 | IEEE-754 double | Gate smoothing gain |
| Count | 32 | Signed integer | Running hit counter |
| Spare | 32 |  |  |

Table 36.  Tracker Alignment Parameters

| Name | Length (bits) | Value | Description |
| --- | --- | --- | --- |
| Time Tag | 32 | Unsigned integer | Spacecraft MET |
| Grouping | 2 | 11 = None | Grouping flags |
| Subpacket Id | 14 | 0x001e | Identifies subpacket type |
| Length | 16 | 32 | Number of data bytes in subpacket |
| Align | 4 * 64 | IEEE-754 double | IRU alignment quaterion |

# Appendix 3 - Alarm & Result Codes

Table 37.  Alarms

| ID | Description | Information |
| --- | --- | --- |
| 0 | Unused |  |
| 1 | Bad command checksum |  |
| 2 | Out of macro contexts | Macro Id |
| 128-191 | Monitored value is too low | Value and limit |
| 192-255 | Monitored value is too high | Value and limit |

Table 38.  Results

| Result Code (hex) | Description |
| --- | --- |
| 0x00 | No error, command executed |
| 0x01 | No error, command appended to macro |
| 0x02 | Unknown opcode |
| 0x03 | Bad argument |
| 0x04 | Cannot run macro; no contexts |
| 0x05 | Cannot be used outside of a macro |
| 0x06 | Macro compilation error |
| 0x07 | Macro not killed (not running?) |
| 0x08 | Bad EEPROM program |
| 0x09 | Cannot restore macros; bad checksum |
| 0x0a … 0x0f | reserved for common software |
| 0x10 | Cannot move cover, actuator disabled |

# Appendix 4 - Acronyms

Table 39.  Acronyms

| Acronym | Definition |
| --- | --- |
| BC | Bus Controller |
| CA | Closest Approach |
| CCD | Charge-Coupled Device |
| CCSDS | Consultative Committee for Space Data Systems |
| C&DH | Command & Data Handling |
| CFI | CONTOUR Forward Imager |
| CONTOUR | COmet Nucleus TOUR |
| CRISP | CONTOUR Remote Imager/Spectrometer |
| DPU | Data Processing Unit |
| EEPROM | Electrically Erasable Programmable ROM |
| FPU | Focal Plane Unit |
| FW | Filter Wheel |
| G&C | Guidance and Control |
| HOP | High Output Paraffin |
| I2C | Inter-Integrated Circuit |
| IR | Infra-Red |
| LED | Light-Emitting Diode |
| MET | Mission Elapsed Time |
| MIMU | Miniature Inertial Measurement Unit |
| RAM | Random Access Memory |
| ROM | Read Only Memory |
| RT | Remote Terminal |
| S/C | Spacecraft |
| TBD | To Be Determined |
| TDT | Terrestrial Dynamical Time |
| TPU | Tracking Processor Unit |
| XOR | eXclusive OR |