***** File DUCMA.DOC                                                          
                                                                              
VEGA DATA DOCUMENTATION                                                       
                                                                              
A description of the experiment is in the following references:               
                                                                              
Simpson, J. A., Rabinowitz, D. and Tuzzolino, A. J. 1989, "I. PVDF            
detector signal dependence on mass and velocity for penetrating               
particles", Nucl. Instr. Meth., A279, 611-624.                                
                                                                              
Simpson, J. A. and Tuzzolino, A. J. 1989, "II. Instruments for                
measurement of particle trajectory, velocity, and mass", Nucl.                
Instr. Meth., A279, 625-639.                                                  
                                                                              
                                                                              
The Vega data consists of 4 files, two files each for Vega-1 and Vega-2.      
                                                                              
1) Vega 1 dsfast17 file:                                                      
                                                                              
The dsfast17 file includes all the fast telemetry data (data obtained         
every two seconds).  The fast telemetry data covers the entire                
Halley's comet encounter, lasting approximately four hours.                   
The telemetry noise events have not been removed                              
from the data. Each readout includes; 1)the time at which data                
were obtained in seconds (given in time since the Vega launch                 
date), and the Blissi clock described in the technical manual,                
2) Two eight integer status commands also described in                        
the Ducma Technical Manual, 3) two temperatures, the detector                 
temperature and the electronic temperature explained                          
in the technical manual, 4) the dust events given as ten                      
integers which represent counts in each of four different                     
thresholds, M4-M1, as well as the anticoincident counts, M4NV-M1NV,           
and the two V detector counts, VL and VH, which register                      
noise events. More detailed explanations may be found in the                  
Ducma technical manual on file at the Small Bodies Node of PDS.               
A sample data line appears as follows:                                        
                                                                              
                                                                              
Ducma     Blissi     Command     Status      Detector    Elect.               
clock     clock                               Temp.      Temp.                
38252812     1      10100100    11011001     -18.01      30.86                
                                                                              
                                                                              
M4    M3      M2    M1    M4NV   M3NV   M2NV   M1NV    VL     VH              
0     0       1     2       0      0      0      0      0      0              
                                                                              
2) Vega 1 Dvega101 file:                                                      
                                                                              
Dvega101 file includes the encounter data without any information             
about status commands and temperature variations.                             
                                                                              
The noise spikes have been removed. This file is designed for easy data       
analysis and lists simply the time of an event in seconds and the total       
counts in each threshold, M4-M1, the anticoincident events, M4NV-M1NV,        
and the noise events, VL and VH, all obtained during that time interval.      
The masses associated with each threshold follow: M1: 1.5 x 10**-13 g,        
M2: 5.6 x 10**-11 g, M3: 1.6 x 10**-9 g, and M4: 4.0 x 10**-8 g.              
                                                                              
                                                                              
3) Vega 2 dsfast27 file:                                                      
                                                                              
This file is the entire fast telemetry data for Vega-2 .  Its format is       
similar to sfast17, except Vega-2 obtained data every second instead of       
every two seconds.                                                            
                                                                              
4) Vega 2 Dvg2cln1 file:                                                      
                                                                              
This file is the encounter data for Vega-2. Its format is similar to          
Dvega101. Note the accidental calibration and noise spikes have been          
removed.  Again Vega-2 obtained data every second.                            
                                                                              
Below are two charts to help in the conversion of BLISSI clock times for      
Vega1 and Vega2 to DUCMA clock times and 'calendar time'.                     
                                                                              
DUCMA times are given in seconds after launch                                 
BLISSI times are given in seconds                                             
                                                                              
Vega1                                                                         
DUCMA start time: Dec. 15 1984 10:33:37                                       
from file dsfast17.tab                                                        
------------+-----------+--------------------------+--------------------+     
 DUCMA time |BLISSI time|    DUCMA Time to CA 	   |      Real time	|          
  (seconds) | (seconds)	| (seconds) |(DD hh:mm:ss) | (YY-MM-DDThh:mm:ss)|     
------------+-----------+-----------+--------------+--------------------+     
  37910088  |    179	|   612424  | 07 02:07:04  |  86-02-27T05:13:02	|        
  37917104  |   7195	|   605408  | 07 00:10:08  |  86-02-27T07:09:58	|        
  38344948  |      8	|   177564  | 02 01:19:24  |  86-03-04T06:00:42	|        
  38352136  |   7196	|   170376  | 01 23:19:36  |  86-03-04T08:00:30	|        
  38431348  |     13	|    91164  | 01 01:19:24  |  86-03-05T06:00:42	|        
  38438524  |   7191	|    83988  | 00 23:19:48  |  86-03-05T08:00:18	|        
  38511536  |      2	|    10976  | 00 03:02:56  |  86-03-06T04:17:10	|        
* 38522512  |  10976 	|        0  | 00 00:00:00  |  86-03-06T07:20:06 |       
  38526412  |  14878	|     3900  | 00 01:05:00  |  86-03-06T08:25:06	|        
  38612184  |    202	|    89672  | 01 00:54:32  |  86-03-07T08:14:38	|        
  38619168  |   7188	|    96656  | 01 02:50:56  |  86-03-07T10:11:02	|        
------------+-----------+-----------+--------------+--------------------+     
                                                                              
Vega2                                                                         
DUCMA start time: Dec. 21 1984 10:29:46                                       
from file dsfast27.tab                                                        
------------+-----------+--------------------------+--------------------+     
 DUCMA time |BLISSI time|    DUCMA Time to CA 	   |      Real time	|          
  (seconds) | (seconds)	| (seconds) |(DD hh:mm:ss) | (YY-MM-DDThh:mm:ss)|     
------------+-----------+-----------+--------------+--------------------+     
  37478720  |   49156   |   785332  | 09 02:08:52  |  86-02-28T05:11:08	|     
@ 37483380  |   53818 	|   780672  | 09 00:51:12  |  86-02-28T06:28:48	|      
@ 37483380  |   37435 	|   780672  | 09 00:51:12  |  86-02-28T06:28:48	|      
  37483384  |   37436   |   780668  | 09 00:51:08  |  86-02-28T06:28:52	|     
  37486588  |   38595	|   777464  | 08 23:57:44  |  86-02-28T07:22:16	|       
  38079280  |       1	|   184772  | 02 03:19:32  |  86-03-07T04:00:28	|       
  38086472  |    7191	|   177580  | 02 01:19:40  |  86-03-07T06:00:20	|       
  38173960  |       5	|    90092  | 01 01:01:32  |  86-03-08T06:18:28	|       
  38181148  |    7194	|    82904  | 00 23:01:44  |  86-03-08T08:18:16	|       
  38252812  |       1	|    11240  | 00 03:07:20  |  86-03-09T04:12:40	|       
* 38264052  |   11242   |        0  | 00 00:00:00  |  86-03-09T07:20:00 |     
  38268860  |   16049	|     4808  | 00 01:20:08  |  86-03-09T08:40:08	|       
------------+-----------+-----------+--------------+--------------------+     
                                                                              
*-times of Closest Approach (CA)                                              
                                                                              
@-BLISSI clock apparently reset from 53818 to 37435 during 4 second           
	DUCMA time period beginning at 37483380 seconds, resulting                   
	in two very different BLISSI clock values 'mapping' to the                   
        same DUCMA time and Real time.